## Slide 1: Overall description of the Ion Source & LEBT
Øystein Midttun
System Leader – Ion source and LEBT
SRR 1 – Ion Source & LEBT
2018-07-17--18

## Slide 2: ESS layout (July 2018)
You are here
Ion source and LEBT
Target
Local control room

## Slide 3: Overview of accelerator tunnel
Ion source and LEBT
Electrical power (racks)
Cooling water skid
Local control room

## Slide 4: Table of content
System Requirements (high level)
Specific safety systems (engineered control)
Operating & safety procedures (administrative control)
Test & Verification
  Allowed testing Envelope
Open issues
System Requirements
Specific safety systems
Operating & safety procedures (administrative control)
Test & Verification
  Allowed testing Envelope
Open issues

## Slide 5: System Requirements – Beam parameters at RFQ entrance
Particle Protons (H+)
Current 70 mA
Energy 75 kV
Pulse length 2.86 ms
Repetition rate 14 Hz
Duty cycle 4%
Emittance (99%) 2.25 mm mrad
Emittance (rms) 0.25 mm mrad
Stability
  Flat top ±2%
  Pulse to pulse ±3.5%

## Slide 6: Sub-system overview
Ion source
Solenoid 1
Solenoid 2
Iris
Chopper
Collimator
Commissioning tank
EMU 1
EMU 2
Faraday cup
Pumping box
Permanent tank
ACCT
NPM 1
NPM 2
ACCT: AC current transformer
EMU: Emittance measurement unit
NPM: Non-invasive profile monitor
Doppler shift
Electron
repeller
Electron
repeller
Gate valve
Gate valve

## Slide 7: Sub-systems – Ion source
Plasma chamber
Extraction system
Pumping box
Repeller
HV power supply
Isolation transformer
Magnetron
H2 bottle
3 x solenoid
Waveguide
High voltage (HV) platform
Ion source
Front End and Magnets
Voltage divider

## Slide 8: Sub-systems – LEBT
Plasma chamber
Extraction system
Pumping box
Solenoid
2 x steerer
Iris
Diagnostics tank
Solenoid
2 x steerer
Chopper
Repeller
Repeller
Commissioning tank (RFQ)
HV power supply
Isolation transformer
Collimator
Magnetron
H2 bottle
3 x solenoid
Waveguide
High voltage (HV) platform
Ion source
Low energy beam transport (LEBT)
Front End and Magnets
Voltage divider
Beam stop
N2 bottle

## Slide 9: Sub-systems – Beam Diagnostics
Plasma chamber
Extraction system
Pumping box
Solenoid
2 x steerer
Iris
Diagnostics tank
Solenoid
2 x steerer
Chopper
EMU H+V
Faraday cup
NPM H+V
Doppler shift
Repeller
Repeller
ACCT
Commissioning tank (RFQ)
HV power supply
Isolation transformer
Collimator
Magnetron
H2 bottle
3 x solenoid
Waveguide
High voltage (HV) platform
Ion source
Low energy beam transport (LEBT)
Front End and Magnets
Beam Diagnostics
ACCT
Voltage divider
EMU H+V
Faraday cup
NPM H+V
Doppler shift
Beam stop
Alternative location of beam instruments for commissioning
ACCT: AC current transformer
EMU: Emittance measurement unit
NPM: Non-invasive profile monitor
TMP: Turbomolecular pump
N2 bottle

## Slide 10: Sub-systems – Vacuum
Plasma chamber
Extraction system
Pumping box
Solenoid
2 x steerer
Gate valve
Iris
Diagnostics tank
Gate valve
Solenoid
2 x steerer
Chopper
EMU H+V
Faraday cup
NPM H+V
Doppler shift
2 x TMP
Repeller
Repeller
ACCT
2 x TMP
Commissioning tank (RFQ)
2 x TMP
HV power supply
Isolation transformer
Collimator
Magnetron
H2 bottle
3 x solenoid
Waveguide
Primary pump
Primary pump
High voltage (HV) platform
Ion source
Low energy beam transport (LEBT)
Front End and Magnets
Vacuum
Beam Diagnostics
ACCT
Voltage divider
EMU H+V
Faraday cup
NPM H+V
Doppler shift
Beam stop
Alternative location of beam instruments for commissioning
N2 bottle
ACCT: AC current transformer
EMU: Emittance measurement unit
NPM: Non-invasive profile monitor
TMP: Turbomolecular pump

## Slide 11: Sub-systems – Cooling water
Plasma chamber
Extraction system
Pumping box
Solenoid
2 x steerer
Gate valve
Iris
Diagnostics tank
Gate valve
Solenoid
2 x steerer
Chopper
EMU H+V
Faraday cup
NPM H+V
Doppler shift
2 x TMP
Repeller
Repeller
ACCT
2 x TMP
Commissioning tank (RFQ)
2 x TMP
HV power supply
Isolation transformer
Collimator
Magnetron
H2 bottle
Ion source
LEBT 1
LEBT 2
3 x solenoid
Waveguide
Primary pump
Primary pump
High voltage (HV) platform
Ion source
Low energy beam transport (LEBT)
Front End and Magnets
Cooling water
Vacuum
Beam Diagnostics
ACCT
Voltage divider
EMU H+V
Faraday cup
NPM H+V
Doppler shift
Beam stop
Alternative location of beam instruments for commissioning
N2 bottle
ACCT: AC current transformer
EMU: Emittance measurement unit
NPM: Non-invasive profile monitor
TMP: Turbomolecular pump

## Slide 12: Sub-systems – Safety
Plasma chamber
Extraction system
Pumping box
Solenoid
2 x steerer
Gate valve
Iris
Diagnostics tank
Gate valve
Solenoid
2 x steerer
Chopper
EMU H+V
Faraday cup
NPM H+V
Doppler shift
2 x TMP
Repeller
Repeller
ACCT
2 x TMP
Commissioning tank (RFQ)
2 x TMP
HV power supply
Isolation transformer
Collimator
Magnetron
H2 bottle
Ion source
LEBT 1
LEBT 2
3 x solenoid
Waveguide
Primary pump
Primary pump
High voltage (HV) platform
Ion source
Low energy beam transport (LEBT)
PSS0 controlled area
and radiation shielding
Front End and Magnets
Cooling water
Vacuum
PSS
Beam Diagnostics
ACCT
Voltage divider
EMU H+V
Faraday cup
NPM H+V
Doppler shift
Beam stop
Alternative location of beam instruments for commissioning
N2 bottle
ACCT: AC current transformer
EMU: Emittance measurement unit
NPM: Non-invasive profile monitor
TMP: Turbomolecular pump

## Slide 13: Sub-systems – Control system
Plasma chamber
Extraction system
Pumping box
Solenoid
2 x steerer
Gate valve
Iris
Diagnostics tank
Gate valve
Solenoid
2 x steerer
Chopper
EMU H+V
Faraday cup
NPM H+V
Doppler shift
2 x TMP
Repeller
Repeller
ACCT
2 x TMP
Commissioning tank (RFQ)
2 x TMP
HV power supply
Isolation transformer
Collimator
Magnetron
H2 bottle
Ion source
LEBT 1
LEBT 2
3 x solenoid
Waveguide
Primary pump
Primary pump
High voltage (HV) platform
Ion source
Low energy beam transport (LEBT)
PSS0 controlled area
and radiation shielding
Front End and Magnets
Cooling water
Vacuum
PSS
Beam Diagnostics
Control system
ACCT
Voltage divider
EMU H+V
Faraday cup
NPM H+V
Doppler shift
HV controls
Ground potential controls
Beam stop
Alternative location of beam instruments for commissioning
N2 bottle
ACCT: AC current transformer
EMU: Emittance measurement unit
NPM: Non-invasive profile monitor
TMP: Turbomolecular pump

## Slide 14: Specific safety systems – Electrical
– For energization of electrical equipment (e.g. racks, power supplies) we have the Electrical Safety Plan that needs to be presented to the Electrical Safety Leader
– Lock-out tag-out is performed by the Electrical Safety Leader
ESS-0242842 – ESS RULES FOR ELECTRICAL LOCK-OUT/TAG-OUT

## Slide 15: Specific safety systems – Personal safety
– Ion source safety fence with PSS access control mitigates the high voltage hazard

## Slide 16: Specific safety systems – Radiation safety
– The ion source produces x-rays with energies up to 75 keV
– These x-ray originates from electrons that accelerated back to the plasma chamber
– The ion source safety fence includes 2 mm thick lead plates to reduce the radiation below natural background

## Slide 17: Specific safety systems – Machine protection
– For commissioning we have local protection (interlocks) for all devices

## Slide 18: Test & Verification – TRR
From the test readiness review (TRR) we gathered the different stakeholder to define:
  Which test to be done
  The prerequisites for the tests
  Coordination of the tests
  Safety issues

## Slide 19: Test & Verification – TRR
TRR documentation
  Meeting minutes in Confluence –https://confluence.esss.lu.se/display/LG/Test+and+Readiness+Review
  Test and verification plan – ESS-0317305 - Ion source and LEBT verification plan
  Test and verification report – collection of results from the test and verification plan

## Slide 20: Test & Verification – TRR
– Tracking of progress in Jira
– Test are stored as Jira issues, where we can document progress and report

## Slide 21: Test & Verification – allowed testing envelope
Any beam mode of the ESS accelerator is ok for the ion source and LEBT commissioning
To protect the machine, the following envelope must be respected (controlled by software)
  High voltage 70-80 kV
  Microwave power < 2 kW
  Pulse length < 6 ms
  Duty cycle < 8%
  Pulse length for emittance measurement in the commissioning tank 200 µs (tbc by Beam Diagnostics)

## Slide 22: Ion source and LEBT