## Slide 1: LEBT solenoids and correctors
Øystein Midttun
System Leader – Ion source and LEBT
SRR 1 – Ion Source & LEBT
2018-07-17--18

## Slide 2: System – LEBT
Plasma chamber
Extraction system
Pumping box
Solenoid
2 x steerer
Gate valve
Iris
Diagnostics tank
Gate valve
Solenoid
2 x steerer
Chopper
EMU H+V
Faraday cup
NPM H+V
Doppler shift
2 x TMP
Repeller
Repeller
ACCT
2 x TMP
Commissioning tank (RFQ)
2 x TMP
HV power supply
Isolation transformer
Collimator
Magnetron
H2 bottle
Ion source
LEBT 1
LEBT 2
3 x solenoid
Waveguide
Primary pump
Primary pump
High voltage (HV) platform
Ion source
Low energy beam transport (LEBT)
PSS0 controlled area
and radiation shielding
Front End and Magnets
Cooling water
Vacuum
PSS
Beam Diagnostics
Control system
ACCT
Voltage divider
EMU H+V
Faraday cup
NPM H+V
Doppler shift
HV controls
Ground potential controls
Beam stop
Alternative location of beam instruments for commissioning
N2 bottle
ACCT: AC current transformer
EMU: Emittance measurement unit
NPM: Non-invasive profile monitor
TMP: Turbomolecular pump

## Slide 3: Table of content
System Requirements
Protection systems
Test & Verification
Open issues

## Slide 4: System Requirements
Particle Protons (H+)
Proton current 0-74 mA
Transmission > 95%
Energy 75 kV
Pulse length 2.86 ms
Repetition rate 14 Hz
Duty cycle 4%
Emittance (99%) 2.25 mm mrad
Emittance (rms) 0.25 mm mrad
Chopper efficiency 99%

## Slide 5: Two-solenoid LEBT
Proton source
– creates the beam
Iris
– controls the current
Chopper and collimator
– controls the pulse length
Solenoid
– focuses the beam
2.5 m

## Slide 6: Two-solenoid LEBT
6
H+
H2+
2.5 m
H3+

## Slide 7: Protection systems – Temperature sensors and flow meters on cooling water manifold
– Temperature sensors on iris and collimator
– Temperature switches on solenoids
– Controlled by the interlock system

## Slide 8: Test & Verification – ESS-0317305 - Ion source and LEBT verification plan
System testing
  Solenoid x 2
  Steerers x 2 (horizontal and vertical)
  Repeller electrode
  Iris
Protection systems testing
  Manual testing of interlocks, i.e. flow meters, temperature and pressure sensors
Remaining installation
  Chopper electronics
  A team from INFN-LNS will come to ESS for installation and commissioning
  This activity will be coordinated to be performed at the same time as the installation of the 2nd EMU head

## Slide 9: Outstanding issues
# | System/Comp. | Status | Description | Due date | Remark
1 | LEBT test and verification | Not started | All tests in the verification plan | end-August | Procedure defined in ESS-0317305 - Ion source and LEBT verification plan
2 | Chopper electronics | Not installed | A team from INFN-LNS will come to ESS for installation and commissioning | October, tbc with in-kind partner | Missing the chopper is not critical for any beam line components
3 | Chopper hardware | Being designed | Chopper needs hardware change to improve the efficiency | December | Not critical for beam commissioning. Delivery by in-kind partner.