## Slide 1: Cables, Racks, and the rest
Johan Norin
www.europeanspallationsource.se
20 November 2018

## Slide 2: Cables
 | Nov 2017 | Nov 2018
Cables in cdb | 1687 | 2636
Tunnel patch cables | 0 | 731
Cables without connector information | 994 | 31 (BCM fiber and IPM)
The number of cables have increased.
Cable information is more complete.
Some target instrumentation is still missing from the cable database.

## Slide 3: Cable endpoints
Endpoint resolution is increased. This is ongoing.
2017
Cable endpoints are racks and diagnostic systems.
Exemple: rack 14 in row 5 to DTL Faraday cup
2018
Cable endpoints are physical patch panels and electronics.
Exemple: row 14, rack 5, panel 3 to DTL Faraday Cup actuator
LBS information is added.

## Slide 4: Cable database validation
µTCA/IPC
NPMD
(BLE)
ECAT
SHV-5 Hueber Suhner
NPMA
(Actuator)
Motor - 4P19IOSHFRH
Encoder - 4P19IOSHFRH
Limit switch - 4P19IOSHF
Souriau UT06128SH female
Souriau UT06128PH male
Souriau UT0W61210SH female
Souriau UT0W6106SH female
Souriau UT0W61210PH male
Souriau UT0W6106PH male
SHV-5 Hueber Suhner
NPMFE
(FE electronics)
RJ45 male
Hirose HR10A-10P-12S
RJ45 male
Souriau UT06128PH male
Camera data - Cat.6 S/FTP LSHF
Cam PS and trigger- 4P24IOSHF
HV
SHV-5 Hueber Suhner
SHV-5 Hueber Suhner
SHV-5 Hueber Suhner
SHV-5 Hueber Suhner
img int HV cathode - 1C20RG-58HV
img int HV anode - 1C20RG-58HV
img int HV gain - 1C20RG-58HV
RJ45 male
RJ45 male
NPM communication - Cat.6 S/FTP LSHF
(3 cables in MEBT as the ECAT and uTCA are in separate racks.)
?
?
Fiber bundle tbd
Tunnel
FEB/G02/GSA
Are all cables correct?
Exemple: NPM BIF 2018-10-26

## Slide 5: Rack locations (No changes)
Location | Number of beam diagnostics racks
Front end building (FEB) | 10
Klystron gallery | 27 (4 free)
Test stand area | 6
Gallery support area (GSA) | 4
Target access area (TAA) | 5 (2 free)
Sum | 52 (6 free)

## Slide 6: Rack electronic allocation
Boxes represents allocated space for equipment.
Worst size scenario assumed during planning.
Many small changes since 2017.
Device | # | Location
BCM | 1 | MBL-010
BPM | 4 | MBL-010 – MBL-020
ICBLM | 20 | SPK-100 – MBL-060
LBM | 1 | MBL-010

## Slide 7: The rest
Naming tool:
All cable endpoints must be named in the ESS naming service.
  Section-subsection:Discipline-Device-ID
  SPK-040LWU:PBI-BPM-001
Cables:
All ”long” cables are named in the cable database.
System-Subsystem-Class-ID
22B010784
Internal rack cables:
Separate system from cdb.
Control group - Function
WS01-signal1

## Slide 8: The rest
Naming tool
CDB names
WS01-signal1
FBS (Facility Breakdown Structure)
FBS defines positions (slots) for everything.
ESS.ACC.B01.B02.B11.B05.B01
ESS
Accelerator
PBI
Beam loss monitors
Group ICBLM-11
System:HBL-200Crm:PBI-BLM-001
Sensor: HBL-200Crm:PBI-ICBLM-001

## Slide 9: The rest
The FBS is one of several ESS-wide databases:
FBS – Positions (systems and equipment slots based on function)
LBS – Locations (rooms, buildings, beam sections)
EAM – Hardware (what goes into the positions)

## Slide 10: The rest
Present count of equipment:
Diagnostic systems: 529
Beamline elements: 959
MTCA crates: 78
Electronics: 1143

## Slide 11: The rest
Thank you!