## Slide 1
Aperture and Grid electronics
Anders J Johansson, Lund university 22 November 2018

## Slide 2: Aperture monitor
16 blades and 24 temperature sensors
Will be measuring the temperaure and the current.
Will trigger the MPS if limits are exceeded.
Will be placed at four places:
  Tuning dump
  A2T (movable blades)
  Proton beam window
  Proton beam instrument plug

## Slide 3: Grid
Horizontal and vertical current sensing wires
Additional bias planes
Wires in SiC
Current thresholds in each separete wire triggers MPS
  1 MS/s and 300 kHz analog bandwidth
  Additional MPS triggers to be studied
Higher level algorithm to calculate estimated power profile on target.

## Slide 4: Conceptual design
Beckhoff based for slow signals (i.e. temperatures, motion control)
MTCA.4 based implementation for high speed signals (i.e. currents)
Current measurement by off the shelf hardware
  CAENels FMC module FMC-Pico-1M4 4-channel 20-bit 1 MSPS FMC Floating Ammeter
Fast signal processing by FPGA
  IOxOS IFC_1410 FMC carrier with FPGA and CPU

## Slide 5
12-slot
MTCA
1410
Pico
Pico
1410
Pico
Pico
MCH
Timing
Reciever
MPS interface
12-slot
MTCA
1410
1410
Pico
Pico
Pico
Pico
Total number of channels in two crates
depends on solution for MPS and crate-to-crate communication.
MCH
Timing
Reciever
*

## Slide 6: Necessary number of channels
Aspect ratio of rastered beam is approx 1:2.7
Assumption: 80 channels, one dimension per crate
  80 channels for horizontal.
  30 channels for vertical
Gives 1 wire per 2,3 mm (approx)
  Based on a total size of 181 x 67 mm.

## Slide 7: Number of channels in one crate
Conservative estimate
TR (1 slot)
CPU (1 slot)
MPS-interface (1 slot)
Pico 1M4 (21 FMC / 9 slots)
  72 channels
Optimistic estimate
TR (1 slot)
MPS-interface (1 FMC / ½-slot)
Pico 1M4 (23 FMC / 10.5 slots)
  84 channels

## Slide 8
12-slot
MTCA
1410
Pico
Pico
1410
Pico
Pico
MCH
Timing
Reciever
CPU
12-slot
MTCA
1410
1410
Pico
Pico
Pico
Pico
MCH
Timing
Reciever
1410
MPS interface
CPU
1410
MPS interface
Pico
7
2
76 channels horizontal
32 channels vertical
Solution without crate-to-crate communication

## Slide 9: Additional functions
Self-test functionality
  Identify broken wires
Bias-voltage supply to bias-planes

## Slide 10: Open questions
Analog signal processing/filtering stage
Individiual wire bias
Shielding strategy
MPS threshold processing
Post-processing /data visualisation
…
-Will depend on evaluation of test results:

## Slide 11: Grid protoype
Tested in J-parc November 2018.