## Slide 1
Slow Control Performance
UART USB 230,400 baud 10b
~ 23 KB / sec
cmd/resp packet 16 Bytes (4 [8] Bytes payload)
~ 0.7 msec per packet
Write(Read) Transaction 4 packets
~ 3 msec per word (4 bytes)
E.g. Loading controls for LOKI ~ 7K words => 20 secs worst case
If assume using Block Transfers ~ x 4 faster
If use full packet payload x 2 faster
OK (if LOKI is typical)
Assumptions:
Operates one transaction at a time. Command handler in fpga firmware,
s/w overhead is small.
Not considered Calibration Runs special requirements?

## Slide 2
Block Write init
Block Write Init resp
Block Write Data
Block Write Data
Block Write Term
Block Write Term resp
Wr Err
Wr Err