Description:	This document describes the design and current state of FPGA firmware for the neutron sensitive Beam Loss Monitoring system (nBLM) of the ESS accelerator
Title:	Firmware Design Report for nBLM

Authors:	Grzegorz Jabłoński
Co Authors:	Wojciech Jałmużna, Rafał Kiełbik, Wojciech Cichalewski, Andrzej Napieralski
Version:	1.0
Date:	2019.02.05

Revision Table

Revision	Date	Modification
1.0	2019.02.05	Final version provided for review
1.1
1.2
1.3
1.4
1.5
1.6
1.7
1.8
1.9
2.0

Table of Contents

# Introduction
The primary goal of the Beam Loss Monitoring (BLM) system is to monitor beam losses of the ESS accelerator and detect abnormal beam behaviour and promptly inhibit beam production in case of beam failures to keep the machine safe from beam-induced damage. The nBLM subsystem is a part of this system, based on Micromegas detectors designed to be sensitive to fast neutrons and insensitive to low energy photons (X– and gamma–rays). Its specification can be found in [1].
The works summarised therein has been performed in the frame of Polish in-kind contribution to ESS [2].
The Workunit 2 (icBLM and nBLM controls and realization) comprises:
- Development of FPGA firmware that runs on the icBLM and nBLM back-end electronics (BEE) and has the following tasks:
  - Process the incoming data (from ADC or other front-end electronics)
  - Provide the data to the (EPICS) control system for monitoring purposes
  - Run algorithms for machine protection purposes that assess the beam conditions and in case of unacceptable beam losses inform the Beam Interlock System by dropping the BEAM_PERMIT signal and also providing data that is needed to analyse the conditions that led to dropping the beam permit
  - Perform checks to verify that the system components and functions are working properly.
- Development and implementation the following software:
  - icBLM specific algorithms for data processing that run on the icBLM BEE CPU,
  - The low-level drivers to interface to the (EPICS) control system,
  - Implementation of EPICS databases to store and process the data,
  - Development of graphical user interfaces to visualize the icBLM specific data.

Software development for the nBLM system is covered by a separate contract and is not in the scope of this contract. Nevertheless, the software demonstrating the functionality of the nBLM software and allowing its performance evaluation has been also provided.

# Current implementation status
The description below refers to the revision tagged v0.5 made available to CEA for the purpose of software development (January 8th, 2019). The implemented features correspond to the specification revision uploaded to Jira on August 9th, 2018.
## Hardware and software platform
The hardware platform consists of the IFC_1410 FMC carrier AMC, equipped with Xilinx Kintex UltraScale KU040 FPGA and ADC_3111 FMC board (8 channels 250 Msps 16-bit ADC). The firmware has been implemented within the TOSCA framework, provided by the board manufacturer, IOxOS. There are two option for the controlling CPU – the POWER processor on the AMC module or the Concurrent AM90x/41x in the MTCA crate.
## Currently implemented blocks
All the blocks fully described in the specification have been implemented.
The implemented blocks include:
- Data acquisition from ADC (8 channels)
- Raw data selection
- Preprocessing
- Neutron detection algorithm (6 channels)
- Pulse processing block
- Buffering of data-on-demand
## Blocks not implemented

The blocks that are not implemented include:
- Protection function block
- FBIS interface block
- Smart trigger block
- Low Latency Link block
- Backplane triggering
## FPGA resource utilization

Resource type	Utilization percentage
CLB LUTs	54.71
LUT as Logic	53.15
LUT as Memory	3.36
CLB Registers	31.82
Register as Flip Flop	31.82
Register as Latch	0.00
CARRY8	14.01
F7 Muxes	1.33
F8 Muxes	0.17
F9 Muxes	0.00

Currently the project meets timing, however routing congestion warnings appear and custom synthesis options are required. 85% of CLBs are used. Implementing missing features may cause the Vivado design system to pack unrelated logic to single tiles and cause routing and timing closure problems.

# Past problem and issues

## DDR Calibration
The TOSCA framwork has had a bug, causing segmentation violation errors on the host CPU during the on-board DDR memory calibration procedure most of the time. Several reboots of the IFC_1410 modules were needed to make the board operate properly. The problems became more severe after migration of the Vivado version from 2016.4 to 2018.2. The problem has been finally identified by IOxOS and fixed in December 2018.
## Timing closure problems
The examples provided by IOxOS do not synthesize without timing errors “out of a box”. Most implementation runs of our project resulted in pulse width timing violations related to the 250 MHz clock driving the DDR memory controller. Finally we have been able to fix the problem by constraining the global buffer output driving this clock to a specific location. With this constraint, the memory clock can be increased to 275 MHz.
## DMA performance problems
Initially we were instructed to use the Tosca kernel driver for the communication between CPU and FPGA. This driver provided very low DMA throughput of order of 550 MiB/s. Later on we have transitioned to the ESS-Tsc driver with the throughput of 950 MiB/s.

# Current issues
## Loss of data during simultaneous DMA transfers from both DDR banks
There is a bug in the TOSCA firmware or device driver causing data loss when the DMA transfer is performed simultaneously from two different memory banks using different DMA channels from different threads. The workaround is protections of the DMA transfer function in the userspace program by mutex, but this solution reduces performance.
## Tsc driver not supporting scatter-gather operations and prone to resource leaks
Tsc driver has high performance, but requires allocation of contiguous physical memory buffers for operation. When memory is fragmented, it is not possible to allocate these memory buffers and a CPU reboot is required. Tosca driver did not have this problem, but it offered much lower performance.
These memory buffers have to be manually allocated and are not freed automatically when the device file is closed. It requires appropriate signal handlers in the userspace program to avoid resource leaks.
## Problems with PCIe Gen3 link to Concurrent CPU
The PCIe link speed between Concurrent CPU and the IOxOS board alternates between Gen1 and Gen3 after each system reboot.
## Readback from algorithm parameters register blocks
Readback from algorithm parameters block does not work. It is a firmware issue and will be fixed.
## No separate interrupt support for both memory banks
Only one interrupt, common for both memory banks, is supported. It is a firmware issue and will be fixed.
## Tsc Driver cannot access PON space when run on Concurrent CPU
    TscMon ( and custom software applications ) fail to access registers placed on PON configuration space ( such as Power On for FMC cards ) when run on Concurrent CPU. The same software and TscMon commands can be successfully run on embedded IFC1410 processor. The bug prevents proper behaviour of the software when only one PCIe endpoint (to Concurrent) is present in the design.
# Performance evaluation

The proper firmware operation has been verified with the mem_dma_reader_tsc program. The firmware has a built-in reference data generator, providing the predefined test data. The collected raw data, identified events and the neutron summary received on the CPU side are compared against the results of the reference C++ implementation. The extensive tests, running for several days, have helped to detect several logic errors in the firmware as well as problems with the IOxOS platform.
For the purpose of evaluation of data throughput over the PCI-Express connection, both the scenario of continuous data transfer from two channels and the data transfer from the limited window around the beam pulse have been tested. Each test has been performed in two variants, with the DMA bug workaround and without it.

## Channels 8 and 11 enabled – continuous data transfer from both DDR banks, Concurrent CPU

Command line:
./mem_dma_reader_tsc -b 2048  -c 2304 -e 10 -s 3
Without DMA bug workaround:

DMA thread 1 : 5078069248 (0x12EAD3000) total bytes in 10000.121 ms => 484.277 MB/s
DMA thread 0 : 5078183936 (0x12EAEF000) total bytes in 10000.267 ms => 484.280 MB/s

CRC errors in channels 8 and 11 due to missing data have been observed, however no overwrite problems occurred.

With DMA bug workaround:
DMA thread 0 : 4177930240 (0xF9062800) total bytes in 10005.838 ms => 398.206 MB/s
DMA thread 1 : 4053379072 (0xF199A800) total bytes in 10006.128 ms => 386.324 MB/s
Several overwrite errors in channels 8 and 11 have been observed during the data acquisition.

As we can see, the DMA error workaround degrades the performance significantly. Even without the workaround, the system is barely able to retrieve data from two raw data streams.

## All channels enabled – raw data transfer with duty cycle 8.239 ms/65.535 ms, Concurrent CPU

Due to a firmware limitation, allowing maximum pulse period of 65535 microseconds, to simulate 9 ms data acquisition period with 14 Hz pulse frequency (71.4 ns) the acquisition time during a single trigger period has been set to 8.239 ms.

./mem_dma_reader_tsc -b 2048  -c 16383 -e 10 -s 3
Without DMA bug workaround:
DMA thread 1 : 2600857600 (0x9B05F000) total bytes in 9999.886 ms => 248.040 MB/s
DMA thread 0 : 3216953344 (0xBFBED000) total bytes in 10000.081 ms => 306.790 MB/s
During the data processing, CRC errors in multiple channels have been observed.
With DMA bug workaround:

DMA thread 1 : 2600828928 (0x9B058000) total bytes in 9999.104 ms => 248.057 MB/s
DMA thread 0 : 3216953344 (0xBFBED000) total bytes in 10000.056 ms => 306.791 MB/s
No errors have been observed.

As we can see, even with the DMA bug workaround, the system is able to continuously transfer data from 6 raw data channels, 6 event channels, periodic data channel and neutron summary from 6 channels.

# Future plans

As a next step, we are planning to implement the machine protection functionality. Then, we are going to update the periodic data channel according to the newest specification version. Finally, the smart trigger functionality will be implemented.

# References

[1]	Requirements and Technical Specifications - ESS nBLM System (https://jira.esss.lu.se/browse/BIG-1245)
[2]	Schedule technical annex to the in-kind contribution agreement signed between European Spallation Source and Department of Microelectronics and Computer Science, Lodz University of Technology on 2016-11-08; CHESS id: ESS-0149090