## Slide 1
14.05.2019
1
Sven Degenkolbe, Jörg Schacht, Reinhard Vilbrandt, Axel Winter, H.‑S. Bosch, Dirk Naujoks, Detlef Wieseler and the W7-X Team
Safe operation of the Wendelstein 7-X fusion experiment

## Slide 2
Outline
14.05.2019
1
Introduction of Wendelstein 7-X
  Goals
  Major elements
  Timeline
Main components and sources of hazards
  Heating systems
  Superconducting coil system
  Gas system
  High voltage
Structure of the control system
Conclusion

## Slide 3
About Wendelstein 7-X
14.05.2019
1
Max Planck Institute for Plasma Physics
Branch Greifswald  Wendelstein 7-X (Stellarator)
Data: Openstreetmap
Max Planck Institute for Plasma Physics
Branch Garching  ASDEX Upgrade (Tokamak)

## Slide 4
About Wendelstein 7-X
14.05.2019
1
Wendelstein 7-X is the world largest fusion device of the stellarator type.
Goals:
Prove the suitability of this type of magnetic confinement for a power plant
Plasma discharges up to 30 minutes

## Slide 5
Major elements and parameters of Wendelstein 7-X
14.05.2019
1
50 non-planar NbTi coils 5 types DC <18 kA
20 planar NbTi coils 2 types DC <16 kA
Central support ring
Helium piping
cryostat vessel 420 m3 thermal insulation
plasma vessel 80 m3
265 m2 in-vessel components
plasma 30 m3
4.5 m machine height 16 m machine diameter 735 t device mass 435 t cold mass 3.4 K
2.5 – 3 T magnetic induction on axis

## Slide 6
Construction of W7-X, 4/5 modules in the final position
14.05.2019
1
maschine
base
non-planar SC coils
plasma vessel
planar SC coils
outer
vessel
thermal insulation
central support ring
SC bus bar He piping

## Slide 7
View of the Wendelstein 7-X 2017
14.05.2019
1

## Slide 8
Timeline of the project Wendelstein 7-X
14.05.2019
1
10 years assembly
2004-2014
pump-down
cool down
magnet ramp-up
flux surfaces
2014
1st plasmas 5 limiters Eh4 MJ
Tp1s
2015
inertial cooling 10 divertors Eh200 MJ
Tp10-100 s
2017-2018
30 months assembly
2019-2021
water cooling 10 HHF divertors Eh18000 MJ
Tp100-1800s
2022 …
18 months assembly
2016

## Slide 9
Main systems
14.05.2019
1
Vacuum System
W7-X
Torus
Power Supply
Magnet System
Cryo Supply
Water
Gases
LHe, LN2
Signals
Current
Neutral gas
density
Energy
General Supplies
Liquid He & Liquid N2
Gases
Compressed Air
Ventilation & Air Conditioning
General Control: Signals, CDC & CSS
W7-X
Torus Hall Ground floor and Level -1
Torus Hall Level -2
Periphery
General Power Supplies
General Water Supply
Fire Protection System
Water Cooling System
Gas Introduction System
Plasma Heating Systems
Monitoring & Control:
Sensors & Diagnostics
Coding Location:
Access System
Technical Services
PS Heating Systems
W7-X central device
gas supply
cooling water
cryo supply
vacuum supply
power supply of magnet systems
plasma heating
diagnostics
monitoring and control
infrastructure (buildings,
general supply)

## Slide 10
Heating Systems
14.05.2019
1
Electron cyclotron resonance heating (ECRH)
max 1 MW at 140 GHz; 10 Gyrotrons
Neutral beam injection (NBI)
Hydrogen 1.65 MW per source; Deuterium 2.5 MW per source
4 sources
Ion cyclotron resonance heating (ICRH)
2 MW at 30 – 115 MHz, 2 generators
 non absorbed power inside the plasma vessel will damage components
Gyrotron 140 GHz, 1 MW

## Slide 11
Superconducting coil system
14.05.2019
1
50 non-planar coils 5 types; DC < 18 kA
20 planar coils 2 types; DC < 16 kA
2.5 – 3 T magnetic induction on axis
Mechanical forces on the structure up to 3.6 MN
Quench: coils loose superconductivity
 Quench detection system
Cooled with helium at 3.4 – 4.5 K
 Pressure relief system
Non-planar coil
Part of the pressure
relief system

## Slide 12
Gas system
14.05.2019
1
Use of hydrogen, deuterium for plasma experiments
Use of hydrogen, diborane for conditioning (glow discharge cleaning, boronization)
 Gas detection system

## Slide 13
High voltage
14.05.2019
1
110 kV feed-in and 20 kV feed-in
transformed to different voltage levels
For heating systems:
multi purpose high voltage supply DC:
ECRH 60 kV 50 A
NBI 65 kV 95 A
ICRH 30 kV 160 A

## Slide 14
Water cooling circuits
14.05.2019
1
At experiments: Cooling water with 28 °C
At baking: water at 150 °C p > 10 bar

## Slide 15
Different kinds of radiation
14.05.2019
1
Radiation produced by the heating systems (microwave, radio waves)
Lasers: 4 Systems with class 4 lasers
Radiation produced by the plasma  x-rays, ultra violet
During deuterium operation fast neutrons will be produced
Special requirements from the authority
Radiation monitoring system
Radiation protection area with special access
Currently no deuterium operation

## Slide 16
High-pressure water mist extinguishing system
14.05.2019
1
Example of one extinguishing area control cabinets
Thermal differential and thermal maximum detectors of all main cable shafts

## Slide 17
Process control system
14.05.2019
1
W7-X control system with hierarchical structure
Segment control (real time) plasma discharges
Programmable logic controller
Central operational management
 Process supervision functions

## Slide 18
Fast interlock system
14.05.2019
1
Plasma density, electron temperature, stray radiation, diamagnetic energy, temperatures of components are used to interlock the heating systems

## Slide 19
Central safety control system (cSS)
14.05.2019
1
central
control
local
control
K1
UK3
UK1
UK2
K3
UK3
UK1
UK2
K2
UK3
UK1
UK2
local
control
local
control
cSS
component xy:
safety interface
W7-X emergency stop
Operation permits
safe state signals
safety signals
safe state signals
local safety instrumented functions
central safety instrumented functions

## Slide 20
Organisational measures (examples)
14.05.2019
<number>
Safety analysis at the start of the design process of each component is mandatory
Functional Safety Management System established following the IEC 61511
Procedures before operation:
Before plasma operation systems are checked
Prior to plasma operation check for persons inside the radiation protection area
During plasma operation no access to the radiation protection area
 monitored by the cSS, if door is opened  operation permits revoked

## Slide 21
Conclusion
14.05.2019
<number>
Different kinds of dangers have to be considered at different operations modes
 System model will be developed
Requirements Engineering
The use of safety standards from industry is necessary