## Slide 1
Notes: Slide 1: Company Logo Full Page
Before you start editing the slides of your talk change to the Master Slide view:
Microsoft Office :Menu: View > Slide Master;
Macintosh – View > Master > Slide Master
Edit the following items:
On the Slide Master (first master slide) – lower area
a) On the left Delete the text and write the title of the event/Conference, Location
b) On the right delete the text and write the name and surname of the speaker and the date (day, month , year)
Close Master View

## Slide 2
Before the tender processes
  Magnet construction quality plan
  Magnet verification quality plan
  Magnet safety and standards
  Magnet interface description
  Design report documents
  CDR meetings
Technical specifications
Tender process
Construction, tests etc.

## Slide 3: D1, Q8 and C8 manufacturing, verification and quality plan
Notes: Slide 2: Title of the Presentation
Before you start editing the slides of your talk change to the Master Slide view:
Microsoft Office :Menu: View > Slide Master;
Macintosh – View > Master > Slide Master
Edit the following items:
On the Slide Master (first master slide) – lower area
a) On the left Delete the text and write the title of the event/Conference, Location
b) On the right delete the text and write the name and surname of the speaker and the date (day, month , year)
Close Master View
To start adding slides insert a new slide and select a Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank

## Slide 4: Table of contents
Manufacturing
  Manufacturing stages
  Magnets construction
    Yoke
    Coils
    Electrical connections
Verifications and Measurements
  Inspection and factory acceptance tests
    Yoke
    Coils
    Assembled magnet
Notes: Slide 3 – (..) : Content of the presentation
Insert a new slide: Home > “New Slide” and choose a slide Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank
If you want Copy & paste an element from the Clip Board to the particular slide: 1. Click on a box to mark it.
2. Position the mouse pointer on the box frame: Copy! 3. Click on the particular slide: Paste!
How you intend to use the elements is your choice. You can combine the text block style with the background colour in different manner.

## Slide 5: Table of contents
  Magnetic measurements
    Hall probe measurements
    Rotating coils measurements
Quality control
  Supplier selection
  Design review meeting
  Materials certifications and components datasheet
  Inspections
  Factory acceptance tests
  Magnetic measurements

## Slide 6: Manufacturing
Manufacturing stages
  The magnets (D1, Q8, C8) shall be completely outsourced. E-ST will provide
    the technical specifications and conceptual drawings
    the detailed magnetic design.
  The Supplier shall provide
    the mechanical design
    the magnetic measurements.
  A tendering process will designate the Supplier.
  A Design Review Meeting will be held to discuss and approve the Technical Files of the magnets.
    Verifications and measurements (types and procedures) shall be discussed and approved as well.
  After the approval of the Technical Files the construction of the magnets will begin.

## Slide 7: Manufacturing
Yoke construction
  Yokes (quadrants for the Quadrupoles and Correctors) will be realized gluing 1 mm laminations.
  Glue shall be high radiation resistant (epoxy resin compound).
  Yoke will be painted to protect the lamination pack against rust.
  The type of paint shall be specified in the Contract.
    The paint shall be flame retardant and high radiation resistant.
    The color shall be agreed with ESS and specified in the Contract
  Pole profile surfaces and components dedicated to the alignment shall not be painted.

## Slide 8: Manufacturing
Coils construction
  The coil windings shall be realized by means of OFHC copper conductors of proper cross section wrapped by a fiberglass layer. A further fiberglass layer wrapped on the formed coil will realize the ground insulation.
  Each coil shall be impregnated by means of suitable high radiation resistant epoxy resin and shall not be painted.
  No welding or junction of the conductor shall be allowed.
  The impregnated coil shall not be repaired by any means in case of defective one.
  Each impregnated coil shall be thermally protected by means of suitable thermal switches (normally closed) which will be glued on the coil during the assembly stage of the magnet construction.

## Slide 9: Manufacturing
Electrical connections
  The coils shall be connected according to the technical drawings of the specified magnet (drawings provided by the Supplier).
  The electrical connections to the relevant power converter shall take place in a protected location on one side of the magnet (to be agreed).
  The connection between the coils terminals shall be realized with copper conductor of proper cross section.
  The thermal switches protecting the coils of the magnet shall be connected in series in such a way not to form a current loop.
  The electric distribution circuit of each magnet shall be insulated from the magnet yoke (which shall be grounded) and able to sustain a specified test voltage.

## Slide 10: Quality and verifications
Designation of the Responsible persons.
User – ESS
WPR
Customer – E-ST
PL
Supplier
RP

## Slide 11: Quality control
The Supplier shall be selected by a tender process.
A Design Review Meeting (DRM) will be held; the Supplier shall prepare a Technical File to be discussed and approved. It will include:
  The construction drawings and the construction process description for each type of magnet,
  A detailed time schedule concerning the deliverables object of the Contract,
  The detailed procedures concerning the tests and verifications envisaged during the magnets construction,
  The detailed procedures concerning the magnetic measurements.
  The detailed procedure of the Factory Acceptance Tests.

## Slide 12: Quality control
After a successful DRM the E-ST PL will release formal approval for the next stages.
  Construction (with tests and verifications)
  Factory acceptance tests
  Magnetic measurements

## Slide 13: Quality control
Certifications and datasheets
  All the materials selected for the construction will comply with the European rules and regulations and, in particular, will comply with the document ESS-0063691 - List of allowed/not allowed materials to be incorporated in equipment to be installed in the accelerator tunnel.
  The Supplier shall provide certifications and data sheets for the materials and components.
    Magnetic iron to be used for the yoke construction
    Copper pipes to be used for the coils construction
    Epoxy resin Araldite F® to be used for the coils impregnation
    The varnish to be used to paint the magnetic yokes
  All the certifications and data-sheets shall be included in a Technical Report.

## Slide 14: Quality control
Inspections – Yoke
  The first 10 stamped laminations shall be dimensionally checked. Then the laminations shall be verified one out of 10000 pieces.
  Each assembled yoke (quadrant for the Quadrupoles and Correctors) shall undergo an extensive dimensional check session. The procedure shall be proposed by the Supplier and approved by E-ST.
  Only for quadrupoles and Correctors
    Once assembled, the 4-quadrants yoke will undergo an extensive dimensional check session. Critical areas will be listed in the technical specifications (full aperture region, critical overall dimensions etc.).
    The above dimensional check shall be repeated after opening the yoke in 2 halves and closing it again.
  Verification results will be included in a Technical Report.

## Slide 15: Quality control
Inspections – Coils
  Visual inspection.
  Dimensional verifications.
  Ground insulation and an inter-turn insulation test. The procedures shall be proposed by the Supplier and approved by E-ST.
  Coil resistance measurement. The procedures shall be proposed by the Supplier and approved by E-ST.
  Pressure test and temperature test. The procedures shall be proposed by the Supplier and approved by E-ST.
  Test results will be included in a Technical Report.

## Slide 16: Quality control
Inspections and Factory Acceptance Tests – Assembled magnets.
  Dimensional check to guarantee the conformity with the technical drawings (poles profile geometry and other critical areas).
  Only for Quadrupoles and Correctors – The test shall be repeated after opening an closing the magnet.
  Electrical continuity test between the yoke and every other metallic component not related to the main electrical circuit. The procedure shall be proposed by the Supplier and approved by E-ST.
  Ground insulation test. The procedure shall be proposed by the Supplier and approved by E-ST.
  Hydraulic tests (pressure and flow test). The procedure shall be proposed by the Supplier and approved by E-ST.
  Tests result will be included in a Technical Report.

## Slide 17: Quality control
Magnetic measurements
  Hall probe measurements session
  For mapping the magnetic field along the magnet mid-plane, in a specified region which will include the good field region. Procedure proposed by the Supplier and approved by E-ST.
  Rotating coil measurements session
  For analyzing the harmonic content of the magnetic field. Procedure proposed by the Supplier and approved by E-ST.
Magnetic measurement results will be described in a dedicated technical report.

## Slide 18
Thank you
Notes: Last Slide 2: Aerial Photo of Elettra