## Slide 1: MEBT Integration Status and Plans
Joao Paulo Martins
Control Systems Engineer
European Spallation Source ERIC
2020-01-30

## Slide 2: Introduction
(Extracted from Thomas Fay/Philippe Rabis’ presentation)
I think ICS has some room for improvement in communication of system statuses to stakeholders, hopefully this helps somewhat.
This time slot won't give sufficient duration for many details.
Intention here is mostly to provide a rapid-fire overview.
Several internal ICS projects need to reach "usable" maturity for RFQ commissioning and beam to MEBT FC (Calibration Service, Critical PV access authorisation, IOC deployment).

## Slide 3: MEBT Integration Status and Plans
MEBT Control System Overview
EPICS Integration Aspects
MEBT Chopper Controls
MEBT Magnets Controls
Conclusion
Summary

## Slide 4: MEBT Integration Status and Plans
MEBT Control System Overview
EPICS Integration Aspects
MEBT Chopper Controls
MEBT Magnets Controls
Conclusion
Summary

## Slide 5: MEBT Control System Overview
The full-scale MEBT:
Eleven (11) Magnets (quadrupoles with combined H/V correctors);
Three (3) RF cavities (bunchers);
Chopper;
Nine (9) different types of diagnostics instruments;
MEBT at a glance

## Slide 6: MEBT Control System Overview
Controls Hardware
The Full Scale Control System
Mag.
Chopper
Buncher
BPM
BCM
nBLM
FC
EMU
WS
SC
BSM
NPM
x 11
x 3
x 7
x 4
x 4
x 3
x 3
x 2
MTCA
ECAT
PLC
VM
MTCA
PLC
VM
MTCA
PLC
VM
MTCA
MTCA
MTCA
MTCA
MTCA
MTCA
MTCA
PLC
ECAT
ECAT
PLC
ECAT
ECAT
LLRF
RFLPS
SSA
Control

## Slide 7: MEBT Control System Overview
Controls Software: an (rough) estimation of the number of IOCs:
  Not considering MPS, Vacuum and various soft IOCs running on VMs;
Estimation of the number of IOCs
Quad. Control IOC (1)
Ster. Control IOC (22)
Mag. LPS (1)
Chopper IOC (1)
Chopper LPS (1)
SSA Control IOC (3)
RFLPS - SIM IOC (1)
RFLPS - FIM IOC (3)
LLRF IOC (3)
BPM IOC (2)
BCM IOC (2)
nBLM IOC (4)
FC IOC (1)
EMU IOC (1)
SC IOC (3)
EMU LPS IOC (1)
SC LPS IOC (1)
WS IOC (3)
NPM IOC (2)
BSM IOC (1)
Total = 26
Total = 10
Total = 21
Total ~= 57 IOCs and counting…

## Slide 8: MEBT Control System Overview
Controls Hardware
The Full Scale Control System
Mag.
Chopper
Buncher
BPM
BCM
nBLM
FC
EMU
WS
SC
BSM
NPM
x 11
x 3
x 7
x 4
x 4
x 3
x 3
x 2
MTCA
ECAT
PLC
VM
MTCA
PLC
VM
MTCA
PLC
VM
MTCA
MTCA
MTCA
MTCA
MTCA
MTCA
MTCA
PLC
ECAT
ECAT
PLC
ECAT
ECAT
LLRF
RFLPS
SSA
Control

## Slide 9: MEBT Control System Overview
Controls Hardware
The system for first phase (SSR2A)
Mag.
Chopper
Buncher
BPM
BCM
nBLM
FC
EMU
WS
SC
BSM
NPM
x 11
x 3
x 7
x 4
x 4
x 3
x 3
x 2
MTCA
ECAT
PLC
VM
MTCA
PLC
VM
MTCA
PLC
VM
MTCA
MTCA
MTCA
MTCA
MTCA
MTCA
MTCA
PLC
ECAT
ECAT
PLC
ECAT
ECAT
LLRF
RFLPS
SSA
Control

## Slide 10: MEBT Integration Status and Plans
MEBT Control System Overview
EPICS Integration Aspects
MEBT Chopper Controls
MEBT Magnets Controls
Conclusion
Summary

## Slide 11: MEBT Integration Status and Plans
MEBT Control System Overview
EPICS Integration Aspects
MEBT Chopper Controls
MEBT Magnets Controls
Conclusion
Summary

## Slide 12: EPICS Integration Aspects
Motivation:
  Speed up IOC development;
  Standardization;
  To support different EPICS Base version, different EPICS modules versions, for different architectures;
What E3 is?
  A build facility for EPICS IOCs;
  A runtime environment for EPICS IOCs;
  A collection of EPICS modules (extensions) and IOCs maintained by ICS;
What E3 is not?
  The deployment system for the EPICS IOCs;
  Something that will prevent your IOC to run (if the workflow is followed);
ESS EPICS Environment (E3)

## Slide 13: EPICS Integration Aspects
I have this IOC running on EEE, now I have to port it to E3;
  The structure is almost the same, for *most* of the IOCs this is a matter of minutes (or hours);
  HW & Integration Group is here to help you;
I need this EPICS extension on my IOC, is it compatible with E3?
  Please take a look to the pool of modules already supported on E3. Almost everything you need will be there (calc, stream, sequencer, mrfioc2, ecmc, ADCore, any many more);
  If not, HW & Integration Group is here to help you;
Is my IOC going to load the same modules after reboots, E3 updates, etc..?
  YES. Your IOC will load the modules according to the versions that YOU specified;
I need to learn how to develop with E3!
  There is extensive training material on Confluence: https://confluence.esss.lu.se/display/HAR/ESS+EPICS+environment+%3A+e3
ESS EPICS Environment (E3)

## Slide 14: EPICS Integration Aspects
ESS EPICS Environment (E3)
There is a lot to be developed and integrated yet, though:
  Deployment system;
  Critical PV access authorization;
  Calibration Service;
  MASAR service;
  Experiment data archiving;
ICS is committed to the deliver all the Control System Services with quality, but focus should be to run IOCs!
EPICS Base version 7.0.3.1 is the default; (https://confluence.esss.lu.se/x/4iN8Ew)
CS-Studio / Phoebos / BOY / Display Builder – still work to do;

## Slide 15: EPICS Integration Aspects
Standard IOC Features
Autosave:
  Periodically saves the current value of pre-defined PVs into a text file;
  ICS Infra Group already have the permanent storage (with backup) for these files;
iocStats:
  Provides EPICS PVs with diagnostics about the running IOC: memory and CPU consumption, uptime, heartbeat signal;
  Enables remote reboot of the IOC;
recSync:
  Publish the list of PVs of the IOC to Channel Finder Service;
Archiving:
  Configuration of the archiving system is made outside the IOC: Archiver Appliance;
Alarms and Access Security:
  Built-in features of EPICS; Should be defined by system leader and implemented by integrator;

## Slide 16: MEBT Integration Status and Plans
MEBT Control System Overview
EPICS Integration Aspects
MEBT Chopper Controls
MEBT Magnets Controls
Conclusion
Summary

## Slide 17: MEBT Integration Status and Plans
MEBT Control System Overview
EPICS Integration Aspects
MEBT Chopper Controls
MEBT Magnets Controls
Conclusion
Summary

## Slide 18: MEBT Chopper Controls
Architecture
Pulser PS (-)
MicroTCA Crate
MicroTCA CPU
MicroTCA Event Receiver
Timing Events
Fine delay
Digital out
Pulser PS (+)
Local Protection PLC
50 Ω
50 Ω
MEBT Fast Chopper
Serial commands
Trigger pulses
MEBT Chopper Beam Dump
Temperature Signals
Power Supply
Status
Output to MPS:
Chopper Status
(relay output)
VM

## Slide 19: MEBT Chopper Controls
Rack components were installed with temporary power;
Local tests performed:
  Pulsers communication;
  Event Receiver and fine delay outputs (standalone mode);
  PLC integration with EPICS;
Main OPI already in Display Builder format;
  PLC IOC OPI needs to be ported;
Next activities:
  Clear definition of timing events that will drive the MEBT Chopper;
  Integrated tests;
  Verification of PLC signals;
Status

## Slide 20: MEBT Chopper Controls
For the next phase: integration with FBIS;
  FBIS needs to know if emergency mode really happened;
  Overall status (LPS status) informed to MPS from the PLC;
  Digitalization of the voltage signals that goes to the loads;
Interface Control Document (under review):
  CHESS Document: ESS-1530169
Future integration with FBIS

## Slide 21: MEBT Chopper Controls
High-voltage pulsers configurable parameters (PVs):
  Manual/remote;
  Amplitude (1 kV to 2.75 kV);
  Pulse Width (1us to 20us);
Trigger configurable parameters:
  Coarse delay from event reception;
  Fine delay (nanosecond range);
  Distance between pulses *;
Event Receiver System (MRF EVR) is flexible and easily configurable, we need clear definition on when to trigger the pulsers from an operational point of view;
Operation
t
Event reception
at the EVR
Electric trigger
at the EVR output
Coarse delay
Fine
Delay

## Slide 22: MEBT Chopper Controls
Operation
Timing System Events and HV Pulsers Outputs
t
PULSE
COMING
HV Pulse
Pulse current before MEBT Chopper
Pulse current after MEBT Chopper
PULSE
START
PULSE
END
t
t
PULSE
START
PULSE
END
PULSE
COMING

## Slide 23: MEBT Integration Status and Plans
MEBT Control System Overview
EPICS Integration Aspects
MEBT Chopper Controls
MEBT Magnets Controls
Conclusion
Summary

## Slide 24: MEBT Integration Status and Plans
MEBT Control System Overview
EPICS Integration Aspects
MEBT Chopper Controls
MEBT Magnets Controls
Conclusion
Summary

## Slide 25: MEBT Magnets Controls
MEBT Magnets combine quadrupole with horizontal and vertical corrector functions;
One dedicated power supply for each component: 11 x 3 = 33 PS;
  Unipolar PS with 300 A output for quadrupole;
  Bipolar PS for the H/V correctors;
One dedicated rack for each magnet;
Local Protection System implemented with Siemens PLC;
  EPICS IOC runs on virtual machine;
Architecture

## Slide 26: MEBT Magnets Controls
CAEN FAST PS has an embedded EPICS IOC;
  The integration is extremely facilitated by this feature;
The same power supply will be used in the LEBT;
OPIs already re-designed and compatible with Display Builder;
20 units placed in FEB racks;
Steerers Controls

## Slide 27: MEBT Magnets Controls
Quadrupole Controls
Dedicated unipolar quadrupole power supply;
Up to 300A output;
MODBUS interface;
FAT to happen soon!
IOC needs to be validated;
OPIs to be converted to Display Builder;

## Slide 28: MEBT Magnets Controls
Local Protection System implemented with Siemens S7 PLCs (CPU + distributed IO modules);
PLC monitors the following signals for each individual magnet:
  Magnet windings sensor (thermoswitch);
  Cooling water temperature;
  Cooling water flow;
  Power Supply status (hardwire);
In case of any faulty condition, local permit to the PS will be revoked and Machine Protection (MPSMag) will be notified;
MPSMag ICD (under review): ESS-0494755
Local Protection System

## Slide 29: MEBT Magnets Controls
Local Protection System

## Slide 30: MEBT Integration Status and Plans
MEBT Control System Overview
EPICS Integration Aspects
MEBT Chopper Controls
MEBT Magnets Controls
Conclusion
Summary

## Slide 31: MEBT Integration Status and Plans
MEBT Control System Overview
EPICS Integration Aspects
MEBT Chopper Controls
MEBT Magnets Controls
Conclusion
Summary

## Slide 32: Conclusion
MEBT Chopper is almost ready for integrated tests;
Correctors Magnets PS needs firmware update and registration to the Control System, but after that they are ready for integrated tests;
Quadrupoles PS will be integrated and tested in Bilbao;
Diagnostics systems (FC, BPM, BCM) being developed and led by BI with the support of ICS;
ICS is fully committed to deliver high level services and controls;
HW&I Group feels enthusiastic about the next commissioning round: focus to “make system run”;
What still needs to be done:
  All OPIs ported/developed to Phoebus/Display Builder;
  IOC configurations for alarms, archiving and access control (need input from system owners);
  All sorts of adjustments and optimizations…
  Documentation;
Considering the first commissioning round

## Slide 33
Questions / discussions;
Special thanks to Idoia Mazkiaran and ESS Bilbao team;
MUITO OBRIGADO!
“Courageous convictions will drag the dream into existence.”
- Neil Peart (1952 – 2020)
- Vital Signs, Rush – Moving Pictures