## Slide 1
Long Pulse Klystron Modulators
and
IOT Power Supplies
based on the
SML (Stacked Multi-Level) topology
advantages and challenges over conventional topologies
Carlos A. Martins
RF Electrical Power Systems
www.europeanspallationsource.se
December 11th, 2013

## Slide 2
Introduction
Klystron / IOT modulator strategy
Two parallel paths:
  1.- Use commercial klystron modulators (without imposing the topology)
  330 kVA (2 klystrons in parallel);
  2.- Develop a new topology that could be used to power IOT’s and klystrons (with minimal modifications)
  660 kVA (4 klystrons / IOT’s in parallel)

## Slide 3
The Stacked Multi-Level (SML) topology
- Principle
AC grid
50Hz
400V
High Voltage
DC or long pulsed
One module
AC grid
50Hz
400V
AC /
DC
DC-link
1.1 kV
DC /
DC
Capacitor bank
1 kV
DC /
AC
AC
15 kHz
1 kV
HF
Transf.
AC
15 kHz
25 kV
AC /
DC
AC + DC
15 kHz
25 kV
DC
(25 kV,
klystrons)
(12.5 kV,
IOT’s
Filter
One module:

## Slide 4
The Stacked Multi-Level (SML) topology
- Principle
AC /
DC
DC-link
1.1 kV
DC /
DC
Capacitor bank 1 kV
DC /
AC
AC
15 kHz
1 kV
HF
Transf.
AC
15 kHz
25 kV
AC /
DC
AC + DC
15 kHz
25 kV
Filter
Module #1
AC /
DC
DC-link
1.1 kV
DC /
DC
Capacitor bank 1 kV
DC /
AC
AC
15 kHz
1 kV
HF
Transf.
AC
15 kHz
25 kV
AC /
DC
AC + DC
15 kHz
25 kV
Filter
Module #N
DC
(115 kV,
klystrons)
(50 kV,
IOT’s
Complete system. Multiple stacked modules connected:
In parallel at the input (grid) side; - In series at the output (HV) side;

## Slide 5
The Stacked Multi-Level (SML) topology
400V,
3-phase, 50Hz
~1 kV
~1 kV
~1 kV
Sinusoidal current absorption;
Power factor correction;
Precise capacitor charging;
Regulation of charging power (flicker free);
Pulse forming;
Droop compensation;
Arc protection
Galvanic isolation;
Voltage amplification;
Modulator main functions by sub-system

## Slide 6
Key points:
Modular concept, allowing increasing the power by adapting the number of modules, keeping their size and weight under control;
Compatible both with PULSED and CW operations and with different types of RF amplifiers (Klystrons, IOT’s, tetrodes, etc.);
Up to 660 kVA average power possible, allowing the supply of 4 x 1.2MW klystrons / IOT’s in parallel;
Lower cost due to usage of standard LV components into a great extent (price target: ~500 €/kWav);
No active power electronic devices placed inside oil tanks (facilitates maintenance);
Reduced footprint/volume due to minimal sub-systems count (sub-systems integrate multiple functions);
Improved efficiency (~94%), due to minimal number of conversion stages;
Excellent AC grid power quality (flicker-free, sinusoidal current absorption, unitary power factor);
400V,
3-phase, 50Hz
Standard “of-the-shelf” LV components
Special HV components & assembly:
in an oil tank: klystrons;
in a dry HV deck: IOT’s
~1 kV
~1 kV
~1 kV
The Stacked Multi-Level (SML) topology

## Slide 7
Other important advantages
ESS will be able to specify an open topology and assure full technical competence on the topology:
facilitates maintenance;
construction of the full scale prototype and series production could be undertaken by a much broader number of companies (even with limited past experience in designing of modulators);

## Slide 8
Development of a reduced scale prototype
in collaboration with Lund Technical University
Pulse voltage: 115 kV;
Pulse current: 20 A;
Pulse power (elect): 2.3 MW;
Pulse width: 3.5 ms;
Pulse repetition rate: 14 Hz;
Average power output: 115 kW;
Average power grid: 126 kVA;
DC (or slow pulsed) voltage: 50 kV;
Pulse current: 34 A;
Pulse power (elect): 1.95 MW;
Pulse width: 3.5 ms;
Pulse repetition rate: 14 Hz;
Average power output: 98 kW;
Average power grid: 104 kVA;
Developed to serve both as a klystron modulator and as an IOT HV Pulsed power supply(*)
Klystron modulator
IOT HV pulsed power supply
(*)
- Same LV power electronics in air insulated cabinets;
- Different HV tank assembly;
400V,
3-phase, 50Hz
LV power electronics
HV tank assembly

## Slide 9
Done (by Dec. 9th 2013):
- Detailed thermal calculations and selection of main components;
Power circuit schematics;
Preliminary mechanical layout;
Control loop studies and simulation for the LV stage (AC grid side + cap. charger);
Selection and purchase of digital controller;
Purchase of power converter stacks; Contact of a local assembly company ;
First meeting with Stangenes held on Sept. 10th for discussions on HV oil tank assembly;
To be done (from Jan. 2014 to end 2014):
Launch call for tenders for: 1)- HV tank assembly; 2)- HV dummy load;
Detailed mechanical layout and cabling;
Control loop studies and simulation of the HV stage (Max Collins, consultant);
Modeling of parasitic elements in HV tank assembly and mitigation;
Simulation of the entire circuit with controls;
Programming of the controller;
Testing and validation;
Construction and equipment of a HV power electronics lab at LTH;
Status of the reduced scale prototype development

## Slide 10
Simulation Results: AC grid front end (1 module)
ZOOM

## Slide 11
Power circuit schematics (in Dec. 9th 2013)
To be detailed into something like this…
(wiring diagram)

## Slide 12
Mechanical layout of the reduced scale prototype
(preliminary)
Note:
For the full scale system, the different blocks shown would expand naturally, keeping the same mechanical layout arrangement

## Slide 13
The Controller: Compact RIO from National Instruments
NI cRIO-9082 Real Time
Volt. Meas. NI-9220, with Dsub
- 100 kS/s, 16 bit, per channel
- 3 x 16 channels
Digital Output NI-9401, with DSub terminals
- 100ns, 5V/TTL, per channel (SE)
- 4 x 8 channels
NI 9155
MXI-Express RIO
Digital Input. NI-9401, with DSub
- 100ns, 5V/TTL, per channel (SE)
- 2 x 8 channels
Relay NI-9481
- 250Vac/2A
- 2 x 4 channels
Voltage Output NI-9269
- 100 kS/s/channel (+/-10V)
- 4 channels, 16 bit
Digital Output NI-9474
- 1us, 5 to 30V,
- 8 channels, sourcing output
Arrival at ESS by now !!!

## Slide 14
Thank you.