## Slide 1: What is all the fuss about IOTs?
Morten Jensen
AD and ICS Retreat Meeting 2013

## Slide 2
2 GV, 125 MW DC supply wanted!
ESS needs power at high frequency (352 and 704 MHz).
Mains power is at 50 Hz!
Convert mains AC to DC and then DC to high frequency AC
Klystrons are typically used for high power accelerators.
They exist at the power levels needed for ESS.
They are really pretty good, reliable and quite efficient.
IOTs at ESS parameters don’t exist.
They may be more complicated.
They need to be developed and carry risk.
Why all the fuss?
Why do we need all these amplifiers?

## Slide 3
The Inductive Output Tube
Invented in 1938 by Andrew V. Haeff as a source for radar
To overcome limitation of output power by grid interception
Pass beam trough a resonant cavity
Achieved: 100 W at 450 MHz, 35% efficiency
Used first in 1939 to transmit television images from the Empire State Building to the New York World Fair
IOTs then lay dormant
Intense competition with velocity modulated tubes (klystron had just been invented by the Varian Brothers.
Difficult to manufacture
The IOT is often described as a cross between a klystron and a triode hence Eimac’s trade name ‘Klystrode’

## Slide 4
IOT
(Density modulated)
Biased
Control Grid
RF input
RF output
Reduced velocity spread compared to klystrons
Higher efficiency
No pulsed high voltage
Cheaper modulator
Control
Acceleration
Deceleration = RF Output
Magnetic field
How does it work?
Source
Beam

## Slide 5
Typical Broadcast IOT
Courtesy of e2v

## Slide 6
Pin
Pout
Klystron/MBK
IOT
MB-IOT
Operating
Power Level
hsat ~ 65-68%
ESS ~ 45%
Back-off for feedback
High gain
Low Gain
Long-pulse
excursions possible
Short-pulse
excursions possible
IOT’s don’t saturate.
Built-in headroom for feedback.
~ 70%
Courtesy of CPI
The Performance Comparison
If you understand klystrons this may help – if not it probably won’t.

## Slide 7
Klystrons
IOTs
Electrical Power Consumed
Power delivered to beam
Power delivered to beam
High Beam Current
Low
Beam Current
Cartoon!

## Slide 8
Small
High Efficiency
Cost typically does not scale with output power
Low power consumption in standby or
for reduced output power
No pulsed HV
IOT Advantages

## Slide 9
3rd Generation Light Source
Storage Ring
Three 500 MHz 300 kW amplifier for SR
- 4 x 80 kW IOT combined
One 80 kW for the Booster
Serial Number
Filament Hours
30000
20000
10000
In Operation
Test system
Operational Hours at Diamond
Peter Martin, Diamond

## Slide 10
CPI 90 kW IOT (K5H90W1)
> 33 000 operating hours
Metrology Light Source
(Willy Wien Laboratory)
Elettra
500 MHz
150 kW IOT based amplifier for Combination of 2x80 kW
CERN
800 MHz
60 kW
Other Facilities using IOTs
12 IOTs

## Slide 11
For high power accelerators:
Power requirement for 500 kW – 1.5 MW
Narrow band (single output cavity)
Single beam – Large cathode
High voltage
High cathode loading
Oil in the modulator and gun
Multi beam - Several smaller cathodes
Higher total perveance
-> Lower voltage
Lower cathode loading
Scalable for higher power levels
(100-140 kW per cathode)

## Slide 12
Design and Simulation
Analytical and Numerical codes available
Commercial codes well developed in addition to manufacturers own
Increased computing power allows improved simulation of grid structures, trajectory and PIC modeling
Gun simulation
IVEC 2009
CPI
CPI
TED

## Slide 13
Higher order mode pillbox cavity or toroidal
Individual beam pipes
Coaxial output coupling
Output cavity considerations
Simulations include:
Field (static and RF)
Trajectory
Particle

## Slide 14
Calabazas Creek Research, Inc. – 352MHz, 200 kW CW
Some components being prepared (not for ESS)

## Slide 15
700 MHz HOM IOT Experience
Design Parameters value units
Power Output 1000 kW (min)
Beam Voltage 45 kV (max)
Beam Current 31 A (max)
Frequency 700 MHz
1dB Bandwidth ± 0.7 MHz (min)
Gain 23 dB (min)
Efficiency 71 % (min)
Diameter 30/76 in/cm
Height 51/130 in/cm
Weight 1000/450 lbs./kg
Collector Coolant Flow 220 gpm
Body Coolant Flow 10 gpm
O/P Window Cooling (Air) 35 cfm
  VHP-8330A IOT
@ 31kV
Test Results (pulsed)
RF Input
Collector
Solenoid,
O/P Cavity
Gun
RF Output
CPI

## Slide 16
Applications of High Power Induction Output Tubes in High Intensity Superconducting Proton Linacs
Testing of Inductive Output Tube based RF amplifier for 650 MHz SRF Cavities, A. Mandal et al, PCaPAC2012
90 kW CW IOT development at L3 Communications Electron Devices, M Boyle et al, CWRF Workshop, 2012
Development of a 402.5 MHz 140 kW IOT, M Read et al, PAC2011
The first continuous wave and long pulse operation, DESY, 2011
Simple Model of an Inductive Output Tube, R. Carter, IEEonED 2010
CPI’s 1.3 GHz, 90 kW Pulsed IOT Amplifier, M. Marks et al, IPAC2010
Modelling and Design of High-Power Inductive Output Tubes, E. Wright et al, PAC2009.
Highly stable IOT based 1.3 GHz/16kW RF Power Source for CW operated SC Linacs, SRF2009
The ALBA RF Amplifier System based on IOTs, P. Sanchez et al, EPAC2008
Installation and Commissioning of the new 150 kW plant for the Elettra RF System Upgrade, A Fabris et al, PAC07
Grid less IOT for Accelerator Applications, C. Wilson et al, PAC2007
IOT testing at the ERLP, J Orrett at al, EPAC2006
First Results of the IOT Based 300 kW 500 MHz Amplifier for the Diamond Light Source, M. Jensen et al, EPAC05
IOT RF Power Sources for Pulsed and CW Linacs, H. Bohlen et al, Lunac2004
Comparison of Klystron and Inductive Output Tubes Vacuum-Electron Devices for Amplifier service in Free-Electron Laser, EPAC04
Recent IOT publications by Laboratories
(not a comprehensive review)
Many Labs are still thinking about IOTs but we need Industry

## Slide 17
 | Single Beam Klystron | MB IOT | 
Peak output Power | 1 | 1 | MW
Cathode Voltage | 95 | 50 | kV
Beam Current | 21 | 31 | A
Efficiency at saturation | 65 | 65 (min) | %
Est. efficiency for operation | <45 | >60 | %
Gain | 48 | 23 | dB
A 700 MHz Comparison
1.3 m
0.6 m

## Slide 18
Where next?
Accelerating Structure | Freq. (MHz) | Quantity | Max Power (kW)
RFQ, DTL | 352 | 5 | 2200**
Spoke | 352 | 30 | 330**
Elliptical Medium Beta | 704 | 34 | 860**
Elliptical High Beta | 704 | 86 | 1100**
** Plus overhead for control
The ESS Requirement
Time to develop Super Power IOT
Green
Innovative
Carbon Neutral
Power saving from high beta – 20 GWh per year

## Slide 19
Parameter |  | Comment
Frequency | 704.42 MHz | Bandwidth > +/- 0.5 MHz
Maximum Power | 1.2 MW | Average power during the pulse
RF Pulse length | Up to 3.5 ms | Beam pulse 2.86 ms
Duty factor | Up to 5% | Pulse rep. frequency fixed to 14 Hz
Efficiency | Target > 65% | 
High Voltage | Low | Expected < 50 kV
Design Lifetime | > 50,000 hrs | 
Tenders for prototypes due back on 19 February 2014
Work is being carried out in collaboration with CERN
ESS to procure prototypes
CERN to make space and utilities available for testing
Target: Approval for ESS series production in 2017/18

## Slide 20
Thank You