## Slide 1: Designs of the Spoke and Elliptical Cavity Cryomodules
P. Bosland
CEA/Saclay IRFU
On behalf of the cryomodule technical demonstrator teams

## Slide 2: The ESS linac
 | Num. of CMs | Num. of cavities
Spoke | 13 | 26
6-cell medium b | 9 | 36
5-cell high b | 21 | 84
Segmented, superconducting linac, with RT focusing elements

## Slide 3
IPNO
IPNO in charge of the design fabrication and assembling
    Uppsala in charge of the
      * Tests stand for cryogenic and RF power tests FREIA (Yogi ‘s presentation)
      * Tests of the spoke cryomodule with IPNO
FR – SW agreement + amendment
Stephen Molloy
Technical Demonstrator
Spoke Cavity Cryomodule
Sébastien Bousson – WP4

## Slide 4
Collaboration IRFU – IPNO
P. Bosland WP5 - G. Olivier
IPNO in charge of the cryostat – design and fabrication
    Vacuum vessel
    Space frame – cavity supports
    Thermal screen
    Superinsulation
    Internal cryogenic pipes
    Instrumentation
IRFU in charge of the “cavity package”, the cryomodule assembly and RF power tests:
    Cavities + helium tank
    Power coupler design, manufacturing, RF tests
    Piezo tuner
    Magnetic shield
    Tooling: field flatness, cavity preparation, cryomodule assembling, …
    Cryomodule assembly
    Tests stand for cryogenic and RF power tests
    Tests of the ECCTD cryomodule
FR – SW agreement + amendment
Christine Darve
Technical Demonstrator
Medium beta ECCTD

## Slide 5
2 double spoke cavities cryomodules
2900 mm
Diameter
1350 mm

## Slide 6: 4-cavity cryomodules
Similarity with SNS in size and purpose : reuse the same concepts
Common design for medium and high beta
  Main components are identical : vaccum vessels, thermal shield, supports, alignment system, etc.
  Only few elements differ : details in cryo piping, beam pipe bellows
6600 mm
Elliptical Cavity Cryomodules
ECC
Diameter
1200 mm
1500 mm
  57mm: length difference between 6-cell medium and 5-cell high beta cavities

## Slide 7: ECC cross-section
50K Thermal shield (Aluminum)
Lateral port
(CTS, alignment)
Tie rods (TA6V)
Positioning jacks
(3 at 120°)
Power coupler
Waveguide transition
Guide rail and wheel
Space frame
Vacuum vessel
(stainless steel - 1200 mm diam.)
Two phase He pipe
Positioning optical devices

## Slide 8
2 double spoke cavities cryomodules
2900 mm
Diameter
1350 mm
Cavities supported by rods fixed on the vacuum tank
No spaceframe

## Slide 9: RF parameters
 | Medium | High
Geometrical beta | 0.67 | 0.86
Frequency (MHz) | 704.42 | 
Number of cells | 6 | 5
Operating temperature (K) | 2 | 
Epk max (MV/m) | 44 | 44
Nominal Accelerating gradient (MV/m) | 16.7 | 19.9
Q0 at nominal gradient | > 5e9 | 
Qext | 7.5 105 | 7.6 105
Iris diameter (mm) | 94 | 120
Cell to cell coupling k (%) | 1.22 | 1.8
p and 5p/6 (or 4p/5) mode separation (MHz) | 0.54 | 1.2
Epk/Eacc | 2.36 | 2.2
Bpk/Eacc (mT/(MV/m)) | 4.79 | 4.3
Maximum. r/Q (W) | 394 | 477
Optimum b | 0.705 | 0.92
G (W) | 196.63 | 241
RF peak power (kW) | 1100 | 
Elliptical cavities
Spoke cavities
Frequency (MHz) | 352,2
Optimum beta | 0,50
Operating temperature (K) | 2
Nominal Accelerating gradient (MV/m) | 9
Lacc (bopt.x nb gaps x l/2) (m) | 0,639
Bpk (mT) | 79 (max)
Epk (MV/m) | 39 (max)
Bpk/Eacc (mT/MV/m)) | <8,75
Epk/Eacc | <4,38
Beam tube diameter (mm) | 50
RF peak power (kW) | 335
G (W) | 130
Max R/Q (W) | 427
Qext | 2,85 105
Q0 at nominal gardient | 1,5 109

## Slide 10
Ti He vessel
Ti cone and tuner attachement
Hydroformed Ti bellow
(+/- 3mm range)
Power coupler port
Stiffeners on the Spoke bars
(vacuum pressure)
Spoke cavity
Medium beta elliptical cavity
Stiffeners
(Lorentz force detuning compensation)
418 mm
1259 mm
550 mm
994 mm

## Slide 11: HOMs in the medium beta cavity
Frequency (MHz) | r/Q (Ohm) | QL estimate
1506.48 | 0.444 | 13000
1509.32 | 0.0021 | 7000
1515.76 | 0.0020 | 5000
1524.86 | 0.127 | 3000
1534.57 | 0.0001 | 2000
1542.20 | 0.0032 | 3000
High beta has 1 L-band below cutoff
Medium beta
r/Q versus beta

## Slide 12: Medium beta cavity HOM catalog …
! HOM frequency 1762MHz close to 5 x beam frequency !

## Slide 13: Above cutoff but…
Energy mainly trapped in the 4 inner cells

## Slide 14: Work in progress to allow the mode to escape from the inner cells and be damped outside the cavity
Qloaded = 5.1e4

## Slide 15: Medium beta RF/Mechanical parameters
Cavity wall thickness (mm) | 4
Tuning sensitivity (kHz/mm) | 217
Stiffness (kN/mm) | 1.47
KL static Lorentz coefficient (Hz/(MV/m)²) (fixed ends) | -0.71
KL static Lorentz coefficient (Hz/(MV/m)²) | -21.1
KL static Lorentz coefficient (Hz/(MV/m)²) for Kext=21 kN/mm ( ) | -2.06
Max. relative pressure (bar) in He vessel at 300K keeping V.M. stress in cavity wall < 40 MPa (fixed ends, pressure test case) | 2.2
Max. Von Mises stress (MPa) in cavity wall with 1.5 bar in helium vessel | 28
R rings
R rings
Fixed
ends
Free
ends
Free
ends
Fixed
ends
Static Lorentz detuning
Pressure sensitivity

## Slide 16: Piezo tuners working at cold
CTS linearity at 4.2K of type V-HIPPI
Type V for SPL beta = 1 5-cell prototype - +/- 3 mm range on the cavity
Elliptical cavities:
Tuner of Saclay V type
2 piezo stacks
Stepper motor and planetary gearbox (1/100e) at cold and in vacuum

## Slide 17
Piezo tuner – type Saclay V
tested with the HIPPI cavity

## Slide 18: Fundamental power coupler Spoke: 335 kW Elliptical cavities: 1100kW
Test of the HIPPI power coupler on the HIPPI cavity at 1.8 K, full reflection
HIPPI power coupler (KEK-type window) tested to 1.2 MW, 10% Duty factor at Saclay

## Slide 19: Magnetic shield
Limit contribution of the trapped flux to the surface resistance to 4 nW
limit the external static field to Bext = 14 mG.
→ required shielding efficiency equal to 35.
Achievable with 1.5 mm, µr =20000 shielding material
Ex: magnetic shield of the elliptical cavities

## Slide 20: ECC Cavity strings
Spoke cavities with couplers
2 elliptical cavities with couplers, tuners and magnetic shields

## Slide 21
Cavity string assembly in clean room
Cold mass assembly (outside the clean room)
Thermal shield
Spaceframe
Vacuum
vessel
Design concept of the tooling: most of the parts will be used for both types of cryomodules
Main steps of the assembly procedure

## Slide 22
Assembly procedure in clean room
Procedure for elliptical cryomodules:
Tooling for spoke cavities:
Tooling for elliptical cavities:

## Slide 23
Assembling tools in clean room at IPNO

## Slide 24
Assembly procedure: outside the clean room
Procedure for elliptical cryomodules:

## Slide 25: High beta prototype cavity

## Slide 26
Start of the development of cavity preparation with the SPL 5-cell cavity b=1
Very similar to the ESS cavities
Vertical Electropolishing system of the SPL cavity at b=1 in Saclay
cavity preparation

## Slide 27
Thank you for your attention