## Slide 1
SAMPLE ENVIRONMENT
Overview of day 1 equipment and possibilities
Daria Noferini
CSPEC ICEB 1, 8th June 2020

## Slide 2: Scientific specifications
CSPEC promises to the community
TG2 [ConOps document]
  CSPEC shall probe magnetic excitations in magnetic fields up to 12 T.
  CSPEC should follow kinetic processes with time steps of less than 1 minute.
  The design of the instrument will accommodate the sample environment equipment required to match the science case.
  The systems design shall provide the space and flexibility necessary to host and drive future developments, for instance further focusing optics for smaller sample sizes, possibly integrated into the sample environment, further in-situ sample environment such as secondary characterization (RAMAN or NMR), and polarization analysis.
  Sample environment within the CSPEC scope for the wide range of scientific cases studied on CSPEC should be consistent with the demands of signal to noise.

## Slide 3: The sample environment pot
Where everything happens

## Slide 4: The sample environment pot
Flexibility for science
cryogenic vacuum
Gate Valve
(Al, 2.5-4 mm)
Protective barrier
high SNR
specific scientific case needs
/ ambient p

## Slide 5: The sample environment pot
Flexibility for science
high pressure
gas absorption/desorption
combined characterization
operando measurements
controlled humidity
high temperature
small samples
high magnetic field

## Slide 6: Day 1 equipment (in scope)
Day 1.0
Cryofurnace
T-range 3-600 K
ΔT = 0.1 K
ILL
Janis
Sample rotation stage and goniometer
6 T magnet
(from HZB)
Oxford inst.

## Slide 7: Day 1 equipment (in scope)
Day 1.1
Dilution insert
Michel Caussignac’s PhD thesis (1980)
ISIS
12 T magnet (access to)
HZB
Automatic sample
changer
Pump and probe setup
In kind collaboration
J. Pieper, Univ. of Tartu (Estonia)
Details t.b.d (Harald Schneider/SAD)
ESRF
In situ optical activation of the biological function of a membrane protein + time-dependent QENS.
SNS
S
S
S
A

## Slide 8: Further (preliminary) ideas
Extend the pump and probe
From proteins to different scientific cases
E.g. Solid electrolytes for intermediate temperature fuel cells

## Slide 9: Further (preliminary) ideas
Simultaneous combined characterization
QENS/INS @CSPEC
structure (indirectly)
(especially if long wavelengths are used)
complementary timescale
IR, Raman, DLS, DSC, NMR, dielectric spectroscopy…
Ongoing proposal with Roskilde University (Bo Jakobsen, Kristine Niss, Dorthe Posselt) Focus on soft, glassy and biological matter
Peltier based sub cryostat @ ESS (SANS)
Cell for QENS+dielectric spectroscopy at high pressure @ ILL
Possible other collaborations
E.g. DLS + NSE @ JCNS/RWTH Aachen University

## Slide 10: Further (preliminary) ideas
Special sample environment for biology
Hazardous material, controlled humidity, simultaneous characterization…
Covid-19 related grant opportunities across EU
[e.g. Swedish Research Council– VR (SE), Lighthouse (DK) etc.]

## Slide 11: Further (preliminary) ideas
From ideas to action
Find interested partners
Resources &
people
Start of the project
ESS sample environment support groups
Other instrument teams (e.g. T-REX, MIRACLES…)
Interaction and coordination with
&
Continue to identify the needs of scientific communities

## Slide 12
Thank you for attention!
Questions for the team?
People from SAD?

## Slide 13
Something more?
(backup slides)