## Slide 1: DESY and European XFEL
Dirk Nölle
DESY, MDI
XFEL, WP-17
Beam Diagnostic Mini Workshop
at ESS AB ( Linneasalen )
Notes: How to edit the title slide
Upper area: Title of your talk, max. 2 rows of the defined size (55 pt)
Lower area (subtitle): Conference/meeting/workshop, location, date, your name and affiliation, max. 4 rows of the defined size (32 pt)
Change the partner logos or add others in the last row.

## Slide 2: Accelerator Consortium
Notes: How to edit the title slide
Upper area: Title of your talk, max. 2 rows of the defined size (55 pt)
Lower area (subtitle): Conference/meeting/workshop, location, date, your name and affiliation, max. 4 rows of the defined size (32 pt)
Change the partner logos or add others in the last row.

## Slide 3: Accelerator Complex: 17.5 GeV Start -up Version
100 accelerator modules
800 accelerating cavities
1.3 GHz / 23.6 MV/m
25 RF stations 5.2 MW each

## Slide 4: XFEL – Parameter Set
 | Baseline | New Parameter Set
Electron Energy | 17.5 GeV | 10.5/14/17.5 GeV
Bunch charge | 1 nC | 0.02 - 1 nC
Peak current | 5 kA | 5 kA
Slice emittance | < 1.4 mm mrad | 0.4 - 1.0 mm mrad
Slice energy spread | 1.5 MeV | 4 - 2 MeV
Shortest SASE wavelength | 0.1 nm | 0.05 nm
Pulse repetition rate | 10 Hz | 10 Hz
Bunches per pulse | 3000 | 2700

## Slide 5: E-XFEL/FLASH Time Structure: High Duty Cycle
Repetition rate
Macro-pulse
Bunch
Slice
t
I
100ms
Duty cycle ~ XFEL 0.65%
1-5 mA
t
I
XFEL 600s
Macro-pulse duration
I
t
I
XFEL 222ns
bunch spacing
1 nC
100-500 fs
2.5kA
Up to 27000 Bunches/s
FLASH and E-XFEL will have the same time structure

## Slide 6: Status Accelerator Modules
material for production of 640 cavities almost completely delivered and quality checked
remaining material ordered
weekly meetings with involved companies
83 cryostats and cold masses ordered
call for tender for remaining 20 by Q1/2012
contracts for cold magnets, current leads, HOM absorbers, frequency tuners, couplers, BPMs awarded with delivery of pre-series and series components matched to module production schedule

## Slide 7: Accelerator Modules
‘XFEL village’ at Saclay:
string & module assembly
training with prototype modules ongoing
first pre-series assembly planned Q1/2012
Almost all infrastructure for the series production in place
Accelerator module test facility at DESY:
cavity, magnet & module tests,
klystron and waveguide tests
cryogenics installation ongoing
training with prototypes
first cavities tests planned Q2/2012
first module tests planned Q3/2012

## Slide 8: Cold Linac Infrastructure
Contracts for klystrons, modulators, pulse cables awarded
Pulse transformers to be awarded Q1/2012
Modulator hall constructed

## Slide 9: Cold Linac Infrastructure
Refurbishment of HERA cryo plant started
Challenging schedule because of early operation start in 2014 to operate the XFEL injector
Planning, production and installation of cryogenic equipment for accelerator and AMTF continued

## Slide 10: Tunnel
Tunneling is almost finished, about 6 km of tunnel have been build

## Slide 11: Injector
Injector access shaft (XSI)
junction of 1st and 2nd injector
(only one built for start-up)

## Slide 12: Injector
Low remanence focusing quadrupoles produced
Prototype of transverse deflecting structure produced, to be installed at PITZ
3.9 GHz accelerator module (for bunch length control), design finished, prototype cavities in test
Start Commissioning End 2014
Laser heater mechanical design matured, first components tendered

## Slide 13: Bunch Compression
R56=60-120mm
R56=
60-120mm
R56=30-100mm
ss = 2 mm
Ipeak= 50 A
sE = 0 %
E = 130 MeV
ss = 1 mm
Ipeak= 100 A
sE = 1.5 %
E = 130 MeV
ss = 0.1 mm
Ipeak= 1 kA
sE = 1 %
E = 500 MeV
ss = 0.02 mm
Ipeak= 5 kA
sE = 0.3 %
E = 2000 MeV
3 stage bunch compression for wide range of compression scenarios and minimized sensitivities to RF-regulation imperfections and electron beam driven instabilities

## Slide 14: Bunch Compression
Gun
ACC1
3rd
ACC2
ACC3
ACC4
ACC7
~
~
BAM
BCM
BCM
BAM
BAM
Laser
LLRF
LLRF
LLRF
A 
A 
BC2
BC3
R56=180mm
R56=43mm
R56=0.8mm
FLASH 1
FLASH 2
FLASH 3
LLF + BLC + MIMO + BBF at ACC1/ACC23
(act still on setpoint)
< 20fs rms arrival jitter
< 75fs pkpk
with adaptive SP correction
without adaptive SP correction
Beam Based Feedbacks for control of longitudinal parameters
Measurements of beam arrival time (BAM) and bunch compression (BCM) feedback on RF parameters
Concept implemented and tested at FLASH
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 15: Collimation & Beam Distribution
Collimation
Feedback
Distribution
Dump
Undulators
Collimation system for beam halo cleaning and emergency beam stop
Transverse Intra-Bunch Feedback
Flexible beam distribution system for quasi-simultaneous operation of two primary electron beam lines

## Slide 16: Beam Distribution Shaft – XS1

## Slide 17: European XFEL – Undulators
Tendering process for > 450 m undulator started
Focusing quadrupoles manufactured and shipped for precision fiducialization
Prototype of undulator intersection set-up in mock-up tunnel

## Slide 18: Schedule
Tremendous progress of construction, infrastructure planning and ramp up of accelerator component fabrication
Working hard to finish installation in time for
  start of injector commissioning mid 2014
  start of linac commissioning mid 2015
  observe first SASE by end of 2015

## Slide 19: Touch Points ESS - XFEL
What are fields, where development can be reused by,
or easily adapted to ESS?
Crate System: MTCA.4
LLRF: System Design suited, Frequency needs Adaption
Timing System: Similar Time Structure/Requirements
Machine Protection System: Very Similar Requirements
Diagnostics: Some Common Requirements
  (Cold) BPMs
  Beam Loss Monitors
  Beam Size Measurements
    Screens
    Wire Scanners
  Dosimetry System

## Slide 20: XFEL goes µTCA (MTCA.4)
XFEL will be based on the new MicroTCA.4 standard
  Double size AMC modules with PCIe link to CPU
  Rear Transition Modules for signal conditioning
All Diagnostic Systems (except BPM) go for µTCA
  Best integration to
    XFEL timing system
    Machine Protection System
    Use common firmware framework and
      server infrastructure
  Use Standard Boards
    DESY DAMC02
    Struck 8300: 10x16 Bit, 125 MHz ADC
    Industrial Boards are coming up
  Custom made rear transition modules (RTM)

## Slide 21: µTCA: Clocks, Triggers and Interlocks
Enc.Clock
Trigger
Enc.Clock
Trigger
Interlock
AMC
ADC
AMC
ADC
To Timing Distribution
MCH
Cross-
Point-Switch
AMC
Timing
2 radial clocks per AMC,
Low jitter, configurable direction
8 bussed M-LVDS lines,
For triggers, clocks and interlocks
Backplane
Cross-
Point-Switch
Ethernet and PCIe
Interlock
MTCA.4

## Slide 22: MicroTCA Remote Management
Online status of modules:
Inserted, fault
Temperatures, voltages
Reset, power on/off
Act. Power consumption

## Slide 23: Compact and unified accelerator controls @ MTCA.4
High reliability /hot-swap /remote diagnostics /shelf management
High data rate / flexible in configuration
Display of a MicroTCA crate with actual status
Shows e.g. LEDs and temperatures
One AMC with details
Open with click on module
Defines the remote management on all system levels (AMCs, RTMs, fans, power supplies)
µTCA rear transition modules
  Rear management (30W max)
  Double size AMC with Zone 3 plug to RTM
Clock and trigger distribution on the backplane
  Allow data acquisition with ps stability
  Trigger multiple AMCs from a bus
  Distribute interlocks on the backplane
Provides low latency links between FPGAs (point-2-point)
Common data distribution to FPGA on a bus
µTCA backplane (MTCA.4):
  µTCA standard Ethernet
  µTCA standard SATA
  µTCA standard PCIe, 4 lanes
  4 bi-directional point-2-point
  8 term. M-LVDS bus lines
  2 radial clocks
  1 PCIe clock

## Slide 24
FLASH and XFEL Low Level RF system
  32 cavities @ 10MW RF klystron station
  >100 RF signals real time processed per RF station
  Controller: adaptive feed-forward / MIMO feedback
  Beam loading 5mA with flexible bunch pattern
  Automatic cavity frequency tuning + Piezo compensation LFD
  QL tuning, flat gradient operation, quench detection
  Klystron life time management system
  Compact (need to reduce space x 6)
  Stability requirements: dA/A < 0.01%, d < 0.01 deg
A/A=3e-5
=4mdeg
LLRF and MTCA.4

## Slide 25
LLRF layout cost optimized for large number of RF channel
Compact and unified accelerator controls @ MTCA.4
Klystron Driver
Up-Conversion Section
10xDown-converter
10x16bit/125MSPS ADCs
Controller
for XFEL x 6 DAQ units
are used
ZONE 3
ZONE 3
AMC Backplane
Rear transition module
Advanced Mezzanine Card
AMC Backplane
Down-converter:
f= 100MHz-4GHz
Klystron driver:
f = 100MHz-4GHz
Cost optimized version
1 or 2 cavity control:
Combine DWC & Klystron driver
Combine ADC & Controller
 2 boards instead of 4
cost reduction for LLRF
controls
Approx. hardware costs:
~ 25 kEuro per RF station
(includes: 6xRF, 1VM, 2xPZT driver, LO,
12 slot crate, MCH, PS, CPU, Timing,
MPS, Stepper motor, RF backplane,
+ 6 free slots for BPM/HOM/KLM/others)
RF in
RF out

## Slide 26: XFEL Timing System
New timing system
  Fiber optic links 1.3GHz
  with drift compensation
  AMC prototype is receiver and transmitter
  ps stability (< 5ps RMS)
  Clock, trigger and event distribution
1.3GHz
Clock
Data

## Slide 27: XFEL Timing System
Distributed system connected by compensated LWL links
1.3 GHz Line Speed with 130 Mb/s data rate
Deliver Triggers and Clocks
Provide deterministic data transfer of Pulse related data
Stongly tied to the MPS system

## Slide 28: Maschine Protection System
Distributed, fast and configurable OR Gate
Collects fast and slow interlock signals for complete Machine Status
  Fast within RF Pulse: BLM, Transmission Interlock; Couplers; LLRF (Quench Protection) …
  Slow from Pulse to Pulse: Magnets, RF; Valves; Screens, …
Beam Operation only if matched to Machine Status
Cut RF Pulse in case of fast Interlocks
MPS Boards based on µTCA (DAMC02)
LWL based independent communication between the modules
Beam termination by switching off Drive Laser, RF systems, and Kickers
Suited to operate with Beam Switches

## Slide 29: Machine Protection System
Operator dials in requested bunch pattern
MPS „ANDs“ Bunch Pattern with Machine Status
  Depending on Screens, Scanners, Magnets, …
Allowed Pattern info distributed via Timing System
  Pattern checked by Laser and Charge diagnostics, inconsistent with prediction -> abort
  Transmission, BLM, Coupler or any fast alarm -> abort
Alarm Masking on XFEL bunch level
Two Abort Locations/Mechanisms
  Stop Injector: Stop Beam Production
  Distribution Kicker System to Dump
Reaction Time about 15 µs (worst case, dominated by signal travel.)

## Slide 30: Charge Monitor System
XFEL Operation Range 0.02 – 1 nC
  Charge monitors provide noise level of less than 1 pC, and
  will run up to 2 nC
~ 40 Conventional transformers (Toroids)
Location: Between „functional sections“ of the machine
Toroids are connected by a fast network to interlock on transmission failures (TPS)
Detect
  “Poor transmission”
  Bunch pattern failure
  Bunch distribution failure

## Slide 31: Cold BPM, Buttons
2 Types of Cold BPM (Button, Re-entrant Cavity)
Modest Resolution: 50 µm
Operation at few k Level (connected to cold quad)
Close to the Cavities -> Clean room Class 10!
Installed in XFEL Prototype Accelerator Modules
Series Production of Bodies ongoing
First Feed-throughs (about 100) delivered
Button
String of PXFEL3

## Slide 32: BPM Mechanics
Potential for In-house BPM Design and Construction
  BPM bodies (Buttons, Cavities, Striplines)
  Feedthroughs
    RF designs: In-House
    Fabrication in Industry (some also In-House)

## Slide 33: BPM Electronics
DESY has a long tradition in BPM Electronics Design
With exception of PETRA III (ITECH) and XFEL (In-kind Contribution PSI) all machines use in house BPM electronics
Recent Development:
Low Charge Button BPM electronics for FLASH II
RTM to be used with SIS800 16 bit, 125 MHz ADC
Single Bunch Electronics using the delay line principle
Uses processing power of VIRTEX5 on the SIS800
Prototyping will be finished in Summer
Commissioning of FLASH II planned for Spring 2013

## Slide 34: Beam Size Measurements
Hotspots for Screens/WS
4 stations with known phase advance
for optics characterization
Two systems:
  ~ 50 Screens
  12 (fast) Wire scanners
  Some installed at the “same” place
FLASH result -> OTR not usable for compressed Beams, => extensive R&D Program for luminescent Screens
Wire scanners
  Triggered, Fast scans within a bunch train (1 m/s)
  Also Slow Scans
  Will be compatible to ISO5 (CRC 100)
Both DESY In-House developments, parts purchased from industry
Screen Mover
Vert. Wire scanner
Hor. Wire scanner
Light
Beam

## Slide 35: Screen Systems: Screen Mover for low particle installations
Design for ISO5 (CRC100)
Separated vakuum/motor part
Easy to adapt to different stroke
Connection to MPS

## Slide 36: Beam Loss Monitor System for XFEL
Readout
Electronics
micro-TCA crate
HV
Power supply
PMT
Scintillator
Beam Loss Monitor
e,γ,n0
Alarm (to Machine Protection System)
~350 Beam Loss Monitors (More than half – in undulator area)
DAMC02 with custom RTM
8 Channel/board; double width
Comparator, ADC, Alarm Generator
Test Pulse Driver
HV driver for Cockcroft Walton
Fast Interface to MPS
BLM will use mostly Scintillators some Cherenkov radiators
Use electromagnetic showers
Prototypes of BLMs build and tested in FLASH
Production of housings and scintillators subcontracted to IHEP
Electronics production In House (via DESY ZE)

## Slide 37: Dosimetry – system components & setup
Sensor chip (γ)
DESY AMC2 (µTCA)
Host platform integration
Frontpanel interface of AMC board conducts undulator dosimetry signals
(12-slot µTCA production-crate)
FMC
mezzanine
card slot
Dosimetry mezzanine card (FMC) on AMC motherboard for the Machine-Protection-System (MPS) carries dosimetry for measurements inside shielded electronic racks
Frontpanel interface allows connection of external dosimetry sensors
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 38: Thank you
For your attention
And thanks also to all the colleagues, who supplied me with material