## Slide 1
Wire scanners and Halo measurements in ESS Cold linac
Benjamin Cheymol
Beam diagnostic workshop, Lund 2012-03-21

## Slide 2: Outline
Introduction
Thermal load
Integration
Detector
Halo measurement

## Slide 3: Introduction
Profile measurement with wire scanner will be used for commissioning and cross check for non invasive profile during operation
WS and non invasive profile will be positioned in the warm section of the cold linac.

## Slide 4: Introduction
Graphite wire can not be used close to the cryo module
Tungsten wire will be used
The wire scanner will be operated in SEM mode in the Spoke section.
Shower will be measured in medium and high beta sections.
Mechanical design similar to the warm linac wire scanner (Slow wire scanner)

## Slide 5: Thermal load
1000
Less critical than the warm Linac
500 ms beam pulse can be used above 300 MeV (2x2 mm beam size)
Beam energy [Mev]
2500
2000
1500
500
2500
3000
2000
1500
1000
3500
Tungsten wire 50 mA, 500 μs
σx=σy=2mm
Tmax [K]

## Slide 6: Detector
Different option for detector
    Scintillator
    Ionization chamber
    Cerenkov detector
    Solid state detector
Cover all the azimuthal coordinate
Segmented detector
    Spatial information of the shower

## Slide 7: Integration
Wire scanner will share the same space with non invasive profile
Example of integration with non invasive profile (luminescence monitor)

## Slide 8: Issues
Shielding due to the non invasive profile has to be estimated
Estimation of the emittance increase
Uncontrolled losses
    Quadrupole activation
    Heating of cryomodule

## Slide 9: Halo measurement
A telescope can be used to detect event in coincidence
    At low energy the number of event is low
    Impossible to fit in the warm section
Investigate the possibility of using active element in the beam

## Slide 10: Outlook
Monte Carlo simulations on going
    Shielding
    Detector choice
    Cry module heating
Check the different solutions for Halo measurement

## Slide 11
Thanks for your attention