## Slide 1: Welding of Port Tubes to Monolith Vessel Scope of Work, Requirements and Acceptance Criteria
Dr. Sara Ghatnekar Nilsson, WPM Monolith Systems, target division

## Slide 2: Agenda
1 ESS Basics
2 Scope of Work, Requirements and Acceptance Criteria
3 Tolerances

## Slide 3: ESS Basics, Target and Instruments
ESS Instrument Layout
ODIN
DREAM
NMX
MIRACLES
BEER
C-SPEC
T-REX
MAGIC
BIFROST
HEIMDAL
FREIA
LoKI
SKADI
VESPA
ESTIA
Monolith
Accelerator tunnel
Instrument hall
West sector
Instrument hall
North sector
Neutron beam guides

## Slide 4: ESS Basics, Monolith Vessel and Port Tubes
ESS-Beam Instrumentation
PBW Vessel
Proton beam
Proton beam
Proton Beam Window
Proton Beam Instrumentation Plug
Moderator and Reflector
Target Wheel
Neutron Beam Port Tube
Monolith Vessel
Target Monitoring Plug
Monolith Vessel
Port tubes
nn-bar
Neutron beams to sample stations.

## Slide 5: ESS Basics, Monolith Vessel and Port Tubes
ESS-Beam Instrumentation
Proton beam
Proton Beam Window
Proton Beam Instrumentation Plug
Moderator and Reflector
Target Wheel
Neutron Beam Port Tube
Monolith Vessel
Target Monitoring Plug
Neutron beams to sample stations.
Neutron beam port tube
Neutron beam insert carrying the optics
Neutron beam

## Slide 6: ESS Basics, Monolith Vessel and Port Tubes
Manufacturer Vessel: AVS and Cadinox
In-Kind from ESS-Bilbao
Method: Submerged arc-weld and TIG weld towards vacuum side
Facts: Diameter≈6m, H:6m, W:40 tons
Manufacturer tubes and nn-bar: Ensa and Asturfeito
ESS-managed contract
Method: Laser weld
Facts nn-bar:
L: 2.7m, H:0.9m, Width:1m
W:11 tons (frame) + 18 tons (adapter)
Facts tubes at Vessel side:
L:2.7m, H:0.7m, Width:0.2m
W:1.2 tons

## Slide 7
Scope of Work, Requirements and Acceptance Criteria
2

## Slide 8: Scope of Work
3 tubes in place
3 tubes in place
view from inside of the Monolith Vessel
The scope of work is under a contract between ESS-Bilbao and Ensa and is focused in the welding of the 39 Port Tubes, the NN-Bar Frame and the Connecting Pipe to the Monolith Vessel.
The delivery of Port Tubes and NN-Bar Frame is under the scope of Ensa. The Monolith Vessel and Connecting Pipe supply is In-Kind delivery from ESS-Bilbao.
Work on site consists of:
Work preparation (protections, scaffolding, laydown area, water, air, electricity, tools, etc)
Lifting and alignment of components before welding
Welding of 39 Port Tubes + 1 NN-Bar Frame + 1 Connecting Pipe
Non-destructive testing of the welds (includes pressure test)
Dimensional control after welding

## Slide 9: Legal Requirements
Legal requirements that need to be fulfilled:
AFS 2017:3 (Swedish regulations)
AFS 2016:1 (PED, Swedish regulations)
Construction code: EN 13445
Directive 2014/68/EU (PED)
Mechanical classification: MQC4A
AFS 2006:8 pressure testing (Swedish regulations)
The requirements are met by following:
KFM (Design basis)
Welding procedures: EN ISO 15614-1
Welds acceptance criteria: EN ISO 5817 (Class B)
Welders qualification: EN ISO 9606-4/ EN ISO 14732
Special training of welders (RSQ)
Visual Testing (VT): EN ISO 17637/ EN ISO 23277
Dye penetrant Testing (PT): EN ISO 3452-1/ EN ISO 5817 (Level B)
Radiographic Testing (RT): EN ISO 17636-1 (Class B) / EN ISO 10675-1 (Level 1) / EN ISO 19232-3 (Class A)

## Slide 10: Functional Requirements
Fulfil dimensional requirements after welding.
The welds must :
  Withstand mechanical loads according to KFM ESS-0135150
  Be leak tight and according to vacuum standards
ESS-3185128
Installation drawing
KFM ESS-0135150

## Slide 11: Requirement on Weld Thickness
A decision was made to have 8mm thickness in the welding area.

## Slide 12: Acceptance Criteria
Welds acceptance criteria: EN ISO 5817 (Class B)
Individual leak tests of the tubes < 10-6 Pa m3 / s (10-5 mbar l / s).
Shape and position of tubes after welding must be fulfilled according to tolerances on installation drawing.
Pressure test of the Confinement system (PBW port block, tubes and lower & upper Vessel).

## Slide 13
Tolerances
3

## Slide 14: Tolerances
Originally, the space requirements between tubes and inserts were extremely tight. The main reasons were to prevent streaming, and that the tolerance input from NSS was in the range of fractions of mm in order to not loose the scientific signal-to-noise ratio.
Several tolerance chain workshops have been held at ESS with a holistic perspective under leadership of ESS Technical Coordinator Dr. Masatoshi Arai, resulting in a relaxation of some strict tolerances, e.g. the range in the xyz-window around the focal point that Instruments can view in order to not loose signal-to-noise ratio were relaxed to X±5mm; Y±3mm; Z±2mm

## Slide 15
Tolerances by Robert Svensson
Work Unit Lead for Neutron Beam Port Blocks
3