## Slide 2: Strategy for RP and REMS for instruments
PRESENTED BY Joffrey germa

## Slide 3: Agenda
1 RP veto
2 Access to the roof and the beam line
3 Shielding configuration management
4 Monitoring

## Slide 4: RP veto
  As requested for accelerator, RP has required means to prevent:
  Access
  Operation
  The access RP veto could be used to prevent access into the cave without RP if the sample is foreseen to have a high dose rate after beam.
  The operation veto key could be used to prevent operation during an unsafe situation (e.g. removal of shielding)

## Slide 5: Access to the roof and the beam line
  Access to the roof:
  If classified as supervised area, no specific requirement
  If classified as controlled area, access should be restricted by PSS or RP
  Access to the beam line:
  WO and RWP needed
  Prevent operation (shielding configuration management)
  Survey during the opening of shielding (close shielding if necessary)
  Work is done
  Shielding reinstallation and RP check before allowing operation

## Slide 6: Shielding configuration management
  Main reference in shielding:
ESS Handbook for Radiation Protection Chapter 9. Shielding ESS-0239725
ESS rules for configuration control of radiation shielding for safety ESS-0240190
ESS procedure for designing shielding for safety ESS-0019931
  Definition:
  Radiation shielding for safety, hereafter “shielding”, refers to a physical barrier installed for the purpose of passively lowering exposure of people to ionising radiation. Shielding passages (e.g. ventilation, cable ducts or chicanes) in the shielding are part of the shielding itself. The installation of the barrier can have multiple purposes, but if one of the purposes of the installed material is that it shields radiation, it shall be considered as shielding.

## Slide 7: Shielding configuration management
  Radiation Protection (RP) configuration control of movable shielding applies when the shielding is not controlled by a Personnel Safety System (interlock or ”key management”)
  Permanent shielding shall require tools, keys or other mechanical means such as hoists or lifting vehicles to move. Hence, some shielding is controlled by its size or weight.
  When a shielding is not in place, Operational RP shall apply operations or access veto to hinder any possible exposure to ionising radiation until the shielding has been restored.

## Slide 8: Monitoring
  What is foreseen?
  1 monitor around the cave to check the area classification
  1 monitor as close as possible to sample environment inside the cave to give a dose rate information before entering
  Questions:
  How to treat alarms around the cave? (local alarm, shutter, proton beam)
  How to ensure that the shutter is closed and efficient? (PSS, monitor)

## Slide 9: Finish presentation