## Slide 1: UCN Source: SD2 in moderator cooling block
Blahoslav Rataj
On behalf of the HighNESS consortium
Second Workshop on UCN and VCN Sources at ESS, 9 - 10 May 2023

## Slide 2: Outline of the presentation
(i) A location of moderator moderator cooling block in the ESS target model
(ii) Calculating PUCN using the UCN production cross-section in SD2
(iii) Designing the UCN SD2 converter with a cylindrical channel
(iv) Designing the UCN SD2 converter with a direct view on the NNBAR emission surface
(vi) Testing the gamma shielding made of Bismuth
(v) Testing the water reflector around the converter
Notes: Aggiungi international collaboration

## Slide 3: Placing the UCN SD2 converter into the moderator cooling block (option 2)
Adapted from Zanini, L., et al. "Very cold and ultra cold neutron sources for ESS." Journal of Neutron Research Preprint (2022): 1-17.
Notes: Aggiungi international collaboration

## Slide 4: The position of moderator cooling block in the target monolith
Adapted from Zanini, L., et al. "Very cold and ultra cold neutron sources for ESS." Journal of Neutron Research Preprint (2022): 1-17.
Adapted from Odén U. ”Virtual tour of the ESS monolith.” Workshop on Very Cold and Ultra Cold Neutron Sources for ESS (2022).
Notes: Aggiungi international collaboration

## Slide 5: The position of moderator cooling block in the target monolith
Adapted from Santoro, V., et al. "Development of a high intensity neutron source at the European Spallation Source: The HighNESS project." arXiv preprint arXiv:2204.04051 (2022).
Notes: Aggiungi international collaboration

## Slide 6: Current baseline model with the moderator cooling block
Possibility to design a solid deuterium converter in the moderator cooling block (MCB) that would make use of the cold neutrons streaming from the LD2 moderator to produce ultracold neutrons (UCNs)
NNBAR FOM for the baseline model
  2.53 x 1017 n⋅Å2/s/sr
NNBAR experiment
Notes: Aggiungi international collaboration

## Slide 7: Selecting the UCN production cross-section for solid deuterium
MCNP cannot transport UCNs
  Ultracold neutron production rate PUCN [n/s/cm3] can still be calculated using a UCN production cross-section for solid deuterium and cold neutron spectrum measured in MCNP
  Investigated various available UCN production cross-sections for the solid deuterium
Notes: Aggiungi international collaboration

## Slide 8: Selecting the UCN production cross-section for solid deuterium
Adapted from Gutsmiedl, E., et al. "Production of ultra-cold neutrons in solid α-oxygen." Europhysics Letters 96.6 (2011): 62001.
Used in our calculations of PUCN
UCN energy < 150 neV
Notes: Aggiungi international collaboration

## Slide 9: Map of PUCN for the baseline model calculated with the Munich cross-section
UCN production rate PUCN [n/s/cm3] was calculated to compare different models of a SD2 converter
Notes: Aggiungi international collaboration

## Slide 10: Designing the solid deuterium UCN converter with a channel - initial idea
Initial idea: Designing a cylindrical channel through the twister to supply cold neutrons to the solid deuterium converter in MCB
Created a parametric model of the channel and UCN converter
Measured PUCN in the spherical UCN converter and NNBAR FOM simultaneously
The goal of optimisation:
  Maximize PUCN and minimize the loss in NNBAR FOM at the same time
Notes: Aggiungi international collaboration

## Slide 11: Designing the solid deuterium UCN converter with a channel - initial idea
4 parameters were varied in this model:
  Spherical UCN converter
    x coordinate of the centre
  Spherical UCN converter
    z coordinate of the centre
  Cylindrical channel
    radius R
  Cylindrical channel
    position of opening x’
Notes: Aggiungi international collaboration

## Slide 12: Designing the solid deuterium UCN converter with a channel - initial idea
Conducted a general study – fixed R while varying the position of UCN detector sphere and channel opening
  Reported highest PUCN for a given case in the table below
    The position of the UCN detector sphere that minimised the channel length led to the highest PUCN for each case
Notes: Aggiungi international collaboration

## Slide 13: Designing the solid deuterium UCN converter with a channel - initial idea
Conducted a general study where the parameters were varied
Findings:
  A bigger channel radius gave rise to a higher PUCN, but at the cost of loss in NNBAR FOM
  Altough the Be filter cut a part of the neutron spectrum (2.5 – 4 Å) that contributed to the UCN production cross-section, the highest PUCN was measured when the channel opening was aligned with the Be filter. In this case, the distance between the LD2 moderator and spherical UCN converter was minimised.
  A smaller loss in NNBAR FOM if the channel opening was closer to the NNBAR emission surface.
  5 mm thick layer of nanodiamonds that covered the walls of channel increased measured PUCN by approximately 2 %
Notes: Aggiungi international collaboration

## Slide 14: Designing the solid deuterium UCN converter with a channel - initial idea
Conducted a general study – fixed R and varied position of the UCN detector sphere and channel opening
Selected as a reference model for the cylindrical channel option
Maximal acceptable loss in NNBAR FOM
Notes: Aggiungi international collaboration

## Slide 15: Designing the solid deuterium UCN converter with a channel - initial idea
  Selected as a reference model for the cylindrical channel option
    Replaced the spherical UCN converter with a 2 cm thick disc-shaped UCN converter filled with solid deuterium
      Now taking into account the scattering of cold neutrons in the solid deuterium within the UCN converter
        PUCN = 1.10 x 104 n/s/cm3
        NNBAR FOM = 2.41 x 1017 n⋅Å2/s/sr
        V = 0.91 l
        Prompt heatload = 60 W
Notes: Aggiungi international collaboration

## Slide 16: Designing the solid deuterium UCN converter with a channel - initial idea
  Selected as a reference model for the cylindrical channel option
    Replaced the spherical UCN converter with a 2 cm thick disc-shaped UCN converter filled with solid deuterium
      Now taking into account the scattering of cold neutrons in the solid deuterium within the UCN converter
        PUCN = 1.10 x 104 n/s/cm3
        NNBAR FOM = 2.41 x 1017 n⋅Å2/s/sr
        V = 0.91 l
        Prompt heatload = 60 W
Notes: Aggiungi international collaboration

## Slide 17: Designing the UCN converter with a direct view on the NNBAR emission surface
The previous results pointed out the possibility of designing the UCN converter with a direct view on the NNBAR emission surface
  All material was removed below a plane in the twister to accomplish that
Notes: Aggiungi international collaboration

## Slide 18: Designing the UCN converter with a direct view on the NNBAR emission surface
The previous results pointed out the possibility of designing the UCN converter with a direct view on the NNBAR emission surface
  All material was removed below a plane in the twister to accomplish that
Notes: Aggiungi international collaboration

## Slide 19: Designing the UCN converter with a direct view on the NNBAR emission surface
Map of PUCN for both scenarios
Notes: Aggiungi international collaboration

## Slide 20: Designing the UCN converter with a direct view on the NNBAR emission surface
Map of PUCN for both scenarios
About 10 % higher PUCN
Notes: Aggiungi international collaboration

## Slide 21: Designing the UCN converter with a direct view on the NNBAR emission surface
Placed the UCN converter to the green-shaded area in MCB. Can expect PUCN of the order of 104 in this region.
Notes: Aggiungi international collaboration

## Slide 22: Designing the UCN converter with a direct view on the NNBAR emission surface
The UCN converter was filled with solid deuterium and inserted into the Al vessel (0.5 mm thick on the emission surface and 3 mm thick on the other sides)
Thickness of the converter = 13.4 cm
PUCN = 4.51 x 104 n/s/cm3
V = 6.05 l
= 2.72 x 108 n/s
The SD2 UCN converter inside the Al vessel
Notes: Aggiungi international collaboration

## Slide 23: Designing the UCN converter with a direct view on the NNBAR emission surface
The UCN converter was filled with solid deuterium and inserted into the Al vessel (0.5 mm thick on the emission surface and 3 mm thick on the other sides)
Total prompt heatload = 440 W
  Prompt heatload in the converter = 309 W
Total heatload photons = 200 W
Total heatload neutrons = 220 W
The SD2 UCN converter inside the Al vessel
Notes: Aggiungi international collaboration

## Slide 24: Designing the UCN converter with a direct view on the NNBAR emission surface
The UCN converter was filled with solid deuterium and inserted into the Al vessel (0.5 mm thick on the emission surface and 3 mm thick on the other sides)
Thickness of the converter reduced to 2 cm since extraction of UCNs from a thin layer of the converter is possible only
PUCN = 3.81 x 104 n/s/cm3
V = 0.91 l
= 3.44 x 107 n/s
The SD2 UCN converter inside the Al vessel
Notes: Aggiungi international collaboration

## Slide 25: Designing the UCN converter with a direct view on the NNBAR emission surface
Thickness of the converter reduced to 2 cm since extraction of UCNs from a thin layer of the converter is possible only
Total prompt heatload = 150 W
  Prompt heatload in the converter = 74 W
Total heatload photons = 80 W
Total heatload neutrons = 60 W
The SD2 UCN converter inside the Al vessel
Notes: Aggiungi international collaboration

## Slide 26: Designing the UCN converter with a direct view on the NNBAR emission surface
Total prompt heatload (Al vessel + SD2 converter) = 150 W
Calculating additional contribution to heatload due to the beta decay Aluminium 28 in the Al vessel:
  27Al + n → 28Al → 28Si* → 28Si
  The decay heat due to Al 28 beta decay was 9 W
 | Beta particles | Gamma particles
Decay power Al vessel | 9.40 W | 13.5 W
Decay heat Al vessel | 6.61 W | 0.476 W
Decay heat SD2 converter | 1.22 W | 0.139 W
About 70 % (6.61/9.40) of beta particles deposited their energy within the source cell (Al vessel). Most of the gamma particles escaped.
Notes: Aggiungi international collaboration

## Slide 27: Designing the UCN converter with the water reflector
The 1 cm thick layer of water reflector can improve PUCN by about 8 %
1 cm thick water reflector
Notes: Aggiungi international collaboration

## Slide 28: Testing a gamma shielding made of Bismuth
Photon flux
(arbitary units)
Notes: Aggiungi international collaboration

## Slide 29: Testing a gamma shielding made of Bismuth
The polycrystalline bismuth shielding at 77 K was efficient to suppress gammas but also suppressed the spectrum of cold neutrons.
  As a result, a large drop in PUCN can be expected since the cold spectrum of neutrons contributes to the UCN production cross-section.
Notes: Aggiungi international collaboration

## Slide 30: Testing a gamma shielding made of Bismuth
The polycrystalline bismuth shielding at 77 K was efficient to suppress gammas but also suppressed the spectrum of cold neutrons.
  As a result, a large drop in PUCN can be expected since the cold spectrum of neutrons contributes to the UCN production cross-section.
Notes: Aggiungi international collaboration

## Slide 31: Conclusions
An initial study of placing the SD2 UCN converter into the moderator cooling block was conducted
Designing a channel between the LD2 cold moderator and SD2 UCN converter in the moderator cooling block lead to a drop in NNBAR FOM
  PUCN and heatload estimated for a channel with 6 cm radius was 1.1 x 104 [n/s/cm3] and 60 W respectively
The SD2 UCN converter with a direct view on the NNBAR emission surface performed the best w. r. t PUCN and NNBAR FOM
  PUCN and heatload estimated for the 2 cm thick SD2 converter was 3.8 x 104 [n/s/cm3] and 159 W respectively
The polycrystalline bismuth γ shielding is not optimal for SD2 UCN converter but can still be a viable option for superfluid He converter
Notes: Aggiungi international collaboration