## Slide 1: NMX software status update
From events to a structural model
PRESENTED BY Justin Bergmann

## Slide 2: Milestones
  M1 = Spot integration
  M2 = Scaling for multiple detector panels
  M3 = Adaptation to actual NMX data format
  M4 = position uncertainty acceptance criteria
  M5 = Complete Data reduction ready and tested
  M6 = User interface
From now to Hot Comissoning

## Slide 3: From event data to a structural model
  Data readout from detector
  Simulating data to test following steps ✓
  TOA to λ (TOA to λ ✓)
  Spot finding ✓
  Indexing ✓
  Refine indexing ✓
  Spot integration (✓)
  Scaling 🕒
  Merging
  I to SFs
  Phasing
  Model completion
  Refinement
  Map calculation
The data workflow

## Slide 4: Data reduction
Binning of data to Time of flight (TOF) bins ✓
  Avoid reflection overlap
  Flexible adjustment of bin size
  Processing in several seconds or a few minutes (multiple times faster than data collection)
TOA conversion to TOF in scipp and TOF to λ in DIALS (✓)
  https://dials.github.io/projects.html
From event data to image like data

## Slide 5: Datarecduction
From image data to reflexes
Spot finding ✓
  pixel thresholding process followed by the determination of connected regions and size, centre of mass and total intensity estimation
Indexing ✓
  Use orientation matrix is used to assign Miller indices to reciprocal-lattice points
Refine indexing ✓
  Refining one general model of the instrument to use in the following processing
Spot integration (✓)
  peak intensity is evaluated via summation integration or profile fitting

## Slide 6: Scaling (work in progress)
Developing of a replacing python package mainly by Mikael Lund
scaling and normalization of Laue intensity data
yield fully corrected structure amplitudes
Program has to be rewritten to adjust for prosessing several detectors
LSCALE is runing in a Docker container on a modern computer
Pyscale is in development
LSCALE / PySCALE

## Slide 7: Finalysing data reduction
Mergin
  AIMLESS (CCP4) https://www.ccp4.ac.uk/html/aimless.html
  scale refinement, using strong data for an initial scale
I to SFs
  CTRUNCATE (CCP4) https://www.ccp4.ac.uk/html/ctruncate.htm
      Conversion of measured intensities to structure factors
AIMLESS (CCP4)

## Slide 8: Model building and refinement
Phasing
Modelbuilding
  Adding of hydrogen atoms to the model
  Determination of protonation states for acidic and basic side chains
  Hydrogen orientation for water
Refinement
    Phenix
    Refmac5
  Solvent correction
  Restraints and constraints
Validation
From intensities to a model

## Slide 9: Open projects and Concerns
Strategy calculation
User interface
Scaling ready on time
Move of DMSC to DTU
Detachment of DMSC and ESS
Loss of personnel in ECDC and DMSC due to DMSC office move – eventually including NMX IDS

## Slide 10: Questions and sugestions?