## Slide 1: This is a title for a PowerPoint presentation
Optional subtitle
PRESENTED BY <NAME NAMESON>
ESS-ESRF meeting (CATIA KT)
https://indico.esss.lu.se/event/3465/
18 March 2024
ESS Mechanical Engineering Function Dr. Eng. Nick Gazis Leader of Mechanical Engineering (MET), Engineering Analysis (A-team) & Mechanical Measurements Lab (MML)

## Slide 2
Introduction to ESS
1

## Slide 3: ESS buildings handed over end of 2021
Target
Monolith
Klystron Gallery
Exp. Hall
E01
Accelerator Tunnel

## Slide 4: Contributions building ESS
Countries with In-Cash, In-Kind & Observers
Host Countries of Sweden and Denmark
47,5% Construction 15% Operations
In-kind Deliverables ~ 3%
Cash Investment ~ 97%
Non Host Member Countries
52,5% Construction
85% Operations
In-kind Deliverables ~ 70%
Cash Investment ~ 30%

## Slide 5: ESS timeline
2016
Construction work starts on the site
2009
Decision: ESS will be built in Lund
2028
ESS construction completion & SSO start
2003
First European design effort of ESS completed
2012
ESS Design Update phase complete
2025
Machines Ready for Beam on Target
2026
ESS SOUP (Start of User Program)

## Slide 6: ESS design
High Power
Linear Accelerator:
Energy: 2 GeV
Rep. Rate: 14 Hz
Current: 62.5 mA
16 Instruments in Construction budget
Committed to deliver 22 instruments by 2028
Peak flux ~30-100 brighter than the ILL
Target Station:
He-gas cooled rotating
W-target (5MW average
power)
42 beam ports
Ion Source
Total cost: 1843 MEuros 2013

## Slide 7: ESS tunnel views
Then vs now
Parts of Normal
Conducting Linac
Under commissioning
Cryo Distribution Line
Testing underway, followed by
cryomodule installation

## Slide 8: Gallery hall for klystrons & power sources
Then vs now
RF for normal conducting
part installed and tested.
Installation and testing
ongoing in superconducting
part

## Slide 9
Mechanical Design & Engineering
2

## Slide 10: Strategy statement
The Mechanical Engineering Function is responsible to deliver ESS-wide services that lay mainly within the following axes (ESS-1537394):
  Centralization of Mechanical Design & Engineering
  Centralization of Simulations, FEA & Engineering Calculations
  Operate Mechanical Measurements Lab (MML)
  Execute Mechanical Standardization & ISO-GPS Training
  Provide Mechanical Expertise & Reviewing
  Organize the MECH Forum & IKC MECH Forum
for Mechanical Engineering Functional Unit
Cross section of a Spoke Cryomodule

## Slide 11: Mechanical Engineering
Graded Approach implementation:
Most systems need to be built according to design standards with precision & tolerances [so-called ISO-GPS or GD&T rules] to eliminate:
    ambiguity (cause: lack of quality or engineering ways)
    delays (cause: mistakes and known-unknowns)
    additional costs (cause: repairs, reworks, orphan scopes)
Graded Approach
What we work with may not be rocket science but the design comes close in terms of:
engineering complexity
modularity

## Slide 12: Digital Mock-Up
ESS engineering information path
3. CHESS (in-house & IKC input)
Atlassian tool suite
4. Mechanical Design
5. JIRA tasks
6. Released CHESS DWGs
7. Confluence monitoring for Eng. Deliverables
2. Machine Skeleton (Lattice)
1. Requirements (TRM)
Single-point-of-truth in CAD

## Slide 13: High level overview of ESS Accelerator
Target
A2T  DgLg  HEBT
(56 m)
571 MeV
Cryo
Spoke
Medium β
(77 m)
(179 m)
High β
2000 MeV
216 MeV
75 keV
Warm
Source
DTL
MEBT
RFQ
LEBT
(2.4 m)
(4.6 m)
3.6 MeV
(3.8 m)
(39 m)
90 MeV

## Slide 14: ESS target
Key features
Target Safety System
Monitors target coolant flow, pressure & temperature, monolith pressure & target rotation
Rotating solid tungsten target
  36 sectors
  Total mass: 11 tn (3 tn of W)
  Rotatation: 23.3 rpm (synchronized with the pulsed proton beam at 14 Hz)
Helium cooling of target material
Mass flow: 3 kg/s
Pressure: 11 bar
Temperature inlet/outlet: 40°C/240°C
Moderators
Locations of moderators above and beneath of the target wheel, i.e. monolith centre
1st MR plug exploits the upper space, offering:
  Cold, 30 mm high, liquid H2 moderators, 17 K
  Thermal, 30 mm high, H2O moderator, 300 K
Diagnostics and instrumentation
Fluorescent coating of PBW and target front face
Wheel monitoring including position, temperature, vibration, as well as internal structure
Proton Beam Window (PBW)
Proton Beam Instrumentation Plug (PBIP)
Moderator and Reflector
Target wheel
Neutron Beam Extraction Port (NBEX)
Target Monolith Vessel
Target monitoring plug
proton beam
~ 6 m
~ 10 m

## Slide 15: ESS Neutron Instruments
ODIN
DREAM
NMX
MIRACLES
BEER
C-SPEC
T-REX
MAGIC
BIFROST
HEIMDAL
FREIA
LoKI
SKADI
VESPA
ESTIA
Neutron beam extraction
Offers 42 neutron beam ports
Allows neutron science instruments to view either upper or lower moderator position
Small Angle Neutron Scattering (SANS) | LOKI, SKADI
Reflectometry | ESTIA, FREIA
Powder Diffraction | DREAM, HEIMDAL
Single-Crystal Diffraction | MAGIC, NMX
Imaging & Engineering | ODIN, BEER
Direct-Geometry Spectroscopy | CSPEC, T-REX
Indirect-Geometry Spectroscopy | BIFROST, MIRACLES, VESPA
Key features
Proton beam

## Slide 16: Parts & Prototypes Design
Manufacturing, Repairs & Modifications
Beryllium Reflector
Milling of Thermal Moderator
Target baseplate segment
Procedure for securing buckled bellows of Cryo Distribution System –(CDS-SPK) failed auxiliary line

## Slide 17
Thank you