## Slide 2: Report from working group for Bunker access management
TS PSS & Bunker PSS CDR (2024-04-29)
PRESENTED BY Morteza Mansouri

## Slide 3: Bunker Access Management Working Group, assignment
As per Charter - Bunker Access Management Working Group (ESS-4958155), the working group should:
Agree responsibilities for:
  Management of access to the bunker areas
  Configuration control of bunker shielding
  Delivery of required systems and procedures to enable safe access and working in the bunker
Develop access procedures and rules for the Bunker areas in buildings D01 and D03, in alignment with ways of working and rules across ESS for facility safety, security and operation.
Formally document the agreed procedures and rules for access management to the Bunker areas in buildings D01 and D03.
Ensure implementation of the developed rules and procedures.

## Slide 4: Bunker Access Management Working Group, what did we do and how?
Forming the working group including the core stakeholders (PSS, NSS, ESH&S)
Identifying the additional stakeholders (ongoing activity throughout the process)
Identification of requirements by each stakeholder
Assessing solutions for realising the requirements
Define access management procedures to Bunker
Identify and agree on next steps for the stakeholders

## Slide 5: Stakeholders
Stakeholder | Role
ESH&S, occupational health and & safety | provide input and requirements in view of rules for working in confined spaces, fire regulations, and safety trainings
ESH&S, security | provide input and requirements in view of ESS physical protection plans and its legal and regulatory obligations
ICS, PSS | provide input and requirements in view of implementing Personnel Safety System for Bunker, and its integration and consistency with other PSS at ESS
ESH&S, RP | provide input and requirements in view of radiological risks, classification of work areas and categorization of workers with respect to ionizing radiation, implementation of control measures through radwork permits as well as monitoring radiation levels and doses
Rigging | To provide input in view of rigging operation to remove and restore Bunker shielding blocks
Operations | provide input and requirements in view of beam operation and Main Control Room (MCR) role in access management and approval of work orders to areas relevant for beam operation such as Bunker.
NSS | As Bunker designer and developer to provide input in view of feasible solutions and constraints for access to and work at Bunker
Science directorate | As the final user of Bunker to provide input in view of instrument teams work at Bunker

## Slide 6: Requirements
No. | Requirement | Owner
1 | Physical security and access control: As per Categorisation of radioactive materials at ESS (ESS-4755477)[2], the categorization of Bunker with respect to radioactive material is category 4. Neutron Scattering Systems - Radiological Hazards and Radiation Safety Provisions for Operations and Maintenance (ESS-2972939) [3] provides an overview of the radiation sources within Bunker and their respective dose rates and contamination level. A detailed justification on identifying Bunker as category 4 with respect to radioactive material has been discussed in one of the working group meetings too. See the details in Meeting #5 dated 2023-09-04 . As per ESS Plan Physical Protection (ESS-0041572) [4] table 1, Bunker as a category 4 area is considered a Guarded area, and hence implementing Controlled Access (i.e. Verification that only those authorized are given access) is required. | ESH&S, security
2 | Rules for working in Bunker as a Confined Space: As per ESS Rules for Working in Confined spaces (ESS-2071027) [5], a confined space is a place which is substantially enclosed (though not always entirely), and where serious injury can occur from hazardous substances or conditions within the space or nearby (e.g. lack of oxygen). The confined space is usually: with limited openings that are difficult or restricted to enter or exit. not intended for permanent work, but which can be temporarily accessed for maintenance work. with a dangerous atmosphere that may occur due to the presence of certain liquids, substances or chemical residues, but also due to lack of ventilation or due to the work being performed. inadequately lit and/or has poor means of communication. Considering the above criteria, Bunker is a confined space even when the whole roof is removed. Note: In line with Procedure for Work Order Management (ESS-1949392) [6], everyone working in Bunker shall have approved work order with applicable permits. | ESH&S, OHS
3 | Fire safety: As per fire safety regulations, the maximum number of individuals inside the Bunker shall be 10. This is for each Bunker, North-West Bunker in D03 or South-East Bunker in D01. The limit is set by the OHS representative in the working group. Reference document is TBD. | ESH&S, OHS
4 | Search the in-Bunker areas: Similar to other areas with prompt ionizing radiation hazard, e.g. the accelerator tunnel, it must be ensured that no one is left inside the Bunker before restoring the Bunker roof shielding and start of beam operation. See Concepts of Operations for ESS Personnel Safety Systems (ESS-2595616) [7] for further details. | ICS, PSS

## Slide 7: Requirements
No. | Requirement | Owner
5 | Mitigate prompt ionizing radiation hazards: As per Conventional and Radiological Hazard Analysis and Risk Assessment of NSS Bunker Area (ESS-3999144) [8], the sources of the prompt ionizing radiation hazards in Bunker is proton beam to Target operation. Prior to accessing the Bunker, the prompt ionizing radiation hazards shall be mitigated. Also as per [8], prior to accessing the Bunker the gamma radiation hazards from the Target monolith shall be mitigated by closing the light shutter system (LSS). | ICS, PSS
6 | Prevent Access to Bunker: Access to the Bunker (both Bunker roof and In Bunker areas) shall be prevented when prompt ionizing radiation hazard is present, i.e. during proton beam on Target operation or when gamma radiation hazard from monolith is present i.e. during LSS is open. The requirement to prevent access to Bunker roof during BoT is derived from AA NSS11W - Accident Analysis Report - Worker: Unauthorised Human Presence in the Bunker (ESS-2135635) [10] | NSS
7 | Dosimetry: As per [3], the Radiation Protection (RP) area classification for Bunker is as below: Bunker roof during operation: Blue radiation controlled area In-Bunker areas during maintenance: Partly Blue radiation controlled area, and partly yellow radiation controlled area As per ESS Handbook for Radiation Protection Chapter 2. General Radiation Protection Rules (ESS-0239718) [9], all workers in controlled areas shall wear active personal dosimeter. Hence, Electronic Personal Dosimeter (EPD) is required for access to the roof and inside the bunker. | ESH&S, RP
8 | Bunker access zone and training: Bunker is located within the experimental halls. However, the training and authorization requirements for access to Bunker are different from experimental halls. Hence, Bunker shall be an independent access zone from the experimental halls in the access management system (Access Portal), with a designated list of trainings, such as working in Confined space training, Radiation protection awareness, radiation controlled areas, etc. in the learning management system. | ESH&S, RP ESH&S, OHS

## Slide 8: Next steps
No. | Action | Responsible
1 | Design, manufacture and install the staircases to the Bunker, access doors and fences at the Bunker perimeters as per the prescription of this report. | NSS
2 | Prepare new revision for the Conventional and Radiological Hazard Analysis and Risk Assessment of NSS Bunker Area considering the procedures defined in this report | NSS
3 | Design, procure, install and commission the physical access control systems (card readers, cables, etc.) at the access doors to the Bunker. PSS and PACS works on details of interfaces and location of the card readers | OID, Site and building maintenance ICS, PSS
4 | Design, procure, install and commission the required intercom units, security cameras, Operation cameras and the related infrastructure at the Bunker access doors. | OID, Site and building maintenance ICS, PSS
5 | Perform a detailed analysis, e.g. event tree analysis, of the access management procedures for Bunker in view of their sufficiency and efficiency in mitigating the hazards at Bunker. | ICS PSS, with support from the rest of the stakeholders
6 | Organize an independent review of the access management procedures for Bunker | ICS PSS, with support from the rest of the stakeholders
7 | Identify the list of trainings required for accessing the Bunker | ESH&S

## Slide 9: Thank you Questions/comments?

## Slide 10: Back-up slides

## Slide 11: Finish presentation