## Slide 1: IBEX - the new Instrument Control System at the ISIS Pulsed Neutron and Muon Source
Freddie Akeroyd
ISIS Computing Group STFC ISIS Facility, GB

## Slide 2: ISIS Facility
Pulsed neutron and muon source
~30 experiment beamlines
World leading materials research facility
Every year over:
1000 proposals
700 experiments
400 publications

## Slide 3: New Control System?
Old/existing system (SECI) based on LabVIEW:
  C# manager GUI
  Performed well, remains good for most instruments
However concerns for future instruments:
  Performance
  Scalability
  Maintainability
After evaluation exercise, develop new system based on EPICS framework

## Slide 4: EPICS on one slide
Device
Publish Process Variables (PVs)
IN:LARMOR:DAE:MON:5:C
IN:LARMOR:MOT:STACK:THETA:SP
C++
Python
Java
C#
LabVIEW
…
IOC
IOC
IOC
IOC
Channel Access (CA)
Device
Device
Device
Subscribe to Process Variables (PVs)
IN:LARMOR:MOT:STACK:THETA:SP
Notes: EPICS is a software framework for building control systems
  EPICS = Experimental Physics and Industrial Control System
  Widely used: SNS, ESS, Diamond, ITER, APS @ ANL, NSLS-II @ Brookhaven, PSI, SLAC, Fermilab, DESY, Keck Telescope, Gemini Telescope, …
EPICS uses a publish-subscribe paradigm
  In this slide the boxes are processes (it says nothing about where those processes are running)
  Processes can publish information about their state – as process variables (PVs)
  Other processes can request information about a process’s state – subscribe to PVs
  A subscriber can also request that a publisher change its state – e.g. change a set-point
  A process can be both a publisher and a subscriber
  EPICS processes communicate using a protocol called Channel Access (CA)
  CA sits on top of TCP/IP
  EPICS processes are very loosely-coupled
    Publishers don’t care how (or where) their subscribers are implemented (and vice-versa)
    Provides a very flexible architectural framework
IOCs are EPICS processes used to control hardware devices
  IOC = Input/Output Controller
  IOCs communicate with the hardware via device drivers
  IOC publishes PVs which describe the state of the device
  Subscribing processes can ask the IOC to change the state of the device
  Output from one IOC can be used as input to another

## Slide 5: IBEX Technologies
EPICS framework
  also used at Diamond, SNS ORNL and ESS
Eclipse / RCP for the main IBEX GUI
  can use components from CS Studio
Python for scripting
Continue to use MS Windows:
  For compatibility with existing business systems
  Allows install alongside old SECI system
  However IBEX can run on Linux too

## Slide 6: IBEX System Components
Blocks Gateway (aliases)
Blockserver (configurations)
Blocks Archiver
Instrument Archiver
IOC
IOC
NeXus Data Files
MySQL
Neutron Acquisition Program (with EPICS interface)
IOC
Sample Environment
Alarm Server
Message Logger
ActiveMQ
EPICS External Gateway (access control)
Run Control
IBEX Client (GUI)
IBEX Client (Python Script)
IBEX Client (Web Dashboard)
Notes: IBEX is built using EPICS
  IBEX has a distributed, client-server architecture based on the EPICS publish-subscribe paradigm
  IBEX server runs on the NDXxxxxxx machine
  IBEX client can run on any machine connected to the ISIS network
    On the NDXxxxxxx server itself, on a PC in the instrument cabin, on your office PC, on your home PC
IBEX Server is not a single executable
  It is a collection of individual control components called IOCs (Input/Output Controllers), plus loggers/archivers
  IOCs are analogous to VIs in LabVIEW
  Each IOC communicates with one type of device (Galils, Choppers, Eurotherms, CAENs, DAE, etc.)
    Some IOCs can manage several devices of the same type: e.g. the Galil IOC can manage several Galil crates
  EPICS manages the communication between individual IOCs and between IOCs and any client applications
IBEX clients running on the instrument sub-net have read-write access to the IBEX server
  Instrument sub-net = instrument blockhouse + instrument server room + instrument cabin
IBEX clients running elsewhere have read-only access to the IBEX server
The EPICS Gateway determines whether a client has read-write or read-only access
You can run the IBEX client on the NDXxxxxxx server itself
You can point any IBEX client at any IBEX server on any NDXxxxxxx machine

## Slide 7: IBEX Client GUI
Notes: The IBEX Client is the primary means of interaction with the IBEX server
  It is the primary GUI for IBEX
This screenshot shows a typical view. We’ll illustrate the main components one by one.

## Slide 8: Key IBEX Features
GUI uses SWT widgets & CS Studio BOY OPIs
Synoptic view, editor and drill down
  Drill down is to BOY OPIs
  Can define multiple synoptic views
Dashboard summary view
Blocks (user requested key information)
  Block values copied into NeXus (HDF5) data file
  Data collection suspended if block out of range
  (Other PVs logged to diagnostic archive)

## Slide 9: Key IBEX Features (cont.)
Configurations and components
  Which IOCs to start, macros to set etc.
Alarm view (BEAST)
“Table of motors” view
IOC log messages view
Python user scripting window
Instrument selector
  client can view another instrument

## Slide 10: IBEX Client: Table of Motors View
Notes: Table of Motors View
  A quick way to see status of all motors
  Each row is a single Galil motor controller (crate) - up to 8 ports
  As many rows as there are motor controllers
  Pink: motor is stationary; Green: motor is in motion; Grey: motor is not present
  Icons show if motor is homed, in motion or at a limit.
  Drill-down (double-click) to see and change detailed settings of any motor

## Slide 11: IBEX Client: Adding Blocks

## Slide 12: IBEX Client: Block History
Notes: You can view the history of any Block (or PV for that matter)
  Right click on the block and select from the drop-down menu
  This example shows 3 sample temperatures being monitored by a Eurotherm (on LARMOR)
  You can display as many Blocks (or PVs) on a trace as required
  You can change the scale, zoom in, zoom out, you can change the colour of the traces, etc.
  You can export the trace as a tab-delimited file or a Matlab file
  You can save the image as a PNG file

## Slide 13: IBEX Client: Synoptic Editor

## Slide 14: Configurations
Detail appropriate drivers and settings
  Which IOCs to start
    Plus macros, and additional PV values to set
  “Blocks” and “block groups”
    Aliases for relevant experiment PVs
    Also logging, run control limits
  A default synoptic view
Stored as XML files in folders on disk
  Managed and served by “blockserver” process
  Versioned in git

## Slide 15: Components
A configuration can include “components”
  These are like mini-configurations
An instrument’s equipment is composed of:
  Fixed beamline devices (e.g. choppers, slits)
  Variable experiment devices (e.g. cryostat)
A particular configuration would contain:
  A base fixed devices component
  Additional movable equipment components

## Slide 16: Current IBEX Status
Fully deployed to three instruments so far
  2 new, 1 existing
IBEX parts used for Muon Front-end upgrade
  Highlights IBEX benefits more widely
  Lightweight LabVIEW (CA Lab) interface in SECI
Planning upgrade of remaining 27 instruments
  This will take several years!
Working on script server interface
  Using NICOS (FRM-II) to manage scripts

## Slide 17: Acknowledgements
Many people have contributed to IBEX:
  Freddie Akeroyd, Kathryn Baker, Matt Clarke, Simon Fernandez, Lottie Greenwood, Jack Harper, Michael Hart, Gareth Howells, David Keymer, Thomas Lohnert, Chris Moreton-Smith, Dominic Oram (STFC), Martin Bell, Ian Bush, John Holt, Robert Nelson, Adrian Potter, Isabella Rey, Kris Ward, Kevin Woods (Tessella)
Code hosted at: https://github.com/ISISComputingGroup