## Slide 1: Base 3.15 LSB
Lesser Significant Bits in the “current” version of Base

## Slide 2: Assemblies
Old: Manual st.cmd management
  Hard to do for many IOCs
  Using include files creates a debugging nightmare
New: Create text files from numbered snippets
  Number in file name (phase) determines order
  Snippets can add to or replace a phase
  Can use global and local directories (packages may install snippets in global dirs)

## Slide 3: Property events
Old situation: no monitors on metadata
  GUI has to “reopen window” to update limits etc.
New situation: DBE_PROPERTY event type sends updates on metadata changes
  Record type declares fields as properties of the VAL
  Client subscribes to the VAL using DBR_CTRL_* and DBE_PROPERTY event flag
  IOC sends updates when a property (limit etc.) changes
  Fully supported by the CA Gateway

## Slide 4: Pointer Swapping for Arrays
Old way: copy data into a waveform
{ epicsMutexMustLock(CirBufMutex[card][signal]); memcpy((unsigned char *) prec->bptr, (unsigned char *) m_rBuf[card][signal], (size_t)samples * sizeof(float)); epicsMutexUnlock(CirBufMutex[card][signal]); }
New way: swap the pointer
{ epicsMutexMustLock(priv->lock); if (prec->bptr) free (prec->bptr); prec->bptr = priv->nextBuffer; /* no memcpy! */ priv->nextBuffer = NULL; epicsMutexUnlock(priv-lock); }

## Slide 5: IOCs can bind to single NIF
Old IOCs running on hosts with multiple network interfaces were always binding to all
  Creating “duplicate PV” exceptions in clients
  Causing beacon traffic on unwanted networks
New IOCs can configure to bind to a subset
  EPICS_CAS_INTF_ADDR_LIST=192.168.1.23
  Binding to multiple NIFs supported

## Slide 6: Sub-Arrays on the Fly
Old IOCs need a subArrayRecord to extract a partial array
New IOCs support this operation on the fly
  “caget wf.VAL[20:25]”
  Client does not need to be 3.15
  Works only for gets and monitors

## Slide 7: Summary
Assemblies: create files from snippets
Property events: get updated on metadata
Pointer swap: zero-copy array device support
Selective IOC binding: keep other nets clean
Sub-Arrays on the fly: no subArrayRec needed
More things to find in the release notes:
  Multicast name resolution
  Drivers can directly process records
  Multiple parallel callback threads on multi-core CPUs