## Slide 1
Strategy of Instrument Shield at Spallation Source
- experiences at J-PARC –
Masatoshi Arai
Technical Coordinator
(ARIA 2017 May)
Neutron Beam-Line and Shield Design
for Neutron Scattering Instruments
at JSNS J-PARC Project
(ICANS - XVII 2005)
Niita et al.
A New Method for Neutron-Beam-Line Shielding Calculation
(ICANS-XVI 2003)
Maekawa et al.

## Slide 2
Public area
In-site
0.25μSv/h
In-site
50 GeV synchrotron
3 GeV synchrotron
400 MeV
Linac
Hadron Facility
Materials & Life Science
Facility (neutron & muon)
12.5μSv/h
Neutrino Facility
J-PARC (1MW+0.75MW) and its location
- close to public area -
Power Reactor
TOKAI-2
Site boundary
50 μ Sv/y

## Slide 3
Design Criteria
(Japanese Regulation; Public; 1mSv/y , RAD worker 50mSv/y)
Controlled Area :12.5 μSv/h (1/2 of 1 mSv/week)
(Regulation: 25 μSv/h, 50mSv/y)
In-site between 1) and 3) :0.25 μSv/h (1/2 of 1 mSv/year)
Site boundary Radiation : 50 μSv/y (1/20 of 1 mSv/year)
(Regulation: 1 mSv/year)
Operation time
Staff Working hour : 2000 h/year
400-MeV Linac, 3-GeV Synchrotron : 5500 h/year
50-GeV Synchrotron : 5000 h/year
Materials and Life Science Exp. Facility (1MW) : 5000 h/year
Nuclear and Particle Exp. Facility (0.75MW) : 4000 h/year
Radiation Protection Design Scheme at J-PARC

## Slide 4: Method (1)
Very high energy spectrum both in N and P, not existing in reactor.
Tight coupling between Target and Moderator enhance harder spectrum
Energy Spectrum of Neutron and Photon at sns
Neutron spectra from moderator
Photon spectra from moderator
reactor
π0 decay
Those high energy particles create other neutrons.

## Slide 5
Straight guide
Curved guide
Guide line of Dose at side surface
Initially before the construction in 2005
6.25 μSv/h ( = 25(reg)/2(sim)/2(design) )
After operation in 2014
12.5 μSv/h ( = 25/2(simul) )
2) Cumulated Dose at top surface
100 μSv/h/instrument to keep Skyshine
3) Actual observed Dose ~ μSv/h at 300kW
How to keep dose low and extract useful neutrons

## Slide 6
Development of Duct Source Concept
To make it easier for long path calculation
ICANS XVI, 2003
F. Maekawa et al.
Treat separately direct current and
duct scattered term (wall load) by generating source for the second step
Direct current
Scattering term
Generate neutrons
for the 2nd step

## Slide 7
SHRPD (100m) Beam Line simulation
Curved guide (R=5000m)
Straight guide (B2O3 Glass)
Only 10cm Fe is good enough after the curved section.
End of the curved section (Line of sight)
void
Void 60cm
Bunker up to 12m
1mSv/h
< 0.1mSv/h
1mSv/h
Long instrument;
1) Get rid of high-E neutron at curved section as much as possible
2) Then needs only light shield at downstream straight section
Monolith up to 8m
moderator
Sample position

## Slide 8
Typical Shield structure for 1μSv/h for 1MW
20
20
30
10-15
10-15
10-15 cm
30-45cm
At straight section (0.5t/m2)
( 3t/m2 including Concrete Base)
270-290 cm
300
200
20
20-30
100 cm
100 cm
70-90
20
20
20
Concrete
Steel
At Curved section (10t/m2)

## Slide 9
Beam Line shield in the main hall in 2007.
BL03
BL08
3m
Monolith
Bunker

## Slide 10
J-PARC SHPRD (BL08, 100m) in the straight section
Guide shield (Fe 10cm thick)
Light handy crane
Guide
Main building wall
And beginning of corridor
View from up-strm to down-strm.
BL08

## Slide 11
1MeV
1keV
100MeV
1eV
Macro-Xsection of Steel and Concrete (CR) (1/cm) (coarse view)
0,01
0,0001
0,00001
X-section gap in Fe at ~ 10keV
Needs CR compensation
6% in CR
60% in CR
1) At around 10keV neutron can easily penetrate Fe.
2) H in CR reduces energy of neutron.
3) Low-E neutron can be easily shielded by CR and captured by H and emitt 2MeV gamma.
Basic Concept of Value Engineering shielding
Macro X-section 2(Steel) : 1(CR) ;
Material Price; 20 (Steel) : 1(CR);
λFe=19cm
λCR=43cm
Steel
Concrete

## Slide 12: Shielding Design (1)
Fe
5 ton/m
Fe
45 ton/m
Shielding Design Optimization (Value Engineering)
Brute force design
ample money
and space
Value engineering design (study scattering and cross-section)
limited budget
need space saving
huge effort to optimize it
as reasonably inexpensive as possible
Can save cost with keeping Dose
easy design with a large margin
without a hard optimization
snowball increase (cost, floor load, crane)
1500cm

## Slide 13
Magnetite concrete
Shutter
Bunker
Sample
Monolith
Strategy of BL shield and allowance of hot spot
Keep dose <6.25 at side surface
Cumulative dose at top surface <100 μSv/h/instrument
Allow hot spot, where access is limited
Beam stop

## Slide 14
Summary:
J-PARC developed reasonable strategy for RAD safety for a user facility.
We developed simulation code suitable for calculating long instrument.
Optimization of beam line shield as well as optical design was reasonably done, resulting value engineering with keeping Dose rate low and background low.
Actual observation assessed the design strategy and found that the factor 2.0 was over estimate. (safety margin for design)

## Slide 15
I=Io exp(-μaa-μbb-μcc)
γ-ray
Neutron (un commutative): different order resulting big difference
E
Ei
Ea
Eb
Ec
Ef
I=Io exp(-μcc-μbb-μaa)
a
b
c
a
b
c
a
b
c
a
b
c
Ec
Eb
Ea
Ef’
Ei
Neutron scattering process drastically changes the energy;
Energy dependent cross section drastically changes the transport process.
Basic concept for neutron shield

## Slide 16
Public area;
1. Permanently occupied area 25 nSv/h
2. Not Permanently occupied area 0.5 μSv/h
-> outside experimental building (in-site) ? But this is inconsistent with 3.
3. Non-exposed workers 25nSv/h (2000h/y)
Supervised area;
1. normal operation 3 μSv/h
3. Temporary hotspot shall not exceed 3 μSV integrated dose over one-hour.
-> it may allow hotspot by having a fence etc.
The ESS implementation;
RAD sircumstances around ESS

## Slide 17
Event | Description | Radiation workers | Non-exposed workers | Public
H1 | Normal Operation | 10 mSv/y | 0.05 mSv/y | 0.05 mSv effective dose/y
H2 | Anticipated events | 20 mSv/event | 0.1 mSv/event | 0.1 mSv effective dose/occurrence
H3 | Unanticipated events | 50 mSv/event | 1 mSv/event | 1 mSv effective dose/occurrence
H4A | Improbable events | 50 mSv/event | 20 mSv/event | 20 mSv effective dose/occurrence
H4B | Events with multiple failures | 50 mSv/event | 20 mSv/event | 20 mSv effective dose/occurrence
H5 | Highly improbable events | Not defined. | 100 mSv/event | 100 mSv effective dose/occurrence
General Safety Objective (GOS) ESS-000004 in Sep. 11 2013
5000 hour operation
50μSv/y -> 10nSv/h
Implementation: ESS-00001876 in Jan 2013
public areas are subdivided (Zoning by fence) into areas that are permanently occupied and areas that are not permanently occupied.
Public Area:
none permanently occupied (on site) < 0.5 μSv/h
permanently occupied (out site) < 25 nSv/h.
Dose rate Guideline at ESS
2000 hour working
50μSv/y -> 25nSv/h

## Slide 18
1) λ(ΕC)=640m for 3GeV
2) major escaped neutron energy ~ 1MeV
3) dose rate of 1.0 μSv/h at the source area A of 100x100m2
Skyshine estimation
It is about ~100 nSv/h on the site at 30m from the source center and ~ 10 nSv/h at about 150m,

## Slide 19
Expected dose at “y” is
h=h0 ln((L/y)2+1)
y
x
r
Δx
P
AC
S
2L
If, L=5m, 3μSv/h at 1m at the instrument
(2L is size of the shield; typically 10m)
y = 160m for 10nSv/h
y = 32m for 25nSv/h
Direct Dose from Instruments
Instrument Shield
Instrument shield is designed to be < 3μSv/h

## Slide 20
ODIN
DREAM
NMX
MIRACLES
BEER
C-SPEC
T-REX
MAGIC
BIFROST
HEIMDAL
FREIA
LoKI
SKADI
VESPA
ESTIA
VOR
50 m
100 m
150 m
HR-NSE
D01
D02
D03
E02
E01
E03
E04
D08
D07
D04
MA 2017 Mar 22
125 nSv/h at 30m
(100(Sky)+25(inst))
20 nSv/h at 150m
(10(Sky)+10(Inst))
Some concern about RAD level on site around experimental hall
1) Non-exposed workers may not be able to stay here (25 nSv/h).
2) Office building cannot be built here.

## Slide 21
Backup

## Slide 22
Rg
L*
d
Neutron
d
d
d
3
2
1
l1=2d1sinq
l2=2d2sinq
l3=2d3sinq
q
1.0
Q1=4psinq/l1
Q2=4psinq/l2
Q3=4psinq/l3
Ni-Ti multilayer
500- 5000 layers
~ 0.01μm ~ 0.1μm/layer
Line of sight
Series of Bragg reflections by various layer thickness
Curved Supermirror Guide
; Transfer low E neutron

## Slide 23
BL01 4SEASONS
Magnetite concrete
shutter region
Bunker
2.5m
5m
7.5m
12m
Chopper room
Beam stop
Monolith
BL shield and hot spot at the sample position
Cumurative dose 100 μSv/h/instrument

## Slide 24
High Energy neutron elimination either by a To chopper or a curved guide (CG)
(example for 40m instrument (LOS: 28m))
To and Curved Guide (CG) are not perfect to get rid of high energy neutrons.
Flux at moderator (2m)
flux at sample w/o SMG (40m; 1/L2)
CG reduces high energy neutrons 1/100,000.
To and CG has similar effects except for MeV range.
Keep in mind that To and CG are not perfect to take rid of high energy neutrons.
At sample position (40m)
1/100000
1/L2=1/400
500
SMG
To
10-7

## Slide 25
1mSv/h
Numerical model for PHITS
bunker shield
To chopper
BL11
Effect of gate shield (collimator block) for straight BL
Bunker
No To chopper
Monolith
Beam stop
DNA
Example of Gate Shield
AMATERAS
NS=10-5
DNA: back scattering instrument, ΔE~3μeV

## Slide 26
Common open section in bunker for narrowly separated beam lines, 6.7deg. Otherwise each beam line is separated each other by a steel barrier/wall not to have cross talks.
BL20
BL19
BL18
barrier
Barrier to BL21
barrier
Cross Talk in Bunker common space
Gate shield
6.7o
6.7
6.7o

## Slide 27
BL11
Cross Talk (it comes out at latter time)
Cross Talk from BL11
Only one BL11 shutter is opened.
BL11 has cross talk because of the open space in bunker.
BL11
BL10

## Slide 28
CSPEC
NMX
MIRACLES
ESS instruments in E02
z, mm
m=2.5
m=4 to 2.5
m=2.5 to 5
BEER

## Slide 29
MAGIC
HEIMEDAL
TREX
The MC position can be readjusted to 80m

## Slide 30
10x10m
1m-width
3m-width
NMX
BEER
CSPEC
BIFROST
MIRACLES
MAGIC
TREX
HEIMEDAL
Middle Chopper
Position (MC)
E03
E02
A
A
5t/m2
14t/m2
20t/m2
D03
30t/m2

## Slide 31: We have confirmed the designed performances in the real beam
Result at J-PARC
(FL=100m)
(world record)
Lattice spacing
Bragg Diffraction from
Si crystal
Dd/d~0.035%
Obtained at
KEK KENS
(FL=40m)
High resolution
Dd/d ~ 0.03%
Resolution at BL08 (June, 2008)
PHITS: precision (±20%)
Energy in109 ⇒ 10-3eV order of 12
Intensity 1017⇒108 order of 9
Neutron Spectrum
Peak structure (calc/obs)
ピーク構造（計算／実測）
2 meV
25 meV
Notes: 31

## Slide 32
500meV
125meV
To chopper suppresses high energy background
High Speed To-Chopper 100Hz
Developed by KEK (S.Itoh)
500mm
Compact To-Chopper 25/50Hz
Developed by KOBELCO
R. Kajimoto et al., J. Phys. Soc. Jpn. 80 (2011) SB025
2.0 eV
0.5 eV
0.125 eV
High energy neutrons enter into instrument are thermalized by surroundings, come out at later time and makes a high back ground.
Fermi Chopper transmission
To closing at 25Hz

## Slide 33
Beam Line Shield Dose in distance

## Slide 35
50μSv/y at public area
Reported by Nakashima in ICRS 2004
Simulation by assuming beam loss in accelerator and target stations

## Slide 36
What is J-PARC MLF
Shielding Design for instrument
It is not just shield source radiation,
But we lead most of radiation to the instrument.
Neutronics for long instrument
Schield as much cost effective under keeping safety.
Sample (powder and liquid)
Hall level and hotspot
Outside building and public
Intermediate region between the controlled area and public area
Skyshine
Actual dose is lower than calc.