## Slide 1: Study of the collimators for curved beamline at ESS
V. Santoro D. Di Julio, P. Bentley,
S. Ansell, G. Muhrer
ESS

## Slide 2: The ESS instrument suite

## Slide 3
The ESS bunker (I)
The ESS bunker is a common shielding structure, which extends from the outer surface of the monolith, located at 5.5m from the target, to 15 m for the short instrument sector and to 28m in the long instrument sectors
The Bunker is filled of components, metallic guides, chopper, shutter collimators.
We would like to have
access to the inside of the
bunker during maintenance
in steady operation

## Slide 4
The ESS bunker (II)
Proton Beam
Bunker
Bunker
Bunker Wall
Bunker Wall
Target

## Slide 5
Straight and curved instrument
Sample position
Source
Source
Sample position
High Energy Neutrons
Cold / thermal Neutrons

## Slide 6: The NMX instrument
The NMX instrument is a time-of-flight (TOF) quasi-Laue diffractometer optimised for small samples and large unit cells.
NMX is dedicated to the structure determination of biological macromolecules by crystallography.
The scientific driver is to locate the hydrogen atoms
Where are the hydrogen important?
Enzyme Mechanism
Protein-ligand interactions
Proton transport across membranes

## Slide 7: NMX Original Design

## Slide 8
ESS MCNP model
Engineering Model
MCNP Model
MCNP Model for target +Bunker+instrument hall +instrument cave
produced with Comblayer package developed by Stuart Ansell
https://github.com/SAnsell/CombLayer
NORTH
WEST
SOUTH
EAST

## Slide 9
GEOMETRY of the NMX Beamline (1)
Bunker Wall
NMX (W1)
Short sector
Long sector
Long sector
Short sector
4th International Workshop on Accelerator Radiation Induced Activation

## Slide 10
Guide in the Monolith
Width 4.5 cm (@2m) 3.5 cm @ 5.5 m
Height 4.5 cm (@2m) 4.5 cm @ 5.5 m
Copper Substrate
Guide in the Bunker
Width 4.5 cm (@6 m) Height 3.0 cm (@ 6 m)
Aluminum Substrate
The guide bends with 1.2km radius of curvature
Moderator
GEOMETRY of the NMX Beamline (2)

## Slide 11
Out of the bunker wall ~ 28m from the moderator
Moderator
GEOMETRY of the NMX Beamline (3)
What we are trying to achieve:
after the bunker wall the fast neutron background will be almost negligible and the beam will be composed only by thermal and cold neutrons

## Slide 12
Source term @ 2m position (1)

## Slide 13
Source term @ 2m position (2)
Zoom of the BeamLine in in the target region
Monolith
Moderator
Beam Line
Proton Beam
2m from the moderator entrance of the beam line

## Slide 14: 50 cm W collimator around 16m
50 cm W or Cu collimators at 16m and 24m
50cm Cu/W around 16m
50cm W/Cu ~ 24m
Guide Substrate
Bunker Wall
Monolith

## Slide 15
DOSE MAP for NMX before the bunker wall without collimator
mSv/h
Before the Bunker wall x=2419, y -29.6 z=13.93
Main Beam
somewhere here

## Slide 16
mSv/h
Before the Bunker wall x=2419, y -29.6 z=13.93
DOSE MAP for NMX before the bunker wall with a W collimator
Main Beam
somewhere here

## Slide 17
mSv/h
Before the Bunker wall x=2419, y -29.6 z=13.93
DOSE MAP for NMX before the bunker wall with 2 W collimators
Main Beam
somewhere here

## Slide 18
mSv/h
Collimators in the bunker(I)
Second collimator
First collimator

## Slide 19
Out of the bunker wall ~ 28m from the moderator
Moderator
Position of the first collimator
Collimators in the bunker(II)

## Slide 20
Neutron energy spectrum in the collimator for different materials

## Slide 21
Neutron Energy Spectrum Out Bunker (28m)

## Slide 22
W and Copper Collimator Activation
1000 mSv/h
Tungsten
After 10 years of operation
Copper
400 mSv/h
mSv/h
1 day of cool –down

## Slide 23
Steel Collimator Activation
After 10 years of operation
Mild Steel
250 mSv/h
mSv/h
1 day of cool –down

## Slide 24
W and Copper Collimator Activation
26 mSv/h
Tungsten
After 10 years of operation
Copper
60 mSv/h
mSv/h
7 days of cool –down

## Slide 25
Steel Collimator Activation
After 10 years of operation
Mild Steel
240 mSv/h
mSv/h
7 days of cool –down

## Slide 26
Conclusions
We have performed neutronic calculation of the NMX instrument at ESS
W or Cu Collimators significantly decrease the dose outiside the bunker (very low high energy component)
W or Cu collimators are a better choice than steel collimators due to the activation considerations

## Slide 27
BACK-UP SLIDES

## Slide 28
Comparison between Straight and curved guide

## Slide 29
Comparison of the neutron energy spectrum at 5.5 starting from proton and from neutron source at 2m

## Slide 30: Slice of the beam line at 6m
Neutron Flux
n/cm2s
Guide
Neutrons Energy > 0.1 keV

## Slide 31: Slice of the beam line at 12m
Neutron Flux
n/cm2s
Guide
Neutrons Energy > 0.1 keV

## Slide 32: Slice of the beam line at 18m
Neutron Flux
n/cm2s
Guide
Neutrons Energy > 0.1 keV

## Slide 33: Slice of the beam line at 2399 m
Neutron Flux
n/cm2s
Guide
Neutrons Energy > 0.1 keV
Main Beam
somewhere here

## Slide 34: NMX in the Bunker
SHORT INSTRUMENT SECTOR
LONG INSTRUMENT SECTOR
24.5 m
W1
3.5 m
NMX
11.5 m
NMX Original Design
Proton Beam
NMX
CAD view

## Slide 35: NMX in the Bunker: 2m from the Moderator
W1
Neutron Energy Spectrum
2m from the moderator
NMX Original Design
1 eV

## Slide 36: NMX in the Bunker: 6m from the moderator
W1
Neutron Energy Spectrum
6m from the moderator
NMX Original Design

## Slide 37: NMX in the Bunker: 12m from the moderator
W1
Neutron Energy Spectrum
12m from the moderator
NMX Original Design

## Slide 38: NMX in the Bunker: 18m from the moderator
W1
Neutron Energy Spectrum
18m from the moderator
NMX Original Design

## Slide 39: NMX in the Bunker: 24m from the moderator
W1
Neutron Energy Spectrum
24m from the moderator
NMX Original Design

## Slide 40: NMX Energy Spectra
MCNP entries/divided by Bin Width
NMX Original Design