## Slide 1: Measurements and FLUKA Simulations of Bismuth, Aluminum and Indium Activation at the upgraded CERN Shielding Benchmark Facility(CSBF)
ARIA 17, 22/05/2017
E. Iliopoulou, P. Bamidis, M. Brugger, R. Froeschl, A. Infantino, T. Kajimoto, N. Nakao,
S. Roesler, T. Sanami, A. Siountas, H. Yashima

## Slide 2: Outline
CHARM (CERN High energy AcceleRator Mixed field facility)
CSBF (CERN Shielding Benchmark Facility)
Activation benchmark campaign in September 2016
FLUKA simulations
Sensitivity studies
Results
Conclusions

## Slide 3: CHARM - Location

## Slide 4: CHARM - Layout
Target
Target alcove
Movable shielding
walls
Beam line

## Slide 5: CHARM
Purpose
  Study radiation effects on electronic components (R2E project)
Beam characteristics
  Primary protons from the PS
  24 GeV/c momentum
  5 x 1011 protons/pulse
  350ms pulse length
  max. average beam intensity 6.6 x 1010 p/s

## Slide 6: CSBF (CERN Shielding Benchmark Facility)
Combined facility EN/EA, R2E and RP
Major upgrade for 2016 run
Purpose
  Characterization of the shielding properties of various materials
  Deep shielding penetration studies
    Detector calibration
    Detector inter-comparison
    Activation
Situated laterally above the CHARM target
  One week dedicated beam time per year
  Otherwise, parasitic use of the radiation field emerging from the CHARM target
Complementary to the CERF facility

## Slide 7: CSBF – Layout 2016

## Slide 8: CSBF – Layout 2016

## Slide 9: CSBF – Layout 2016

## Slide 10: CSBF - Location

## Slide 11: Activation benchmark campaign in September 2016
Bismuth, aluminum & indium samples
  14 disk samples
  Different heights in removable sample concrete block
Copper target
Specific production yield comparison
  FLUKA simulations
  Measured activity Production yield

## Slide 12: FLUKA simulations
Protons with 24GeV/c on Cu target
  12mm x 12mm FWHM
Region importance biasing
Usrtrack – scoring for neutron fluence
  Weighting with a set of cross sections of Bi(n,xn)Bi, 27Al(n,a)24Na and 115In(n,n’)115mIn
Correct geometry description
  Scoring volumes

## Slide 13: FLUKA simulations

## Slide 14: Sensitivity studies
 | Type of uncertainty | Uncertainty ( %)
Simulations | Statistical Concrete density | 2 - 6 0.5 - 10
Measurements | γ-spectrometry sample weight beam intensity beam momentum beam position and profile target density target dimensions | 1.3 - 12 1 7 < 1 < 1 <1 <1

## Slide 15: Samples

## Slide 16: Sample placement

## Slide 17: Sample placement

## Slide 18: Beam intensity profile

## Slide 22: Results
Neutron Energy (MeV) |  |  |  | 
Radionuclide | q0.1 | q0.25 | q0.75 | q0.9
Bi-201 | 79.9 | 87.8 | 128 | 173
Bi-202 | 70.6 | 77.4 | 114 | 149
Bi-203 | 59.7 | 66.1 | 104 | 141
Bi-204 | 48.3 | 54.4 | 89.4 | 126
Bi-205 | 38.2 | 42.5 | 70.2 | 110
Bi-206 | 29.5 | 32.7 | 61.5 | 100
Na-24 | 9.39 | 12.2 | 79.7 | 122
In-115m | 1.63 | 2.33 | 7.99 | 59.7

## Slide 23: Conclusions
Upgrade of CSBF for 2016 run
  Dedicated slots for activation experiments
Activation characterization campaign at the upgraded CSBF
Comparison of production yields between FLUKA and
γ-spectrometry measurements
Agreement better than a factor of 2

## Slide 24
Thank you for your attention!

## Slide 25
BACKUP

## Slide 26: FLUKA simulations

## Slide 27: CHARM
4 movable shielding walls
Target holder

## Slide 28: CSBF Upgrade

## Slide 29: CSBF – Layout 2015