## Slide 1
24 May 2017
Arim Lee*, Nam-Suk Jung, Leila Mokhtari Oranj, Hee-Seock Lee
Radiation Protection Team Pohang Accelerator Laboratory / POSTECH, Korea
Leakage of radioactive materials from particle accelerator facilities by non-radiation disasters

## Slide 2: Introduction
Present requirements about fire/inundation to get operation permit
• In Korean Law
- To apply the same level of regulation; non-nuclear or nuclear facilities? - In the case of accelerate facilities, different beam particle? - How to estimate the impact of non radiation disasters (fire/inundation)?
Application of law is ambiguous !!
PAL-XFEL 10.0 GeV, 0.06 nm
<Location of Use Facilities> The use facilities and conservation facilities of radiation generating devices should be installed at a place with the less risk of a fire, inundation or ground subsidence.

## Slide 3: Introduction
Method
Case study
- Fire/flood occurred at acc. Facilities
- Select the five common material inside of accelerator tunnel
Review on leakage of radioactive material to the environment
- Based on the properties of interested materials
Activation calculation of five interested materials
Investigation on properties of interested materials
* Interested materials 1. Dust 2. Insulator 3. Concrete 4. Metal 5. Paint
Purpose
To suggest reasonable application of regulations on fire/inundation(flood) 1) Review the possibility of the leakage of radioactive materials due to fire/flood at accelerator tunnel
2) Estimation of the activation level/radionuclide production
* Initial condition - Beam : electron, proton Carbon, Uranium - Energy : 100. 430, 600, 1000 MeV - Used Monte Carlo codes (FLUKA, PHITS, MCNPX)

## Slide 4: Case study: Fire at Acc. facilities
Facility | Nations | Information |  |  |  | Leakage of Radioactive material
Fermilab- 150 GeV - 400 kW | U.S | Date | October 3, 1987 | Incident region | 34 wire ribbon cable | Not described
 |  | Cause | Over-current in a cable |  |  | 
SLAC - 15 GeV - 0.15 nm | U.S. | Date | May, 2013 | Incident region | Beam switching yard | Not described
 |  | Cause | Magnet in the beam switching yard |  |  | 
 |  | Date | June 25, 2014 | Incident region | Klystron gallery | Not described
 |  | Cause | Electrical fire from switchgear cabinet. |  |  | 
Cornell's electron synchrotron | U.S. | Date | September 16, 2009 | Incident region | Underground storage ring of Wilson Synchrotron Laboratory | Not described
 |  |  | October 14, 2009 |  |  | 
 |  | Cause | Old power supply |  |  | 
Moscow nuclear institute | Russia | Date | February 5,2012 | Incident region | the Alikhanov Institute of Theoretical and Experimental Physics | No (Acc. was shut down.)
J-PARC - 3 GeV, - 1000 kW | Japan | Date | July, 2014 | Incident region | No information | No
 |  | Cause | Diesel generator |  |  | 
 |  | Date | 16 January, 2015 | Incident region | Muon D-line area | No
 |  | Cause | Problem on the circuit of newly installed transformer |  |  | 
Fired parts/components : Magnet, power supply, switchgear cabinet, diesel generator, cable/cable tray  Materials : Metals (stainless, iron, etc.), Insulators (Carbon compounds)

## Slide 5: Case study: Flood at Acc. facilities
Facility | Nations | Information |  |  |  | Leakage of Radioactive material
Fermilab - 150 GeV - 400 kW | U.S. | Date | July 17-18, 1996 | Incident region | Main ring tunnel | No
 |  | Cause | Rainfall (45.72 cm) |  |  | 
 |  | Date | April 18, 2013 | Incident region | No information | Not described
 |  | Cause | Rainfall |  |  | 
J-PARC - 3 GeV, - 1000 kW | Japan | Date | March 11, 2011 | Incident region | Linac tunnel | No
 |  | Cause | Lose of power for water pumping system  Max. depth of water reached 10cm (March 24) |  |  | 
 |  | Date | September, 2014 | Incident region | Muon facility | No
 |  | Cause | Valve connection problems |  |  | 
Fermilab
Fermilab
J-PARC
J-PARC
Flooded components/parts : Preamplifier box (placed on floor @J-PARC), girder, floor  Materials : Metals (stainless, iron, aluminum, etc.), Concrete, Paint

## Slide 6: Issued point of fire/flood event
• In the case of Fire,
- Flammability, Melting point, etc.
Ignition temperature of insulator : 450 ℃
According to flammability experiment of horizontal/vertical cable tray, ceiling temperature of opened tunnel : 250 ℃
⇒ 450 ℃ is set as a standard for combustibility in the accelerator tunnel.
The insulator is assumed to be a material that is likely to start burning.
• In the case of Flood,
- Solubility, resistance to water and alkaline, etc.
Through the flood occurred in J-PARC, we considered the resistance to the alkaline due to the reaction between concrete and water.

## Slide 7: Properties of concerned materials in Acc. tunnel
1) Dust
Location | Information
Surface of tunnel wall & accelerator devices | Radioactive dust in accelerator tunnel normally found is mainly produced by natural erosion and by work of radioactive machine part.
Dust
Dust
Considered events | Considerable properties | Possibility to leakage
Fire | Can move following the air. | Moveable/ Possible
Flood | Can be solved into immigrated water or move following water. | Soluble / Possible

## Slide 8: Properties of concerned materials in Acc. tunnel
Dust
Dust
Insulator
(Carbon compounds)
Insulator
Composition | Information
Carbon compounds | Type: Polyvinylchloride(PVC), Kapton(polyimide), Teflon(PTFE) Used in the accelerator tunnel as insulating materials for control/signal processing cable or wire.
2) Insulator

## Slide 9: Properties of concerned materials in Acc. tunnel
2) Insulator
Considered events | Considerable properties |  | Possibility to leakage
Fire | Polyvinylchloride (PVC) | Self-extinguishing material. Melting point : 154 ~ 213 °C Flash-ignition : 330 ~400 °C / Self-ignition : 385 ~400 °C | Combustible / Possible
 | Teflon (PTFE) | Flammability(UL94) : V-0 Flash-ignition : 560 °C / Self-ignition : 580 °C | 
 | Kapton (polyimide) | Flammability : V-0 Maximum service temperature, Air : 400 ℃ | 
Flood | Polyvinylchloride (PVC) | Water absorption: 0.02 - 0.400 % Good alkaline and water resistance. | Insoluble / Impossible
 | Teflon (PTFE) | Water absorption : 0.21 - 0.49 % Excellent chemical resistance. | 
 | Kapton (polyimide) | Water absorption : 2.8 % Greater resistance to water, resistant to organic solvents. | 

## Slide 10: Properties of concerned materials in Acc. tunnel
3) Concrete
Dust
Dust
Concrete
Location | Information
Tunnel, shielding material | Concrete is the main material for tunnel and shielding. Concrete shield is important to solid activation.

## Slide 11: Properties of concerned materials in Acc. tunnel
3) Concrete
Considered events | Considerable properties | Possibility to leakage
Fire | Changes on the properties depends on temperature 1. 100 ℃ or higher: free pore water release 2. 100 ~200 ℃: physically adsorbed water is released. Safety ensured. 3. 300 or higher: cement hydrate in the concrete chemically altered 4. 400 ℃ ↑ : release chemical combined water 5. 500 ℃ ↑ : calcium hydroxide(Ca(OH)2) is thermally decomposed, 50% reduction in strength by heating 6. 600 ~ 800 ℃ : Cement paste shrink. 80% reduction in strength 7. 1,000 ~ 1,200 ℃, ↑ : Concrete Spalling, melting | Incombustible / Impossible
Flood | C2S is the most frequent among the cement compound. This reacts with water to produce calcium hydroxide (Ca(OH) 2) and the calcium silicate hydrate (C-S-H) → water is changed into high alkaline | Soluble / Possible
Concrete is a nonflammable material.
Over 500 ℃, phenomena will not be appear. ⇒ Concrete need to be considered for a flood event.

## Slide 12: Properties of concerned materials in Acc. tunnel
4) Metal
Dust
Dust
Concrete
Metal
Metal
Location | Information
Accelerator devices | Types: Aluminum, Steel(iron), Stainless steel, Copper Accelerator components are largely made of metals. Irradiated accelerator components are related with residual activity.

## Slide 13: Properties of concerned materials in Acc. tunnel
4) Metal
According to experiment using tray, max. temperature of cable on fire : 700~800 ℃, (400 ℃↓, 500~1000s)
According to NUREC, fire on tray : extinguished in 1000~3000s, no melting. fire on cabinet : extinguished within 38 min.
⇒ Metals need to be considered for a flood event.
Considered events | Considerable properties |  | Possibility to leakage
Fire | Aluminum | Vapor pressure: 2,517 ℃ (100 kPa) Melting point: 660 ℃ / Boiling point : 2519 °C | Incombustible / Impossible
 | Steel(Iron) | Vapor pressure: 3,132 K (2,859 ℃, 100 kPa) Melting point : 1535 °C / Boiling point : 2861 °C | 
 | Stainless steel | Boiling point : 1400 ~ 1455 °C | 
 | Copper | Vapor pressure : 2,563 ℃ (100 kPa) Melting point : 1083 ~ 1084 °C/ Boiling point : 2,324 ~ 2,595 ℃ | 
Flood | Aluminum | Solubility: Insoluble in water, dissolved in alkaline, hydrochloric acid | Insoluble(water) Soluble(alkali) / Possible
 | Steel(Iron) | Solubility: Insoluble in water, dissolved in alkaline, alcohol, ether, dilute acid | 
 | Stainless steel | Solubility: Insoluble in water, soluble in alkaline | 
 | Copper | Solubility: Insoluble in water, soluble slowly in alkaline | 

## Slide 14: Properties of concerned materials in Acc. tunnel
5) Paint
Dust
Dust
Concrete
Metal
Metal
Insulator
(Carbon compounds)
Insulator
Paint
Paint
Type | Information
Acrylic resin-based paint, Epoxy resin-based paint | Acrylic resin-based paint for Acc. tunnel wall. Epoxy resin-based paint for Acc. components & tunnel floor.

## Slide 15: Properties of concerned materials in Acc. tunnel
5) Paint
Considered events | Considerable properties | Possibility to leakage
Fire | Acrylic resin-based paint Easy to burn, combustion is continued even after deletion of flame Flash point: 36 ℃ / Self-ignition: 480 ℃ | Combustible / Possible
 | Epoxy resin-based paint NFPA* rating number of flammability hazard : 2 (Must be heated or high ambient temperature to burn) : 3 (Can be ignited under almost all ambient temperatures), Flash point: 23~26 ℃ | 
Flood | Acrylic resin-based paint Solubility: Soluble in organic solvents/ Resistant to alkaline and acids. Chemical Resistance: Excellent for 5% NaOH, H2SO4 | Insoluble / Impossible
 | Epoxy resin-based paint Solubility: Insoluble in water Water, acid, alkaline excellent resistance . Excellent durability. | 
Paint is combustible.
*NFPA 704 : Standard maintained by the U.S.-based National Fire Protection Association
Acrylic resin-based paint (ACRYDIC A-846)
Epoxy resin-based paint (Epocoat210, NUKOPOX PRIMER EP103, NUKOPOX TOPCOAT ET597)

## Slide 16: Assumed leakage path of radioactive material
Assumption of fire case occurred at accelerator facilities
For fire events, Dust, insulator, paint should be considered
Consider activation level !!

## Slide 17: Assumed leakage path of radioactive material
Assumption of flood case occurred at accelerator facilities
water
For flood events, Dust, concrete, metal should be considered
Consider activation level !!

## Slide 18: Activation calculation using MC codes
Assumption for calculation using MC codes
Codes
1) MCNPX 2.7+SP-FISPACT 2007 2) FLUKA 2011.2c 3) PHITS 2.64+DCHAIN-SP 2001
Beam & Target condition
Geometry & Samples
Beam particles : electron, proton, carbon, uranium
Beam energy : 100, 430, 600, 1,000 MeV or MeV/nucleon, (Beam Intensity : 1kW)
Irradiation: 10 days, Cooling: No-cooling, 30 min, 1 hour, 1 day, 1month
Target material : Copper
Copper target
Beam
Sample size : Φ2.5 cm x 0.5 cm (10 cm3)
Sample materials :
1) Metal 2) Concrete 3) Insulator 4) Paint

## Slide 19: Comparison of MC calculations
Total specific activity calculated by codes
- Heavy ions case : FLUKA > MCNPX+FISPACT > PHITS+DCHAIN-SP
- Proton : MCNPX+FISPACT ≒ FLUKA > PHITS+DCHAIN-SP

## Slide 20: Activity ratio of MC codes vs FLUKA
- Beam : 430 MeV/n Carbon, Cooling time : 1 day
<Major isotopes>
ST304L : 44,44m,47Sc, 48,49V, 51Cr, 52, 54Mn, 55Fe, 58,58mCo, 57Ni
Concrete(ANSI-ANS) : 7Be, 24Na, 31Si, 32P, 37Ar, 42,43K, 45,47Ca, 51Cr, 55,59Fe
Kapton : 3H, 7,10Be, 11, 14C
Epoxy : 3H, 7,10Be, 11,14C

## Slide 21: Comparison of specific activity
Total specific activity from Carbon beam on interested materials calculated using FLUKA code
- Activation : Metal, Concrete > Insulator, Paint

## Slide 22: Comparison of clearance index
Clearance index of concerned materials
- Irradiation : 10 days, beam power : 1 kW
- Activation : Metal, Concrete > Insulator, Paint
*Clearance Index :

## Slide 23
Conclusion
- In order to review the radiological protection for non-radiation disasters (fire, flood), case study and the leakage path of radioactive materials was investigated.
⇒ Fire events : dust, insulator, paint / Flood events : dust, concrete, metal
- The activation calculations were carried out using different MC codes for various beam particles and energy.
⇒ Induced activities by electron beam was the lowest. It was 102 – 105 times less than uranium beam case.
- Safety regulation should be applied regarding beam particle type and beam energy

## Slide 24
Thank you.
Notes: Thank you for listening.