## Slide 1
Carlos A. Martins
ESS – Accelerator Division - RF Electrical Power Systems
www.europeanspallationsource.se
Linac 2016 conference, Oct 2016
660kVA SML modulator design and procurement strategy

## Slide 2
Reduced Scale modulator prototype
( SML topology status on March 2015 )
Part I – Low Voltage driver:
→ successfully tested from Feb. 2015 onwards on resistive loads (@1kV);
Part II – HV oil tank assembly:
→ Delivered at LTH test stand on March 4th 2016
Part I
Part II
Electrical schematic

## Slide 3
HV oil tank assembly received at test stand - 4th March 2016
Preliminary testing of HV oil tank assembly at low voltage - 24th March 2016;
1st testing at High Voltage - 4th April 2016
90kV with droop comp. - 18th April 2016
3 & 4 Testing of complete system
SML modulator :
Testing of the reduced scale prototype
( prototype rated: 115kV/20A; 3.5ms/14Hz )

## Slide 4
Part I
Part II
→ Heat run test successfully performed at nominal (115kV, 20A, 3.5ms/14Hz) for 12 hours consecutively
Integrated test of complete system (Part I + Part II)
SML modulator :
Testing of a reduced scale prototype
( prototype rated: 115kV/20A; 3.5ms/14Hz )
ref

## Slide 5
SML modulator, Full Scale design (660kVA)
- Supply of 4x 1.4MWpk klystrons in parallel
Retractable HV oil tank for easier access
Integrated oil spill bin
All in one frame with permanently mounted wheels for easy transportation
Total footprint: 3.8m x 1.4m
(planned was 5.5m x 1.6m, i.e. 40% less);
Total weight: < 5.5 tons (without oil);
Total volume of oil: ~ 2000 litters;
1.4m
3.8m
2.4m
Compact
HV module

## Slide 6
Procurement strategy
3 modulators rated 660kVA for RFQ and DTL to be procured by ESS Bilbao as part of Spanish IKC;
9 modulators rated 660kVA for Medium Beta to be procured either by ESS Bilbao (Spanish IKC) or directly by ESS ERIC;
In both cases:
  Technical Specifications based on “build-to-print” design:
    Detailed electrical schematics;
    Bill Of Materials;
    Set of 3D mechanical drawings;
Timing:
  SoW document is finished (79 pages);
  Set of mechanical drawings (12 annexes) in view of tendering are ready;
  Call for tender for 3 RFQ/DTL modulators to be launched in Oct. 2016;
  Launch of call for tender for 9 Medium Beta modulators not so clear;