## Slide 1: NBPI integration, shutter and basement handling
Jarich Koning
Remote Handling consultant
Heemskerk Innovative Technology B.V.
www.europeanspallationsource.se
2015 May 2016

## Slide 2: Overview
This meeting:
Large change on ‘Light shutter’, at R5.5-R6m around the monolith – ‘Bridge’ area
Inform you on current status, which will be in the upcoming NBEX PDR
Contents:
System layout (presentation)
Few motion sequences (movies in presentation)
Interactive session (Catia)

## Slide 3: Incentives
Improve shielding bunker from target radiation during shutdown
Improve shielding towards basement
Create opportunities for tailoring shutters
Increase accuracy of in-vessel vs ex-vessel guides
Increase accuracy of NBPI mount
Instruments to remain during seal refurbishment
Create option for an NB shutter
Block port when NBPI removed

## Slide 4: ‘Bridge’ configuration
Depending on instrument, various options, generic elements
Floor filler block or GBS could be used as temporary block during NBPI absence
Locking integrated on several levels (dep. on instrument)
BBG to be pushed forward in BBGH to mate with NBPI flange
BBGH ‘floats’ BBG (gravity compensation integrated)
Tailoring possible, just submit to common shutter/block handling interfaces
LSS shielding
BBG
BBGH
NBPI
Sliding hatch
Fall hatch
Gamma Beam Shutter
Floor filler block
Support frame
Rigid chain actuator
Bunker roof support
Actuator cart on rails
Floor fill shielding
Lower shielding
Shutter cask on cart

## Slide 5: Light Shutter System
Different configurations of BBGH, GBS, NBS possible
Use cases described in ESS-0044607
Case
3.3.1, 1)
Case
3.3.1, 3)
Case
3.3.1, 4)
Case
3.3.4, 1)
Case
3.3.4, 2)
Case
3.3.1, 5)
Case
3.3.1, 1)
Case
3.3.1, 3)
Case
3.3.1, 4)
Case
3.3.4, 1)
Case
3.3.4, 2)
Case
3.3.1, 5)

## Slide 6: NB sealing and BBG
He leak-testing connector
Compression spider
Bridge Beam Guide Holder
Bridge Beam Guide
Guide
Alignment assys
Shutter guide rails
Cooling connectors
Double sealing flange
Gravity compensation springs
BBG: Bridge Beam Guide in operational position (light-green) housed in cradle (translucent-brown), mounted on insert, bourn by rails and a locking system (invisible).

## Slide 7: NB sealing and BBG
GBS: Gamma Beam Shutter in shutdown position
BBG pickup surface
Steel volume
Tungsten volume
Actuator interface

## Slide 8: NB sealing assembly
Double sealing flange cross-section
Gravity compensation of spider
RH bolts
Outer seal
Inner seal
Bellows
Lip welds
Aligning pin
Restraint of spider, 2mm clearance
Water cooling lines integrated in spider

## Slide 9: Locking system
Case 3.3.1, 1), but common concept for all shutters and blocks

## Slide 10: Engaging BBG kinematic mount
Case 3.3.1, 1), but common concept for all BBGHs

## Slide 11: Engage GBS
Case
3.3.1, 1)

## Slide 12: Engage NBS
Case
3.3.1, 1)

## Slide 13: Shutter handling
Case
3.3.1, 1)

## Slide 14: FA handling
Common

## Slide 15: References
Refer to ESS-0044607 for more information
Most will be in NBEX SDD-sol ESS-0058226, too.
Pictures originate from model ESS-0054148
Interface drawing ESS-0054148 (not yet released)
  For now on the share at \Machines Directorate\Target division\Public Read Write\Jarich\2016-05-03 Shutter handling pics\ESS-0054148.3.pdf
This presentation ESS-0058290