## Slide 1: CDS-LTS2 thermo-mechanical analysis results
Janusz Skrzypacz
Jarosław Poliński
Przemyslaw Jaszak
Maciej Chorowski
Critical Design Review Meeting, 11-12 January 2017, Wroclaw, Poland

## Slide 2: Allowable stresses
Allowable stress for sustained loads
for 1.4306 fh = min (fc; f) = 143.3 MPa for 1.4301 fh = min (fc; f) = 153.3 Mpa
Allowable stress for thermal loads for: Eh=193000 [MPa]; Ec=209000 [MPa]
for 1.4306 fa = U(1.25fc + 0.25fh)Eh/Ec = 198.5 [MPa]
for 1.4301 fa = U(1.25fc + 0.25fh)Eh/Ec = 212.4 [MPa]
Sum of the allowable stresses
for 1.4306 fh +fa = 341.8 [MPa]
for 1.4301 fh +fa = 365.7 [MPa]
Occasional allowable stress
f = fh*k = 143.3*1.5= 215 MPa

## Slide 3: Process pipes flexibility analysis

## Slide 4: Process pipes flexibility analysis
No | Parameter | VLP | He supply | TS supply | TS return
1 | DN [mm] | 65 | 15 | 15 | 15
2 | Design pressure PS [bar] | 12 | 16 | 16 | 16
3 | Temperature [K] | 3 | 4.5 | 40 | 50
4 | Fluid density r [kg/m3] | 130 | 130 | 27 | 27
6 | Max. sustained stress s1max [MPa] | 157.9 | 189.7 | 190.4 | 185.9
7 | Max. sustained stress s1WRT [MPa] | 61.82 | 82.16 | 89.37 | 82.47
7 | Max. expansion stress s3WRT [MPa] | 119.2 | 65.08 | 67.13 | 64.6
8 | Max. s4WRT = (s1WRT+s3WRT) [MPa] | 131.1 | 95.07 | 100.8 | 90.38
9 | Max. movement of a flex. element [mm] | 23 | 22.7 | 23.5 | 22.7
LC1 - normal operating conditions
Forces in the all interfaces are lower than specified by ESS

## Slide 5: Process pipes flexibility analysis
s1max
s1WUT
LC1 – Sustained stress s1 [MPa] in the VLP pipe –
the close up the maximal stress location

## Slide 6: Process pipes flexability analysis
No | Parameter | VLP | He supply | TS supply | TS return
1 | DN [mm] | 65 | 15 | 15 | 15
2 | Test pressure PT [bar] | 17.2 | 22.88 | 22.88 | 22.88
3 | Temperature [K] | 300.5 | 300.5 | 300.5 | 300.5
4 | Fluid density r [kg/m3] | 1.4 | 5.7 | 5.7 | 5.7
6 | Max. sustained stress s1max [MPa] | 222.8 | 271.2 | 271.6 | 264.9
 | Max. sustained stress s1WRT [MPa] | 88.7 | 113.9 | 94.19 | 114.3
7 | Max. expansion stress s3WRT [MPa] | 0 | 0 | 0 | 0
8 | Max. s4WRT = (s1WRT+s3WRT) [MPa] | 88.7 | 113.9 | 94.19 | 114.3
9 | Max. movement of flex. elements [mm] | 0.8 | 0.4 | 0.5 | 0.5
LC2 – pressure test conditions
Forces in the all interfaces are lower than specified by ESS

## Slide 7: Process pipes flexibility analysis
s1WUT
LC2 – Sustained stress s1 [MPa] in the TS supply pipe – the close up the maximal stress location
s1max

## Slide 8: Process pipes flexibility analysis
LC2 – pressure test conditions

## Slide 9: Outer Jacket flexibility analysis
CTL sections
Valve Box

## Slide 10: Outer Jacket flexibility analysis
No | Parameter | Outer Jacket
1 | DN | 300/250
2 | Pressure [bar] | -1
3 | Temperature [K] | 293
4 | Continuous load kg/m | 10
6 | Max. sustained stress s1 [MPa] | 55.1
7 | Max. expansion stress s3 [MPa] | 0
8 | Max. s4 = (s1+s3) [MPa] | 55.1
9 | Max bellows movement [mm] | 0.9
LC1 - normal operating conditions
Node | Fx [N] | Fy [N] | Fz [N] | Mx [Nm] | My [Nm] | Mz [Nm]
10 | -297 | 104 | -1589 | -285 | -799 | -345
95 | -1306 | 475 | -1241 | -129 | -127 | -1793
470 | 1563 | 586 | -1968 | 17 | -940 | -150
605 | -1294 | -607 | -606 | -161 | -227 | 116
699 | 2779 | 1113 | -916 | -213 | 568 | -619
4000 | 2544 | 10957 | -2812 | -16736 | 134 | 4718
4700 | 0 | -14295 | -337 | 92 | 0 | 0

## Slide 11: Outer Jacket flexibility analysis
LC2 – failure conditions
No | Parameter | Outer Jacket
1 | DN | 250/300
2 | Set pressure of savety valve [barg] | 0.5
3 | Temperature [K] | 223
4 | Continuous load kg/m | 10
6 | Max. sustained stress s1 [MPa] | 26.21
7 | Max. expansion stress s3 [MPa] | 114.7
8 | Max. s4 (s1+s3) [MPa] | 116.3
9 | Max bellows movement [mm] | 22
Node | Fx [N] | Fy [N] | Fz [N] | Mx [Nm] | My [Nm] | Mz [Nm]
10 | 986 | 5874 | 10966 | -8739 | 1716 | -491
95 | -15045 | -5294 | -13796 | 8358 | -10512 | 1966
470 | 14806 | 7636 | -16092 | 5954 | 365 | 2059
605 | -17019 | -7658 | 13518 | -7082 | 10817 | 3866
699 | 12933 | 24631 | -12065 | -9400 | 9430 | 13654
4000 | -15314 | -6044 | -2234 | 8002 | 704 | -2048
4700 | -107 | 7030 | -321 | 90 | 0 | -41

## Slide 12: Outer Jacket flexibility analysis
In both analyzed load cases the maximal sustained and expansion stresses in the outer jacket are lower than allowable ones.
The forces in the interface points are lower than specified by ESS.
The forces and moments acting on the outer jacket supports have significant values, so that they require a strong support structure.
Summary

## Slide 13: Fixed support
 | Von Misses stress [MPa] | Total deformation [mm]
LC2 – normal operating conditions | 120 | 1.24
LC3 - mechanical loads for LC2 | 114 | 0.85
LC4 – pressure test conditions | 51.65 | 0.218

## Slide 14: Fixed support
Examples of the calculation results for LC2

## Slide 15: Jumper connection vacuum barrier
 | Von Misses stress [MPa] | Total deformation [mm]
LC1 – normal operating conditions | 109 | 1.1
LC2 – only mechanical loads that corresponds to LC1 | 77.8 | 0.24
LC3 – loss of vacuum; the forces and the moments corresponds to LC1 | 129 | 0.43
LC4 – loss of vacuum in opposite side to LC3 | 76 | 0.23

## Slide 16: Jumper connection vacuum barrier
Examples of the calculation results for LC3

## Slide 17: Sliding support
 | Von Misses stress [MPa] | Total deformation [mm]
LC1 – normal operating conditions | 50.1 | 3.1
LC2 – normal operating conditions with only mechanical loads | 78 | 0.4

## Slide 18: Sliding support
Examples of the calculation results for LC1

## Slide 19: Frame 1 calculations
 | Von Misses stress [MPa] | Total deformation [mm]
LC1 – normal operating conditions | 128 | 0.8
LC2 – failure of a process pipe – helium fills the outer jacket and cools it down to 223 K – mechanical and thermal loads were applied. | 156.1 | 2.01
LC3 – failure of a process pipe – helium fills the outer jacket and cools it down to 223 K – only mechanical loads were applied. | 169 | 1.97

## Slide 20: Frame 2 calculations
 | Von Misses stress [MPa] | Total deformation [mm]
LC1 – normal operating conditions | 6.52 | 0.17
LC2 – failure of a process pipe – helium fills the outer jacket and cools it down to 223 K – mechanical and thermal loads were applied. | 196.9 | 4.04
LC3 – failure of a process pipe – helium fills the outer jacket and cools it down to 223 K – only mechanical loads were applied. | 89.5 | 3.4

## Slide 21: Frame 3 calculations
 | Von Misses stress [MPa] | Total deformation [mm]
LC1 – normal operating conditions | 14.87 | 0.24
LC2 – failure of a process pipe – helium fills the outer jacket and cools it down to 223 K – mechanical and thermal loads were applied. | 162.4 | 4.82
LC3 – failure of a process pipe – helium fills the outer jacket and cools it down to 223 K – only mechanical loads were applied. | 152.28 | 4.01

## Slide 22: Frame 4 calculations
 | Von Misses stress [MPa] | Total deformation [mm]
LC1 – normal operating conditions | 140.1 | 1.52
LC2 – failure of a process pipe – helium fills the outer jacket and cools it down to 223 K – mechanical and thermal loads were applied. | 202.94 | 2.24
LC3 – failure of a process pipe – helium fills the outer jacket and cools it down to 223 K – only mechanical loads were applied. | 199.2 | 2.04

## Slide 23: ValveBox Fixed Support
 | Von Misses stress [MPa] | Total deformation [mm]
LC1 – normal operating conditions | 144.5 | 0.96
LC2 – failure of a process pipe – helium fills the outer jacket and cools it down to 223 K – mechanical and thermal loads were applied. | 113.99 | 0.97
LC3 – failure of a process pipe – helium fills the outer jacket and cools it down to 223 K – only mechanical loads were applied. | 101.54 | 0.68

## Slide 24: Sliding Support
 | Von Misses stress [MPa] | Total deformation [mm]
LC1 – normal operating conditions | 13.64 | 0.67
LC2 – failure of a process pipe – helium fills the outer jacket and cools it down to 223 K – mechanical and thermal loads were applied. | 97.33 | 2.5

## Slide 25: Sliding Support
 | Von Misses stress [MPa] | Total deformation [mm]
LC1 – normal operating conditions | 8.5 | 0.05
LC2 – failure of a process pipe – helium fills the outer jacket and cools it down to 223 K – mechanical and thermal loads were applied. | 129.6 | 1.5