## Slide 1: Identification and marking of ESSI deliverables
ESS Quality workshop at Saclay 30/06/2016 | Anaïs BRUNIQUEL
Notes: Introduction :
The components and the signals are identified in order to follow it during the different phases (design, manufacturing, test and assembly for ESSI and operating phase for ESS).
According to the needs from ESS and from ESSI (CEA), the rules to identify has been specified in a technical note. I present these rules in this presentation.

## Slide 2: Rules applied for ESSI deliveries
Two types of code:
  The first is indicated by the ESS naming convention. It applies to all technical systems, devices, equipment and signals which are followed by the control system.
       Naming convention - ESS-0000757 (version 2.0)
  The second code is an Irfu code which applies to all technical systems, devices and equipment included in CEA delivery.
       Identification and marking of ESSI project’s deliverables - CEA-ESS-PJT-NT-0001 1.0 (A)
Application of these dispositions:
  The first rule is applied to the control system (signals, software).
  The two rules are applied to all deliverables of ESSI from CEA.
  A table gives the correlation between the two identifications (PBS tables).

## Slide 3: ESS Naming convention
Example: MBL-EMR:CavM-001
System : cryomodule MBL
Subsystem : EMR for Electromagnetic Resonators
Device identifier : CavM for Elliptical cavity medium beta

## Slide 4: ESSI naming convention
Irfu (U)
IPNO (O)
Infn (N)
ESS (S)
STFC (C)
Corresponds to a code with 2 digits provided by the PAO
Supplier
Purchaser
Corresponds to the last 7 numbers of Irfu drawings or the drawing identifier of partner
Drawing reference(1)
Corresponds to the version of the drawing
(Letter: A, B, C…)
Edition
Corresponds to the chronological number of manufacturing according to if it’s series or prototype (the first digit indicates if it is associated to prototype, series, part of pre-production or spare)
Serial number
Corresponds to a deliverable displayed by a letter.
Deliverable
(1) If there is no drawing reference, a unique identification code can be proposed by the purchaser and apply after the approval by the configuration manager of ESSI project and the PAO. It shall be a group of letters which is representative of the component. For example: Multi-Layer Insulation (MLI) with JUMPVER for the MLI of the Jumper thermal screen (for ECCTD).
U
Z
A
0
0
0
0
1
1
2
R
C
0
0
0
1
Code | Deliverables of ESSI Project
R | ECCTD
H | HBL
M | MBL
Q | RFQ
U | EMU
D | Doppler
I | IPM
1st digit | Description
0 | Prototype -demonstrator
1 | Pre-production
2 | Series
3 | Spare

## Slide 5: Application of the identification codes
Traceability
  The identification code is included in the PBS and in the manufacturing file of each component.
Marking
  The marking place is indicated on the drawings (Interface or general drawing).
  The marking place shall be clearly visible and readable for the assembly and the disassembly of the system (e.g.: RFQ, Cryomodule) or sub-system (e.g.: Tuner, coupler).
  The marking place is defined by the purchaser (WP leader corresponding to the deliverable) and the mechanical engineers (e.g.: Irfu/SIS)
  The marking process shall not be manual. The method shall respect the material proprieties and the mechanical proprieties of the part.
  It may be a label, punch, engraving, or other method which shall be submitted by the supplier to the CEA and shall be approved by the CEA before application.
Notes: The rules of identification shall be indicated in the technical specification for the supply of any components or, at the latest, during the kick off meeting. The purchaser shall also indicate the type of production (series, prototype) to the supplier. Then, the supplier gives the serial number for each manufactured components.
The revision applies when a component is modified (in its design and/or its properties) and when the drawing attached to this component is improved. The revision is an evolution of the identification which corresponds to the modification of the edition of the drawing.

## Slide 7: DSM Irfu
Commissariat à l’énergie atomique et aux énergies alternatives
Centre de Saclay | 91191 Gif-sur-Yvette Cedex
T. +33 (0)1 69 08 xx xx | F. +33 (0)1 69 08 99 89
  Etablissement public à caractère industriel et commercial | RCS Paris B 775 685 019