## Slide 1: Neutron Beam Extraction System Design update for IKON-11
Jarich Koning, Bengt Jönsson
www.europeanspallationsource.se
14/15-09-2016

## Slide 2: Alignment strategy
Port blocks measured at installation (expected <±2mm) ->TNBA
Machine internal mounting pads to correct to within <±0.05mm
Replicate port block situation on test-bench
  Align NBPI + BBG (=shutter) internal guides there (±50µm / <200µrad guide-to-guide)
BBG provides fiducials to help bunker-mounted equipment
NBPI-to-BBG kinematic mount delivers good repeatability
  Blind mount of NBPI and BBG should deliver some ±150µm / <<200µrad absolute
  Notes:
  Building is not directly connected to vessel. Several sources of deformation present.
Target-building Target floor foundation is different compared to bunker floor.
Notes:   TNBA, Theoretical Neutron Beam Axis

## Slide 3: Implemented changes
Relaxation of radiation protection
  BBG not parked in gamma-shielding structure during shutdown
Simplification: only BBG with GBS on top (no other blocks like NBS), and:
Solve fast-closing (<60s) requirement
  One configuration simplifies locking/engaging system
  Allows other actuator which allows faster-closing
Relaxation of position accuracy
  Semi-kinematic mount between NBPI and BBG lead to more available space for NB guides
Increase space for beam guides, and
Solution for Al-to-SS316L connection, and
Solution for seal retainment, and
Integration of NBW in flange
  Integrate all these in one Al60601T6 flange (single-use): saves cost, too
  Yields much more space for NB guides at back flange

## Slide 4: Light Shutter System
GBS on top of BBG. Not configurable.
Each shutter has a braked, ballscrew-style actuator
Shutter actuator pushes BBG up to its mount against Flange/NBW.
BBG then tilts slightly to engage fully to Flange/NBW
Loss of power causes a quick descent of the GBS+BBG
During maintenance, GBS will stay in front of beam port on dedicated hooks
BBG
NBPI
Floor filler block
Rigid chain actuator
Bunker roof support
Floor fill shielding
Handling tooling
Flange/NBW
GBS
Shutter actuator
GBS hooks

## Slide 5: New integrated all Al Flange/NBW
Vacuum seals milled
Sealing length halved
Much more space for NBW: h562 x w270mm
Still have to solve safety case, possibly resulting in several smaller NBW variants
Z, Y and rX Degrees-of-Freedom to position NBW w.r.t NBPI
NBW area
Dowel-in-pin and dowel-in-oblong hole constrain Y, Z and rX
Vacuum sealing edge
Vessel-side water flange

## Slide 6: Flange/NBW & BBG
Mount:
Sphere (3DoFs)
Cylinder (2DoFs)
Top pad touches (1DoF)
NBW provides kinematic mount to BBG
NBW connects Cooling water flow to NBPI
NBW pushes NBPI (on its integrated disc spring stacks) forward on its kinematic mount to port blocks
NBW area
Cooling
Tilting axis
Notes: Extra slides follow

## Slide 7: BBG tilting engagement
Tilting axis
Actuator force
Notes: Extra slides follow

## Slide 8: Beamlines in new shape
Current 3D beamline models:
Freia (pink, large red)
Heimdal (red/blue)
Loki (purple)
NMX (green/grey)
Pictures:
Left: Insert back flange
Mid: With flange, Xsec @5.5m & @R6m
Right: With BBG, Xsec@R6m
Note: flange/NBPI/BBG reflect new focal points at TCS ±89, ±54mm!

## Slide 9: NBEX   Instrument
Highlighted: Common NBEX fixed features
Vertical relocation of wheels only after discussion with NBEX
Sizing of wheels yet to be confirmed
Rest of volume is up to Instrument
BBG Side view
TCS
TCS

## Slide 10: NBEX   Instrument
Highlighted: Common NBEX fixed features
Rest of volume is up to Instrument
NBPI back
view

## Slide 11: Notes for instruments
Currently there is only water cooling (doubles as thermal conditioning) to the insert (ESS-0060741: 35±5°C, ΔTmax=3°C):
  If low-pressure He is required in insert, enclose it permanently
  If flow of anything else is required in insert, make your case today.
Active cells will not process all materials (ESS-0029936):
  If you need anything else then Steel, Stainless Steel, Tungsten, BoronCarbide, Copper, Aluminium, Lead, make your case today. Be aware that Si, ceramics in general are not currently allowed.
There is no cooling/conditioning planned for the BBG
  If you need He in the guides, it has to be permanently enclosed.
No trespassing from bunker into shutter space nor contact are allowed
  Instrument that pushes forward like ESTIA proposed is likely to interfere with safety concept.

## Slide 12: Notes for instruments
Please design beam lines with physical beam guides AND their support to the Insert & BBG.
  Connect cooling fluid in the Insert as well.
Design BBG to contain shielding for slits around Insert
  Current BBG example does not yet have this…

## Slide 13: Questions?
Notes: Extra slides follow