## Slide 1
1
Carlos A. Martins
European Spallation Source – ESS AB
Accelerator Division, RF Group
Solid State Klystron Modulators
for
Long Pulse (>100µs) Linac’s
Topologies and Design Issues

## Slide 2
2`
Sophisticated power electronics systems
Introduction - Modulator? Isn’t it just a power supply?
Can disturb the electrical grid significantly
Very few companies exist worldwide
Impacts highly on the Linac availability (MTBF, MTTR)
MTBF (1 modulator) = ~ 70’000 hrs;
MTBF (1 klystron) = ~ 50’000 hrs;
SS Long pulse (ms) modulator companies | Long list (have designed & built 1 prototype) | Short list (have successfully designed & built several units used in accelerators)
Europe | 5 | 2
USA | 1 | 1
modulator
klystron
Large footprints & Heavy equipment
1m
Vert klystron
modulator
3.8m
1.6m
Considerably costly
Standard low/medium voltage power supply: < 1€ / W
Klystron modulators: > 3€ / Wav
Yes, but not an “usual one”
(impacts strongly on the Linac design, construction, cost, availability)

## Slide 3
3
Typical requirements & parameters
(SS Pulsed klystron modulators)
Pulse width
Rise time
Fall time
time
Flat-top
V
 | SNS | ISIS | HP-SPL | ESS | CLIC
Pulse width (50% amplitude): | 1.6ms | 2ms | ~2.5ms | 3.5ms | 140µs
Flat-top duration | 1.5ms | 2ms | ~2.2ms | 3.31ms | 135µs
Precision/droop at flat-top (low freq,< 1kHz): | <1% | <5% | <1% | <1% | <1%
HF ripple at flat-top (> 1 kHz): | 0.1% | 0.1% | <0.1% | <0.01% | <0.01%
Pulse repetition rate | 60Hz | 50Hz | 50Hz | 14Hz | 50Hz
Nominal pulse voltage | 140kV | 110kV | 115kV | 100kV | 150kV
Nominal pulse current | 70A | 45A | 50A? | 50A | 160A
Nominal pulse power | 9.8MW | 5MW | 5.7MW? | 5MW | 24MW
Nominal average power | 940kW | 440kW | 710kW | 250kW | 170kW
Rise/fall times (99% / 1%) | 100µs | 10µs | ~250µs | ~190µs | 5µs
Maximum energy in case of arc | <10J |  |  |  | 
Maximum reverse cathode voltage | ~10% |  |  |  | 

## Slide 4
4
Pulse transformer (PT) based
Ver. 1: Monolithic PT with LC bouncer
FERMILAB, DESY, CERN, RRCAT, …
Medium voltage electronic pulser installed in air insulated cabinet;
PT installed in a oil tank;
LC passive bouncer compensates for voltage droop;
HV solid state switch generates the pulse and protects the klystron in case of an arc;
Undershoot network demagnetizes the PT;
Voltage reversal on the klystron shall be limited by design of the undershoot network;
Pulse rise/fall times determined by the PT leakage inductances (typically 100..200µs);
No high frequency ripple is generated in the flat-top;
Monolithic system;

## Slide 5
5
Pulse transformer (PT) based
Ver. 3: Interleaved stacked converters as primary side pulser
Medium voltage electronic pulser installed in a air insulated cabinet;
PT installed in a oil tank;
Active voltage droop compensation through feedback;
Low voltage solid state switches required;
Active demagnetization of PT with energy recovery (limited voltage reversal on the klystron);
Active current shut-down in case of arcing;
Pulse rise/fall times determined by the PT leakage inductances (typically 100..200µs);
High frequency ripple is generated in the flat-top (can be filtered);
Modular system (up-to primary side of PT);
DESY

## Slide 6
6
Marx Generator based
High Voltage electronic pulser installed in a air insulated cabinet;
Oil free;
Several Marx cells are charged in parallel and discharged in series;
Active voltage droop compensation in each Marx cell;
Low voltage solid state switches required, but shall be isolated to ground at High Voltage;
No voltage reversal on the klystron;
Short rise/fall times (determined by the dI/dt limiting inductors, typically 10..20µs)
High frequency ripple is generated in the flat-top (can be filtered);
Modular system;
SLAC

## Slide 7
7
Resonant Polyphase
LANL, SNS
Medium voltage H-bridge converters installed in air insulated cabinets;
High Frequency transformers, diode rectifier bridge and output filter in an oil tank;
Active voltage droop compensation through feedback, by H-bridge frequency/phase control;
Low/Medium voltage solid state switches required;
No voltage reversal on the klystron;
Rise/fall times determined by the resonance circuit (typically 100..200µs);
High frequency ripple is generated in the flat-top (can be filtered);
Monolithic system;

## Slide 8
8
Direct switch
Rutherford Appleton Lab
High Voltage direct switch buck-converter installed in a oil tank;
Active voltage droop compensation through feedback is possible (active bouncer);
High voltage solid state direct switch stack is required;
No voltage reversal on the klystron;
Rise/fall times determined by the dI/dt limiting inductor (typically 5..10µs);
High frequency ripple is generated in the flat-top if active bouncer used (can be filtered);
Monolithic system;

## Slide 9
9
ESS cost model and cost optimization
Relative cost (p.u.)
120 cavities (1cav./klyst.) | 1 klys/ mod | 2 klys/ mod | 3 klys/ mod | 4 Klys/mod
# klystrons | 120 | 120 | 120 | 120
# modulators | 120 | 60 | 40 | 30
Average power per modulator | 150kVA | 300kVA | 450kVA | 600 kVA
Cost / modulator | 0.47pu | 0.75pu | 1pu (*) | 1.26pu (*)
Total cost of modulators | 56.4pu | 45pu | 40pu | 37.8pu
Relative cost savings (wrt 1 klys/mod) | 0% | 20% | 29% | 33%
(*) - extrapolation
ESS choice

## Slide 10
10
Development and procurement strategies
- Can’t we just buy them?
 | Strategy I - in house development; - call for tender for series production as “built-to-print” | Strategy II - call for tender for qualification of prototypes (ex: 3 units from 3 manufacturers); - call for tender for series production (ex: best 2 out of the 3 pre-qualified) | Strategy III - single call for tender for the whole quantity
CERN – Linac4 (17 modulators / ~500 kVA) | X |  | 
CERN – RF test stand (1 modulator / 180 kVA) |  |  | X
DESY – XFEL (~25 modulators / ~7.5 MVA) |  | X | 
RAL – ISIS (1 modulator/ ~400 kVA) |  |  | X
ONRL – SNS (~16 modulators/ ~16 MVA) | X |  | 
KEK – JPARC | X |  | 

## Slide 11
11
Electrical grid power quality
- Can’t we just connect them into the wall plug?
Grid power quality
(dictated by the capacitor charger)
EMC (conducted noise, immunity & susceptibility)
Current harmonic distortion (depends on the capacitor charger topology)
Flicker (depends on the capacitor charger topology & on the charging control scheme)
Flicker standards (low voltage public grids)
14 Hz
(DV/V)max=0.35%
Possibility Capacitor Charger:
Active Front End with constant power regulation

## Slide 12
12
1.- Klystron modulators for long pulse (100µs) Linac’s:
  One of the main components of the High Power RF sources;
  Large footprints required in the RF gallery;
  High impact on costs, MTBF/MTTR and machine availability;
  Depending on the power levels and pulse lengths required, may have a strong impact on the grid power quality (harmonic distortion, flicker)
2.- If possible invest on internal prototyping or at least on understanding the topologies and control techniques involved;
3.- Invest in R&D for grid power quality assessment (ex. flicker mitigation techniques)
4.- Adopt a convenient procurement strategy, involving multiple vendors and validation stages (prototyping, pre-series, series);
Conclusions