## Slide 1
Single Spoke Cavity b = 0.37 for MYRRHA
(RF and) Mechanical Studies

## Slide 2
Contents
Description of the cavity and its helium vessel
1.1 Cavity
1.2 Helium vessel
1.3 Assembly
RF design
2.1 Starting points
2.2 RF parameters
Static calculations
3.1 Description of the different loaded cases
3.2 Leak test of the cavity without helium vessel
3.3 Leak test of the cavity with its helium vessel
3.4 Pressure sensitivity in the cryomodule
3.5 Mechanical-vibration modes
RF-Mechanical coupled simulations
4.1 RF parameters
4.2 Sensitivity for cavity tuning
4.3 Helium bath pressure fluctuation
4.4 Lorentz forces detuning factor

## Slide 3
1.1 Cavity
1. Description of the cavity and its helium vessel
RF Design: 2-gap Spoke cavity defined by RF analysis (with CST Microwave Studio)
Material: 3-mm thick bulk Niobium
Donut stiffener (x2)
Spokebase stiffener (x2)
Pick-up probe port
int= 56mm
Fundamental Coupler port int= 56mm
580 mm
int 485 mm
Total weight : 42 Kg
int= 56mm

## Slide 4
1.2 Helium vessel
1. Description of the cavity and its helium vessel
Material: 3-mm thick Titanium grade 2
CODAP:
Pallowable = 0,30 MPa
Pallowable =
Roark formula:
Pcrit =
E = Young modulus
e = thickness
L = free length
v = Poisson coef.
r = cylinder radius
Pcrit = 0,74 MPa
int 530 mm
534 mm
Supports for Cold Tuning System (CTS) (x4)
Bracket for supporting in the cryomodule (x4)
Pick-up Flange
Coupler Flange
Helium Flange
Ring stiffener
Total weight : 22 Kg
Buckling analytical calculation

## Slide 5
1.3 Assembly
1. Description of the cavity and its helium vessel
Welded connections
1 Bellows
Welded connections
Total weight : ~70 Kg

## Slide 6
2.1 Starting points
2. RF design
SPOKE BAR GEOMETRY : feedback from the two Single-Spoke resonators and the Triple-Spoke resonator fabrication (EURISOL)
Spoke bar base (H field area):
no racetrack shape 3D weld seams are not easy (Spoke bar-to-cavity body connection)
no cylindrical shape Hpk too high
Conical shape is chosen
Spoke bar center (E field area): racetrack shape is ok

## Slide 7
2. RF design
GOALS
Epk/Eacc < 4.4
Bpk/Eacc (mT/MV/m) < 8.3
CST MicroWave Studio 2012
Model created with the 3D CAD tools of MWS
Symetries: ¼,
BC: Magnetic planes,
Tetrahedral mesh, Nb tetrahedrons~10 000
1st mode calculated (TM010)
Optimisation of a dozen parameters
2.2 RF parameters [1]

## Slide 8
2. RF design
3.1 RF parameters
Epk
Lcav=435mm
Bpk
Optimized RF parameters | 
Frequency [MHz] | 352.2
Optimal beta | 0.37
Vo.T [MV/m] @ 1 Joule & optimal beta | 0.693
Epk/Ea | 4.29
Bpk/Ea [mT/MV/m] | 7.32
G [Ohm] | 109
r/Q [Ohm] | 217
Qo @ 2K for Rres=20 nΩ | 5.2 E+09
Pcav for Qo=2 E+09 & 6.4 MV/m [W] | 9.35
2.2 RF parameters [1]
Qext~2.2E+06
port=56mm, Z=50Ω

## Slide 9
Leak tests during fabrication
  Bare cavity (=1st fabrication step)
  Cavity with its helium vessel (=Cavity completed)
Keep stresses < 50 MPa
Test inside the cryomodule
  Cooling down at 4K
Define the critical pressure during cool down process
  Mechanical-vibration modes analysis
Check sensitivity to microphonics
  Frequency shift by pulling on beam tubes
Define the sensitivity for the tuning system
  Helium bath pressure fluctuation
  RF sensitivity due to the Lorentz forces
Define a range for the pressure and Lorentz detuning factors
3.1. Description of the different loaded cases
3. Static calculations
Bare cavity
Jacketed cavity

## Slide 10
3. Static calculations
Uzmax = 0.32 mm
On cavity end-cups :
42 MPa
3.2 Leak test of the cavity without helium vessel (1 bar external load)
Without ring stiffener
With ring stiffener
On cavity end-cups :
30 MPa
Donut ribs: 63 MPa max
Ring ribs: 65MPa max
Uzmax = 0.2 mm
Donut ribs: 60 MPa max
> 50 MPa
> 50 MPa
Max stress on cavity walls < Yield stress limit

## Slide 11
3.3 Leak test of the cavity with its helium vessel
Cavity under vacuum/He vessel P=1bar
Cavity P=1 bar/ Helium vessel under vacuum
Uzmax = 0.19 mm
On one cavity end-cup : 27 MPa
Donut ribs: 67 MPa
Uzmax = 0.1 mm
Uzmax = 0.54 mm
35 MPa max stress
at the spoke bar-to-rib junction
Donut ribs: 65 MPa
> 50 MPa
> 50 MPa
3. Static calculations
Max stress on cavity walls < Yield stress limit

## Slide 12
3.4 Pressure sensitivity in the cryomodule
Umax = 0.11 mm
30 MPa at the iris area
Cavity with its helium vessel inside the cryomodule:
Cooling down (Helium bath at 4K)
  0 bar in the cavity
  1 bar in the helium vessel
  0 bar in the cryomodule
Boundary conditions in the cryomodule
Helium vessel maintained by 4 slideways
Middle position fixed by an invar rod
The CTS (Cold Tuning System) is free during the cooling down
35 MPa at the spoke bar-to-rib junction
 The maximum pressure is around 1,6 bar (<-> Yield strength Re (Niobium) = 50 MPa)
3. Static calculations

## Slide 13
3.5 Mechanical-vibration modes
Beam tubes boundary conditions: free-free
Mode | Frequency | Location
1 & 2 | 232 Hz | Beam tube at CTS side
3 | 320 Hz | Spoke bar
4 & 5 | 380 Hz | RF ports
6 & 7 | 420 Hz | Helium vessel
8 | 430 Hz | Spoke bar
9 | 450 Hz | Helium vessel
10 | 480 Hz | RF ports
11 | 495 Hz | Helium vessel
12 | 500 Hz | 2 beam tubes
Mode 380 Hz
Mode 232 Hz
Mode 320 Hz
Mode 500 Hz
The 1rst critical mode (mode 3) >> 50 Hz
3. Static calculations
Critical modes in bold

## Slide 14
4.1 RF Parameters
4. RF-Mechanical coupled simulations
 | ANSYS
Frequency [MHz] | 352,2
Beta | 0.37
Bpk/Eacc [mT/(MV/m)] | 7,06
Epk/Eacc | 4.22
G [Ohm] | 109
r/Q [Ohms] | 217
Lacc = Ngap.b.l/2 [m] | 0.315
Temperature (K) | 2
Q0 Cu@ 300K | 22313
Q0 Nb@ 2K | 1.01*1010

## Slide 15
4.2 RF Sensitivity for cavity tuning
Tuning sensitivity
Df/Dz = 156 kHz/mm (*)
Kcav >15 kN/mm
380 MPa / mm
Remark : 0,13mm max allowable at ambient temperature
CTS blocks
* The CTS blocks are reinforced by stiff bars (not included in this model). Hence, we assume no possible rotation of the blocks.
4. RF-Mechanical coupled simulations

## Slide 16
4.3 Helium bath pressure fluctuation
Nota: bandwith Df =160 Hz
Sensitivity to He pressure Kp [ Hz/mbar] without CTS | +7.65
Sensitivity to He pressure Kp [ Hz/mbar] with CTS | +14
0 bar
1 bar
0 bar
beam tube and CTS support rigidly linked along Z axis
Without CTS
With CTS
The holding support of the cavity inside the cryomodule will have an influence on its deformation. Here, we only consider the coupler port fixed along Z axis.
4. RF-Mechanical coupled simulations

## Slide 17
+14
Kp [ Hz/mbar] (fixed ends) | +14
Cavity stiffness Kcav [kN/mm] | 16
Longitudinal sensitivity [kHz/mm] | 156
+7.65
EVOLUTION OF KP
4.4 Helium bath pressure fluctuation
FEM result with a specific CTS stiffness
4. RF-Mechanical coupled simulations

## Slide 18
4.5 Lorentz Forces detuning factor
Lorentz Factor: KL = f / E²acc |  | 
For 8MV/m |  | 
KL [Hz/(MV/m)2] (without CTS) | KL =-6.0 | Df = -384 Hz
KL [Hz/(MV/m)2] (with CTS) | KL =-5.28 | Df = -338 Hz
Without CTS
With CTS
Radiation pressure in Pa for 8MV/m
In both cases, the coupler port is fixed along Z axis
beam tube and CTS blocks linked along Z axis
4. RF-Mechanical coupled simulations

## Slide 19
-5.28
KL [Hz/(MV/m)2] (fixed ends) | -5.28
Cavity stiffness Kcav [kN/mm] | 16
Longitudinal sensitivity [kHz/mm] | 156
-6.
EVOLUTION OF KL
4.6 Lorentz Forces detuning factor
FEM result with a specific CTS stiffness
4. RF-Mechanical coupled simulations

## Slide 20
5. Next…
1/ Design is finished
2/ Niobium ordered from NINGXIA for 1 cavity. Fabrication finished on 20th April 2013
3/ Detailed technical drawings of the cavity started
4/ Call for tender publication: July 2013