## Slide 1
LIPAc status & design
Linear IFMIF Prototype Accelerator (LIPAc)

## Slide 2
2 accelerators, 2 x 125 mA, 2 x 5MW
Deuteron source
140 mA, 100 keV
RFQ 5 MeV
SRF Linac 40 MeV
(Half Wave Resonators)
High >20 dpa/an 0.5 L
Medium > 1 dpa/an 6 L
Low < 1 dpa/an 8 L
Test Cells
Lithium Target
25 mm thick
15 m/s
Beam shape
200 x 50 mm2
LIPAc = prototype for IFMIF
includes all critical accelerator components
to be tested at nominal beam current at BA site
aims at generating materials irradiation test data for DEMO and future fusion power plants
based on an accelerator-driven, D-Li neutron source to produce high energy neutrons at sufficient intensity and irradiation volume
Total neutron flux  1018 n/m2/s
with a broad energy peak near 14 MeV
IFMIF & LIPAc objectives

## Slide 3
System | Coordinating | Contributing
Injector | CEA | 
RFQ | INFN-LNL | 
MEBT | CIEMAT | 
Cryomodule | CEA | CIEMAT
HEBT & Beam Dump | CIEMAT | 
RF Power System | CIEMAT | CEA / SCK·CEN
Cryogenic Plant | CEA | 
Beam Diagnostics | CEA | CIEMAT
Local Control System | CEA | CIEMAT / INFN
Conventional Facilities | JAEA | 
Central Control System | JAEA | 
RFQ couplers | JAEA | 
Procurement sharing
Components of the prototype accelerator provided by European Institutions
(design, construction, acceptance tests)
Infrastructure (building, auxiliaries, etc) provided by JAEA

## Slide 4
accelerator components mockup
125 mA 9 MeV deuteron beam (1.125 MW)
Injector
100 kV
RFQ & MEBT
5 MeV
Cryomodule
9 MeV
HEBT & Beam Dump
RF System 18 RF chains
Cryogenic plant

## Slide 5
Low energy < 5 MeV
Injector (Ion source, LEBT) beam dynamics
ECR ion source
high level of space charge compensation all along the LEBT line
to meet the requirements: emittance (0.25  mm mrad) + RFQ matching
injection of specific gas in HEBT (krypton  4.10-5 hPa) predicted by calculations
HV electrode in front of the RFQ to trap the electrons (e-repeller)
LEBT no beam loss, optimum injection into RFQ
Initial 4-electrode extraction system
New 5-electrode extraction system
after sparking issues at 100 kV
CEA
Extraction: 140 mA D+  175 mA total (80% D+, 15% D2+, 5% D3+)

## Slide 6
Injector
Injector at CEA-Saclay
Ion source on HV platform
Equipped LEBT
View-port after 1st solenoid

## Slide 7
Injector D+ beam tests
Injector meets the specifications at low duty cycle
No showstopper to reach the specifications with continuous beam
emittance measurement at high duty cycle to be improved
Emittance evolution with beam current
10% duty cycle
From 100mA to 150mA
Optimal tuning for emittance coincides
with correct matching to RFQ (lowB)
100 mA 0.14 
110 mA 0.15 
120 mA 0.16 
130 mA 0.17 
140 mA 0.20 
150 mA 0.26 
Injector arrived at Rokkasho
end of March 2013

## Slide 8
modulation
Voltage/100 (kV)
Av. aperture (cm)
Small aperture (cm)
Shaper GB Accelerator
B
  Main parameters selected
  Increasing voltage following an analytic law
Strong focusing (B=7) to keep the tune depression > 0.4 for better control of space charge
Min. beam loss & main resonances avoided in the accelerator section
This design allowed to obtain a good transmission with good margin
But a lower focusing parameter B at the RFQ entrance will make easier the beam injection from the LEBT (less demanding for the solenoids)
A low-B RFQ studied and adopted
Studies of the transmission of the couple LEBT+RFQ showed a more comfortable tunable range
RFQ design
X'
X
43 mrad
24 mrad
Convergent beam
at the RFQ input

## Slide 9
cryo pumps
RF couplers
RFQ technology
Cooling system  600 kW RF power
28 channels longitudinally drilled along the RFQ modules
3 independent circuits for frequency tuning & field profile control
18 Cu modules 10 m 10 cryo-pumps
22 slug tuners/quadrant 8 couplers
INFN

## Slide 10
technological prototype machined at INFN and local industries, brazed at CERN
2 prototypes scale ½
brazed in 1 single step
RFQ technology
Skid prototype
Full scale Al mockup to validate tuning procedure & mode stabilization by means of beadpull measurements
Vacuum ports
Vanes

## Slide 11
RFQ fabrication and tests
module #16 (High Energy SM)
machined & brazed
Fabrication tolerance
target = 50 m acceptance criteria = 100 m
1st module : 100 m max deformation measured
2nd module : -25 m 1st brazing +13 m 2nd brazing
3 modules (plus RF plug) completed for high power tests at Legnaro in July 2013

## Slide 12
Scrapers: to clean the beam from transverse halo and off-momentum particles (non-accelerated in the RFQ) before the SRF Linac
MEBT design & beam dynamics
designed for 500 W beam power deposition
beam dynamics prediction < 10 W
very compact  2 m, many components
5 quadrupoles & steering coils
2 bunchers, 2 movable scrapers
BPMs (in the center of quads)
turbomolecular pumps on bunchers (1300 l/s /buncher)
CIEMAT

## Slide 13
Medium Energy Beam Transport
MEBT
Quadrupole: prototype completed
validated on a magnetic test bench
Magnetic test at ALBA/CELLS
Bunchers: 5-gap IH structure
Start of manufacturing in Dec-2012
Power tests planned in Aug-2013
Voltage EoLT = 350 kV
Cavity length < 350 mm
CW & pulsed mode operation
Scraper: manufacturing completed,
assembly & tests finished end March 2013
courtesy of AVS

## Slide 14
8 solenoid packages SC magnet (6 T) Steerers and BPM
SRF Linac
Cryomodule
8 resonators (=0.094) Tuning system Coaxial coupler
CEA (coord) CIEMAT

## Slide 15
Solenoid package
Solenoid and Coupler
Antenna
water-cooled
Tee Transition
water-cooled
Connection bellows with vacuum tank
Outer conductor GHe
4 K, vacuum
300 K, Patm
2 prototypes completed, tested when RF power
Source and test-bench will be available (April 2013)
Cold tests @4.2 K Quench at 260 A (210 A nominal)
Checked with steering coils
Test in horizontal position planned in Dec-2012

## Slide 16
Two cavity prototypes completed in Summer 2010, delivered in Sept'10
Original tuner design: relied on a capacitive plunger with a large membrane to allow an elastic deformation of ±1 mm
First troubles during cryogenic tests reported in May 2011
Superconducting Cavities
A0 plunger design
Nb plunger
Potential risks
high peak magnetic field at membrane center
Helicoflex gasket in region of significant field
NbTi flange: poor thermal conductivity
Fabrication issue: neck region contains two NbTi/Nb welds in a recessed area

## Slide 17
Given the rigidity of the resonator, this solution implies a lengthening of the cryomodule lattice  10 cm to ease the tuner integration between He tank & solenoid
Compression plunger
Following up the recommendations of a Review Panel (June '12) new design based on conventional compression tuner principle developed
Tuner only acts in one direction (compression)
Tuning force 8000 N / nose
Disengaged system during cooldown & warmup
niobium
He outlet
He inlet
beam axis
titanium

## Slide 18
Cavity qualification
Plunger port closed
Nb disk EB welded
P02 qualified  RF design of HWR therefore validated
Ex. membrane stress max 60.8 MPa < 150 MPa @4.4K
Cavity licensing (High Pressure Vessel)
stress analysis by an authorized engineering company
 all stresses allowable according to ASME code
Allowable stress S = Min [ Su / 4 ; Sy / 1.5 ]
internal P = 1.5 bar inside the He vessel @300K
internal P + load of 8 kN on beam flange @4.4K
LHe 1.5 bar max
8 kN / beam flange

## Slide 19
Diagnostics-Plate to characterize the beam
Bending magnet (20°) to avoid n-radiation in upstream elements
Magnetic beam expander to limit power density on BD < 200 kW/cm2
Lead shutter closed during beam shutdown to shield residual gamma rays from activated beam dump
Cryogenic pump
Cryogenic pump
HEBT Line & Beam Dump
Scraper to protect the last portion of the vacuum pipe in front of the beam dump
CIEMAT

## Slide 20
Polyethylene
shield
Iron shield
Water shield tanks
Cartridge
Inner & outer cones = Cu (edp)
Cooled by liquid water (high v, 3 bar)
T ~100 ºC not too far from boiling
Beam dump with its local shielding
water + polyethylene (neutron)
iron (gamma)
Remote disconnection system
Beam Dump
Cooling
pipes
cartridge
Inner Cu cone
Bellow
Articulated collar
CIEMAT

## Slide 21
Hydraulic circuit: to study the fluid-dynamics aspects
of the beam dump cooling (vibrations,heat transfer coef estimation, flow and pressure measurements,…)
HEBT & Beam Dump in final stage of detailed design
Cone prototypes built: electron beam welding and electro-deposition
Hydraulic test cooling circuit
Beam Dump prototypes and tests
Al mandrel
with Cu tip
SS flange
1.5m edp prototype
2.5m ebw prototype
demoulding
Contract notification in Summer 2013 for cartridge, BD tank & cooling system

## Slide 22
Beam Instrumentation
Diagnostics Plate
100 keV
5 MeV
9 MeV
Current monitors (ACCT, DCCT, FCT)
Beam Position monitors x 20
Beam Profile monitors (ionization & fluorescence)
Beam Loss monitors (ion chambers)
Micro-Loss monitors (diamond)
Bunch length monitor (Residual gas, GSI-like)
Interceptive: SEM grid + slits (Espread, Emit)
CEA-CIEMAT
End of procurement before end 2013 for all diagnostics

## Slide 23
Site preparation
Start of commissioning
Full Accelerator
Q2
Q3
Q4
Q1
Q2
Q3
Q4
Q1
Q2
Q3
Q4
Q1
Q2
Q3
Q4
Q1
Q2
Q3
Q4
Q1
Q2
Q3
Q4
Q1
2012
2013
2014
2015
2016
2017
Injector
RFQ
MEBT
SRF Linac
HEBT & BD
Diag RFQ
Diag SRF
RF Power systems
Cryoplant
LIPAc commissioning
End of BA Agreement
critical path
Sequence of installation & beam commissioning pulsed proton, deuteron, up to cw
Injector
RFQ + MEBT + D-Plate
Cryomodule + D-Plate + HEBT + BD
Full LIPAc
Installation & Commissioning

## Slide 24
Conclusions
INJECTOR (1st LIPAc accelerator component) has been delivered end of March 2013
RFQ planned to be delivered in October 2014, assuming end of RFQ modules fabrication in February 2014
But some other critical accelerator components deserve special attention to keep the schedule on track, as SC cavities and bunchers

## Slide 25
based on SRF technology
average beam current vs. energy
power  current  energy
IFMIF = multi-MW class hadron accelerator, but differently from other high power accelerators,
stands in the low energy (a few tens of MeV) and high intensity region
 high space charge regime with radio-activation hazard due to deuteron beam
Beam power landscape for hadrons accelerators

## Slide 26
END

## Slide 27
Beam Intensity: Large ACCT ( 178 mm) at the RFQ entrance with specific magnetic shielding
Beam Profile and species fraction (Doppler shift method): use of rad-hard CID cameras and CCD camera outside the vault with fiberscope
Emittance: Allison scanner to sustain 17 kW beam power
Space charge compensation: 4 Grid Analyzer to measure the energy of secondary ions or electrons repelled out of the beam
Bergoz
ACCT
BEAM
FGA design for IFMIF injector
Injector diagnostics

## Slide 28
Chopper addition
Need of pulsed mode with sharp rise/fall times (to limit transient current which would be lost downstream) with beam perfectly matched to the RFQ input conditions all along its duration
But ECR ion source: not able to produce such beam pulses RF cutting technique in the RFQ: could jeopardize the RFQ operation
electrostatic chopper located in the Injector LEBT (between the 2 solenoids)
In addition, this option enables the use of interceptive diags
Available port
EMU

## Slide 29
Principle: ionization of the residual gas
Residual gas pressure: few 10-8 to 10-5 mbar
Resolution ∼ 1 mm Profile rate ∼ few Hz
Apertures >10 cm for DP >15 cm for HEBT
      Test at GSI (5 MeV.A, mA)
IPM
A few Diagnostics…
Beam Profilers development
FPM
IPM in front of BD
Challenges: Large aperture (15× 15 cm2)
Radiation hardness ∼ 7 kSv/h (neutrons)
ceramic (HV + strip plates) field uniformity
Principle: fluorescence by interaction of the beam with the residual gas
2 read-out prototypes tested
    ICID (Intensified Charge Injection Device) camera (MCP + CID)
    PMT: multi anode 32 channels linear array
Campaign tests at CNA cyclotron Sevilla:
D+: 9 MeV and H+: 18 MeV
Extrapolation to LIPAc (125 mA) OK
new tests done at Sevilla (Oct 2011)
…improved profile measurements
ICID camera

## Slide 30
RF Power system
RF module (2 RF chains)
Prototype RF module (1 x 200kW) ready in March'13
First RF module (2 x 100kW) ready in May'13
Solid-state amplifier (16kW)) ready for buncher tests in August'13
RFQ
HWR
Bunchers
Prototype RF module (Oct'12)

## Slide 31
Cryoplant
PC (Power Coupler for cavity) CL (Curent Leads for solenoid)
Heat loads estimation
Process Flow Diagram
Procurement arrangement not yet signed, however
EDR uploaded and approved (end 2011)
Call for tender launched in October'12