## Slide 1
HOM couplers for CERN SPL cavities
Comparison of different design approaches
Work supported by the Wolfgang-Gentner-Programme of the Bundesministerium für Bildung und Forschung (BMBF)

## Slide 2: Outline
Overview
Design Requirements
Design Approaches
Heat Loss
Summary
Outlook

## Slide 3: Overview
PSB
SPS
Linac4
LP-SPL
PS
LHC /
HE-LHC
160 MeV
1.4 GeV
4 GeV
26 GeV
50 GeV
450 GeV
7 TeV
Linac2
50 MeV
Proton flux / Beam power
PS2
Present
Optional Future
1978
1975
1959
2008
LP-SPL: Low Power-Superconducting Proton Linac
PS2: High Energy PS (~ 5 to 50 GeV – 0.3 Hz)
HE-LHC: “High Energy” LHC (³ 14 TeV/ring)
PS2
SPL
LINAC4
SPS
PS
R. Garoby, SPL Seminar 2012

## Slide 4: Overview
RF Power Coupler
Bulk Niobium 5 Cells cavity
Helium Tank
CEA’s tuner
HOM Coupler
Bi-phase helium tube
Magnetic shielding
Inter-cavity support
Bellows
Double walled tube
O. Capatina, SPL Seminar 2012

## Slide 5: Overview
HOM-Coupler
Very high impedance for the notch frequency (704.4MHz)
Low impedance for “all” other modes
Extracted power
Resonant circuit
Antenna
Cavity
HOM-Coupler used to extract or dissipate unwanted, higher order modes in the cavity induced by the beam

## Slide 6: Design Requirements
Monopole modes with the highest R/Q1
1 M.Schuh, F. Gerigk. “Influence of higher order modes on the beam stability in the high power superconducting proton linac“, Phys. Rev. ST Accel. Beams, 2011
Dipole modes with the highest R/Q1
For SPL only the monopole modes are interesting
In case of recirculators or synchrotrons should be also considered
Schematic layout of the linac
(Conceptual design of the SPL II)
H- source
RFQ
chopper
DTL
CCDTL
PIMS
3 MeV
50 MeV
102 MeV
352.2 MHz
β=0.65
β=1.0
750 MeV
4/5 GeV
704.4 MHz
160 MeV

## Slide 7: Design Requirements
2 frequency regions relatively closed to each other
Narrowband coupler
Monopole modes with the highest R/Q1
1 M.Schuh, F. Gerigk. “Influence of higher order modes on the beam stability in the high power superconducting proton linac“, Phys. Rev. ST Accel. Beams, 2011
Schematic layout of the linac
(Conceptual design of the SPL II)
Chart:  = 0.65
| 1505 | 1511 | 1773 | 1780 | 1783
R/Q | 6 | 12 | 6 | 15 | 44
TM020,1/5
TM020,2/5
TM011,3/5
TM011,4/5
TM011,
Chart:  = 1.00
| 1322 | 1331 | 2087 | 2090 | 2449
 | 39 | 140 | 10 | 21 | 9
TM011,4/5
TM011,
TM021
TM022,
3 frequency regions which are widely spread
Broadband coupler or application of multiple couplers
H- source
RFQ
chopper
DTL
CCDTL
PIMS
3 MeV
50 MeV
102 MeV
352.2 MHz
β=0.65
β=1.0
750 MeV
4/5 GeV
704.4 MHz
160 MeV

## Slide 8: Design Approaches
Number of factors such as operational frequency, power dissipation, multipacting, field emission, surface resistance & heating evaluation as well as personal preference  different approaches
Beam pipe
Cavity
Hook coupler with additional inductive stub
2-inductive stub coupler (rescaled TESLA-style)
Broadband coupler with probe
Hook coupler

## Slide 9: Design Approaches
E- and H-field coupling
Notch inductance which together with the red labeled capacitance creates the notch filter
Notch capacitor couples to the outer conductor
Mutual inductance of the resonant circuits
fixing of the whole inner conductor
may support liquid helium for cooling
Capacitive coupling for impedance matching
Every part of the coupler (also the non labeled) affects more or less its frequency dependent impedance characteristic
Coaxial port (50 Ohm)
9

## Slide 10: Design Approaches
Initial estimation for design by transmission line models
Calculation of the lumped circuit elements for a desired frequency spectrum
Transformation in Transmission Lines gives the lengths of the coupler parts
Approximation
by lumped circuit model
Initial
design
10

## Slide 11: Transmission Line Model
Transmission Line Models reduce the problem to a few parameters
Fast and easy computation of the impedance characteristic (with e.g. Mathematica)
Only a rough estimation of the 3D-Model but helpful tool to provide a first design
Very useful to get an idea of the parametric dependencies
Subsequently the optimization will be done with CST MW, HFSS, …
11

## Slide 12: Transmission Line Model
Example for a parametric dependency (3D-Simulation and TML-Model)
Simplified 3D-Model
Splitted modes of the two coupled resonant circuits
Notch filter
l1
l1
l1
l1
l1
l1
l1
l1
TM01 - TEM (Narrowband type v2)
TML-Model

## Slide 13: Transmission Line Model
Circuit equivalents for the different design approaches
Notch filter
Narrowband coupler with hook
Broadband coupler with probe
2-Stub coupler (narrow/ broad)
1-Stub coupler (narrow)

## Slide 14: Narrowband Coupler with Hook
Optimization of the narrowband coupler for beta = 0.65
h1
h2
r0
l1
l2
l3
C1
Ct
M12
Design only suitable for small band width
In case of beta = 1.00 coupler could only be optimized for one frequency
Hook is difficult to cool
Notch filter
simplified model
model including beam pipe
1.5 mm distance
TM01 – TEM [dB]
TM01 – TEM [dB]

## Slide 15: Broadband Coupler with Probe
Larger bandwidth with 3 resonances
Sharper transition frequency region
Better to cool
Optimization of the broadband coupler for beta = 1.00
l1
l2
l4
C1
d
l3
l5
h1
M23
Notch filter
M12
model including beam pipe
simplified model
0.5 mm distance
TM01 – TEM [dB]
TM01 – TEM [dB]

## Slide 16: 2-Stub Coupler
Lower damping of the accelerating mode
Optimization of the 2-Stub coupler for beta = 1.00 (broadband)
l1
l2
C1
d
l3
hm
M23
M12
r

l1
l2
C1
d
l3
hm
M23
M12
r
Notch filter
Higher damping of the higher order modes (< 2.5 GHz)
0.5 mm distance
difficult to adjust
TM01 - TEM [dB]
TM01 - TEM [dB]

## Slide 17: Higher Order Filter
Previous designs not suitable for the first dipole band (sharper transition frequency region is required)
17
2 H. J. Blinchikoff, A. I. Zverev, “Filtering in the Time and Frequency Domain“, John Wiley & Sons New York, p. 107-111, 1976
Figure 2: lumped circuit of a n-th order low pass2
Figure 3: Attenuation of Butterworth filter of different order n2
1 A. I. Zverev, “Handbook of Filter Synthesis“, John Wiley & Sons New York, p. 68, 1967
Figure 1: Attenuation of some Chebyshev filter (n=5)1
Sharper transition frequency region at the costs of lower damping in stop band and higher damping in pass band
Sharper transition frequency region also possible by using filters of a higher order  more complex design
modes that are very closed to 704.4 MHz

## Slide 18: Higher Order Filter
18
1 A. Ainsworth, R. Calaga, et al., “HOM Coupler Optimisation for the Superconducting RF Cavities in ESS “, Proceedings of IPAC2012, 2012
2 W. Xu, .et al. , “New HOM coupler design for high current SRF cavity “, Proceedings of IPAC2012, 2012
double-notch effect by 2nd inductive stub
Increasing the order by using of an additional coupling inductance
This results also in a double-notch1,2 (no adjustment necessary)
TM01 - TEM

## Slide 19: Higher Order Filter
19
Together with a second capacitor the coupler achieve an appropriate broad band characteristic with sharp transition frequency region
monopole HOMs
dipole HOMs
TM01 - TEM
TE11 - TEM
optimized model
1.8 mm distance

## Slide 20: Higher Order Filter
20
In the same manner the broadband coupler can be modified
Transmission of monopole HOMs is higher (5 - 10dB)
monopole HOMs
dipole HOMs
TM01 - TEM
TE11 - TEM
optimized model
0.8 mm distance

## Slide 21: Heat Losses
H-Field of fundamental mode @ 704.4MHz as indicator for thermal losses
Surface resistant difficult to determine due to the residual resistant1,2 (tolerance range of +/-100%)
x 3500
Parameter | Tesla design | Broad band coupler | Hook coupler
Surface losses | 1.212 mW | 0.954 mW | 0.836 mW
Bmax | 9.2 mT | 9.0mT | 9.8mT
Emax | 11MV/m | 10.5MV/m | 9.5MV/m
G = 280 
Q0 = 5x109
Rs = 56 n
worst case estimation for fundamental mode
1 G. Ciovati, et al., “Residual Resistance Data From Cavity Production Projects at Jefferson Lab“, IEEE TRANSACTIONS ON APPLIED SUPERCONDUCTIVITY, 2011
2 T. Junginger, et al., “RF and Surface Properties of Superconducting Samples“, CERN-ATS-2011-037, 2011

## Slide 22: Heat Losses
Consideration of some higher order modes
mode | TM011,  | TE111, 3/5 | TE111, 4/5 | TM011,  | Hybrid
magnitudes of H-field |  |  |  |  | 
frequency | 704.4 MHz | 915 MHz | 940 MHz | 1331MHz | 1409 MHz
Bmax | 9.2 mT* | 0.108 | 0.093 | 0.045 | 0.016
surface loss | 96 W* | 87 x 10-6 | 58 x 10-6 | 5.65 x 10-9 | 0.39 x 10-6
output power | 14 mW* | 1 | 1 | 1 | 1
surface loss per 1W output | - | 87 W | 58 W | 0.016 W | 0.394 W
x 2000
Rs = 56 n
*scaled to 25MV/m and 4% duty cycle

## Slide 23: Summary
Hook coupler (1 inductive stubs)
Broadband coupler with probe
2-Stub coupler (narrow/ broad)
Double-notch designs
Small bandwidth
Maybe considered for medium beta cavities
Very sensitive to Multipacting1
Difficult for active cooling
Larger bandwidth (3 resonances)
Lower damping of HOMs
Preferred for high beta cavities
appropriate for active cooling
Very appropriate for cooling
Less sensitive to Multipacting1
adjustable Notch frequency
Can be realized with hook as well as with probe antenna
Notch filter with large band width
Sharp transition frequency region
More complex designs
1 S. Molloy, R. Ainsworth, R. Ruber,. “Multipacting Analysis for the Superconducting RF Cavity HOM Couplers in ESS“, Proceedings of IPAC2011, 2011

## Slide 24: Outlook
Thank you for your attention
Further designs will be considered
Coupled electromagnetic and thermodynamic simulations
Multipacting analysis
Mechanical design
Building of the first prototypes and experimental analysis