## Slide 1
Double Spoke Cavity b = 0.50 for ESS
(RF and) Mechanical Studies

## Slide 2
Contents
1. Description of the prototype
2. Static calculations
2.1 Analysis on different configurations
2.2 Finite Element Model for stress analysis
2.3 Static results
2.4 Mechanical vibration modes
3. RF-Mechanical coupled calculations
3.1 Finite Element Models
3.2 RF parameters
3.3 Sensitivity for cavity tuning
3.4 Helium bath pressure fluctuation
3.5 Lorentz forces detuning factor
3.6 Summary of the results
4. New optimizations (feedback from MYRRHA cavity design)
4.1 Critical pressure during cool down
4.2 Manufacturing of the cavity
5. Status about the prototypes fabrication

## Slide 3
1. Description of the prototype
  Cavity
    Material: Niobium
    Thickness: 4mm
  Donut at each end cup of the cavity
Needed for leak tests
  4 HPR ports on one end cup of the cavity
Better cleaning of the cavity
  Helium vessel
    Material: Titanium grade 2
    Thickness: 4mm
  Helium vessel made with standard dished end-cups
  Rings linking the cavity to the helium vessel
Reduce critical stress areas around the small ports
Reduce KP and KL
Donut
(left and right side)
4 HPR Ports
Pick-up Port
Ring
(left and right side)
Coupler port
Bellows
The fabrication of 3 prototypes with this geometry has started 1 month ago

## Slide 4
Leak tests during fabrication
  Bare cavity (=1st fabrication step)
  Cavity with its helium vessel (=Cavity completed)
Maintain stresses < 50 MPa
Test inside the cryomodule
  Cooling down at 4K
Define the critical pressure during cool down process
  Mechanical-vibration modes analysis
Check sensitivity to microphonics
  Frequency shift by pulling on beam tubes
Define the sensitivity for the tuning system
  Helium bath pressure fluctuation
  RF sensitivity due to the Lorentz forces
Define a range for the pressure and Lorentz detuning factors
2.1. Description of the different loaded cases
2. Static calculations
Bare cavity
Cavity + helium vessel
Cryomodule

## Slide 5
2.2 Finite element model for stress analysis
FEM model (Mechanical ANSYS V14):
  Cavity
  Helium vessel
  Meshed with shell elements
  Donut
  Ring
  4 HPR flanges
  2 Pick-up and coupler flanges
  Stiffeners of the helium vessel
  Blocks of the helium vessel
   Meshed with solid elements
Properties of materials (at room T°):
Niobium: Titanium:
E = 107 Gpa E = 105 GPa
n = 0,38 n = 0,3
r = 8570 kg/m3 r = 4510 kg/m3
Re = 50 MPa Re = 350 MPa
Rm = 125 MPa Rm = 460 MPa
1
6
2
7
8
3
4
5
2. Static calculations

## Slide 6
0.32mm
43 MPa (HPR port)
Case 1: Leak test
Case 2: Cooling down
0.15mm
34 Mpa (top of the Spoke bar)
 Critical pressure during the cooling down test:
Pcrit = 1,47 bar (smax = 34 MPa)
2.3 Static Results
37 MPa
(End cup)
2. Static calculations
Donut needed to get stresses on the cavity < 50 MPa:
(smax = 37 MPa)

## Slide 7
2.4 Mechanical-vibration modes
Boundary conditions: free-free
N° | Frequency | Mode
1 & 2 | 212Hz | Beam tube on CTS side
3 & 4 | 265Hz & 275Hz | Spoke bar/Helium vessel
5 & 6 | 285Hz | Coupled mode Cavity/Helium vessel
7 | 313Hz | Helium vessel
8 to 11 | 315Hz to 365Hz | Coupled mode Cavity/Helium vessel
12 | 396Hz | beam tubes
Mode 3: 265 Hz
Mode 1: 212 Hz
Mode 5: 285Hz
1st critical mode (mode 3) >> 50 Hz
Mode 12: 396Hz
2. Static calculations

## Slide 8
Mechanical FEM model:
Cavity
Helium vessel
 Meshed with shell elements
Donut
Rings
HPR Flanges
Stiffeners of the helium vessel
 Meshed with solid elements
3.1 Finite element models
Nota :
The shell elements of the cavity walls coincide with the faces of solid elements of the interior volume
All connections between components are realized with coincident nodes
Coupling mechanical and electromagnetic simulations with ANSYS V14 (Mechanical APDL & EMAG):
Hypothesis: 1 symmetry plane
Electromagnetic FEM model:
7. Inner volume of the cavity
 Meshed with solid elements (HF119)
3. RF-Mechanical coupled calculations

## Slide 9
3.2 RF Parameters
 | ANSYS
Frequency [MHz] | 351,76
Beta | 0.5
Bpk/Eacc [mT/(MV/m)] | 6,84
Epk/Eacc | 4.33
G [Ohm] | 127
r/Q [Ohms] | 424
Lacc = Ngap.b.l/2 [m] | 0.639
Temperature (K) | 2
Q0 Cu@ 300K | 26469
Q0 Nb@ 2K | 1.19*1010
3. RF-Mechanical coupled calculations

## Slide 10
3.3 RF Sensitivity for cavity tuning
Tuning sensitivity
f/z = 135 kHz/mm
Kcav = 20 kN/mm
311 MPa / mm
View of the Cold Tuning System in vertical position
3. RF-Mechanical coupled calculations
311 MPa
At 2K: the tuning range is +173 kHz (<-> 1.28 mm of max displacement not to exceed 400 MPa)

## Slide 11
3.4 Helium bath pressure fluctuation (1/3)
Free ends | -113.
Fixed ends | -18.
First case: Cavity without helium vessel
Free ends | +16.5
Fixed ends | +17.9
Second case: Cavity with helium vessel
Sensitivity to He pressure Kp [ Hz/mbar]:
2 boundary conditions
Sensitivity to He pressure Kp [ Hz/mbar]:
2 boundary conditions
P = 0
P = 1
P = 0
P = 0
P = 1
3. RF-Mechanical coupled calculations

## Slide 12
3.4 Helium bath pressure fluctuation (2/3)
Third case (cryomodule configuration taking into account the CTS stiffness):
One beam tube is free
(The end cup of helium vessel is welded to the beam tube)
The Cold Tuning System is fixed on the end cup of the helium vessel
The coupler port is fixed along the beam axis
Again, 2 boundary conditions:
Cavity without CTS (free ends)
The 2 beam tubes are free
Cavity with an infinitely stiff CTS (free – CTS stiffness)
The beam tube is linked to the CTS blocks (along the beam axis)
3. RF-Mechanical coupled calculations

## Slide 13
3.4 Helium bath pressure fluctuation (3/3)
Cavity without CTS
Cavity with infinitely stiff CTS
Sensitivity to He pressure KP [ Hz/mbar] (without CTS) | +16.5
Sensitivity to He pressure KP [ Hz/mbar] (with stiff CTS) | +26
Tuning sensitivity
f/z = 135 kHz/mm
Kcav = 20 kN/mm
Kp may be calculated as a function of the CTS stiffness:
With :
FEM result with a specific CTS stiffness
3. RF-Mechanical coupled calculations

## Slide 14
3.5 Lorentz forces detuning factor
Cavity without CTS
Cavity with infinitely rigid CTS
Tuning sensitivity
f/z = 135 kHz/mm
Kcav = 20 kN/mm
Kp may be calculated as a function of the CTS stiffness:
For 8MV/m |  | 
KL [Hz/(MV/m)2] (without CTS) | KL =-5.13 | f = -328 Hz
KL [Hz/(MV/m)2] (with CTS) | KL =-4.4 | f = -282 Hz
Radiation pressure in Pa for 8MV/m:
FEM result with a specific CTS stiffness
With :
3. RF-Mechanical coupled calculations

## Slide 15
3.6 Summary of the results
Main mechanical parameters of the prototype cavity |  | 
Thickness of the cavity walls | 4 mm | 
Critical pressure | 1.47 bar | 
Stiffness of the cavity | 20 kN/mm | 
Tuning sensitivity Df/Dz | 135 kHz/mm | 
Sensitivity to helium pressure fluctuation KP without CTS with CTS | +16.5 Hz/mbar +26.0 Hz/mbar | 
Lorentz forces detuning factor KL without CTS with CTS | -5.13 Hz/(MV/m)2 -4.4 Hz/(MV/m)2 | For 8MV/m: Df = -328 Hz Df = -282 Hz
3. RF-Mechanical coupled calculations

## Slide 16
4.1. Increasing the critical pressure at 4K
4. New optimizations
On the prototype : The maximum stresses are located at the top of the spoke bar
Option: stiffeners on the base of the spoke bar
18 MPa
Stiffeners
Critical pressure during operation: 1.47 bar  2.77 bar
34 MPa
Cavity stiffness [kN/mm] | 20
Tuning sensitivity [kHz/mm] | 135
KP [ Hz/mbar] Without CTS With CTS | +13.0 +23.9
KL [Hz/(MV/m)2] Without CTS With CTS | -5.10 -4.26

## Slide 17
4.2. To facilitate the manufacturing processes
On the prototype : The metal forming operations (spinning & deep drawing) with 4.2mm thick sheets are not straight forward processes.
Option: Reducing the thickness to 3mm while keeping new stiffeners at the top of the spoke bar
25 MPa
34 MPa
Critical pressure during operation : 1.47 bar  2 bar
Stiffeners
all niobium parts in 3mm
Cavity stiffness [kN/mm] | 10.5
Tuning sensitivity [kHz/mm] | 123
KP [ Hz/mbar] Without CTS With CTS | +22.5 +35.0
KL [Hz/(MV/m)2] Without CTS With CTS | -7.28 -6.05
4. New optimizations

## Slide 18
5. Status about the prototypes fabrication
Niobium material has been controlled at IPN. No problem shipment to manufacturers mid of May.
Fabrication of 3 prototypes (Start= mid of March):
a/ 1 cavity at SDMS (France)
b/ 2 cavities at ZANON (Italy)
Lead time: 13 months for both manufacturers. Delivery of all cavities in April 2014
Kick-off meetings: done beginning of April.
Intensive exchanges about technical “issues”:
  End-cups : in one or two pieces…
  Donut  new stiffener shape
  Stiffeners on the spokebase
  Beam tubes and central drifts: from sheets, blocks or tubes (pb of coaxiality and cavity-to-helium vessel junction)
  Spoke bar-to-cavity body junction: rounded shape