## Slide 1
H- Source: Challenges in Terms of Current and Emittance, Upgradability
Shixiang PENG
State Key Laboratory of Nuclear Science and Technology
Institute of Heavy Ion Physics
Peking University
Email: sxpeng@pku.edu.cn

## Slide 2: Contents
H- Source Research Motivation at PKU
Challenges in Terms of Current and Emittance, Upgradability
PKU 2.45GHz Microwave Driven Cs-free Volume H- Sources
Summary and Prospect

## Slide 3
Layout of Tsinghua advanced proton source(Xi’PAF)
Purpose
Study of Space Radiation Effects, Medical Application…
Main parameter
Energy range: 60~230 MeV
Intensity: 2×1011 ppp
Subsystem parameter
H- Source : 50 keV/10 mA
rms:< 0.2 π·mm·mrad
Time schedule: 100Hz/1ms
Cs-free type
RFQ: 3 MeV
DTL: 7 MeV
Synchrotron: 60~230 MeV
G.R. Li, etc., The 12th Symposium on Accelerator Physics,15 August 2014, Lanzhou University
                Research Motivation(1)

## Slide 4
PET trace Cyclotron (External H- ion source)
Facility Requirement:
H- ion beam: 5mA/30keV
Normalized 4 rms emittance of < 0.6  mm mrad.
Beam operation mode: CW
Source structure: Cs-free
Source size: the smaller the better.
                Research Motivation(2)
PET: Positron Emission Computed Tomography

## Slide 5: Contents
H- Source Research Motivation at PKU
Challenges in Terms of Current and Emittance, Upgradability
PKU 2.45GHz Microwave Driven Cs-free Volume H- Sources
Summary and Prospect

## Slide 6: ·
Magnetron
(FNAL, BNL, ANL, DESY)
Penning Source
(RAL, CSNS)
Surface conversion
(LANL, KEK)
Filament-driven
(TRIUMF, Jyväskylä, J-PARC, CIEA)
RF-driven
(DESY,SNS,CERN)
H- Sources for Accelerators
Surface Production
Volume production
H-
Challenges
Current
Emittance
High Duty factor & Its Variable
Power efficiency
Lifetime
…
ECR-driven volume ?

## Slide 7
Lab | Source type | Cs | Current (mA) | Pulse length(ms) | Rep Rate (Hz) | Duty Factor(%) | Normalized Emittance | Power Efficiency(mA/kW)
Fermi | Magnetron Multicusp W-filam. | Yes No | ~80 5~10 | 0.1 CW | 15 CW | 0.15 100 | 0.3 - - | 50 1
BNL | magnetron | Yes | ~100 | 0.6 | 10 | 0.4-1 | 0.4 | 67
ISIS CSNS | Penning | Yes Yes | ~60 ~50 | 1 0.5 | 50 25 | 5 1.25 | 0.7 0.5 | 6 --
DESY | Multicusp ext. RF | No | 80 | 0.15 | 8 | 0.12 | 0.26 | 2
LINAC4 | Multicusp ext. RF | Yes | 50 | 0.4 | 0.8 | 0.03 | 0.3 | 1.1
J-PARC | Multicusp LaB6 filam. Multicusp int. RF | No Yes | 30 80 | 0.5 0.5 | 25 25 | 1.25 1.25 | 0.18 0.3 | 2
KEK LANL | Multicups Surface Convertor | Yes | 18 |  |  | 12 | -- | 3
SNS | Multicusp int. RF Multicusp ext. RF | Yes Yes | 41 50 | 1 1 | 60 60 | 6 6 | 0.26 0.2 | 1.6
JAERI | Multicusp W-filament | Yes | 60 | 1 | 50 | 5 | 0.23 | 2
TRIUMF CIEA/… | Multicusp- Filament | Yes Yes | 20 18 | CW CW | CW CW | 100 100 | 0.7 0.77 | 3 5
CEA | ECR | No | 3.5 | 1 | 10 | 1 |  | 
H- Ion source around the world
Acknowledgement
T. Roser(BNL), J. Lettry(CERN), T. Rutter, D. Faircloth & S. Lawrie(ISIS, RAL), M. P. Stockli & R.F Welton(SNS) ，Y. Belchenko, A. Ueno (J-PARC), H.F. Oyang(CSNS), D. Bollinger(FNAL), X.L. Jia(CIEA), H. Etoh(JAEA), R. Gobin(CEA/Saclay),V. Dudnikov……

## Slide 8
COURTESY Dan Faircloth, RAL
RAL Penning Source

## Slide 9
SNS RF Driven Volume H- Source
60mA, 6%，Cs-seeded
: 0.26pi.mm.mrad
RF Power: ~60kW
Antenna lifetime: Several weeks
Internal Antenna Source
filter magnets
H- beam
dumping magnet
RF antenna
multicusp magnets
Gas inlet
plasma
view port
Cs collar
e-dump
COURTESY M. Stockli, SNS

## Slide 10
SNS RF Driven Volume H- Source
RSI 87, 02B146 (2016)
External Antenna Source
50 mA, 6%,
Cs-seeded
Cs- seeded
RF Power: 50-60 kW
COURTESY R. Welton, SNS

## Slide 11
80 mA
0.12 %  6%
: 0.25pi.mm.mrad
35 keV
RF: ~30kW
NO Cs
Jens Peters, DESY
DESY RF Driven Volume H- Source


## Slide 12
CERN RF Driven Volume H- Source
Courtesy Jacques Lettry, CERN
50 mA
0.1 %
RF Power: ~45kW
norm, rms: 0.34pi.mm.mrad

## Slide 13
Horst Klein (20th ICFA Workshop summary).
All about H- ion Source
“The ion sources, and especially the H- sources, are still somewhat a black magic. ……Concerning the different types of ion sources, I think the most promising candidates for H- are the Penning ion source and the volume source (Large Volume SPS). The ECR source may be a hope for the future”.
Intuition and hand experience are important components for H- sources development.
A learning period for new team is ~8 years.

## Slide 14: Contents
H- Source Research Motivation at PKU
Challenges in Terms of Current and Emittance, Upgradability
PKU 2.45GHz Microwave Driven Cs-free Volume H- Sources
Summary and Prospect

## Slide 15: PKU 2.45 GHz PMECR H+ Ion Source
Pulsed mode
Standard 2.45GHz PMECR Ion Source
130mA@50kV 6mm
Stability of CW H+ beam
294.6 h
@103h,CEA/Saclay
  53.8mA@50kV
  6mm
  RF power 500 W
*Shi-Xiang Peng, et al., Chinese Physics B, Summited (2016/8)
Ion | H+ | D+ | He+ | O+
I(mA) | 130 | 83 | 65 | 70
Project | DWA/CIADS | PKUNIFTY | Coupled RFQ | SFRFQ

## Slide 16
PKU Cluster H2+/ H3+ ECR Ion Source [1]
Cluster Source
H2+ 42mA(20mA[2]), 54%
H3+ 20mA (2.9mA[3]), 55%
Yuan Xu et al., Rev. Sci. Instrum. 85, 02A943 (2014).
R. Miracoli et al., Rev. Sci. Instrum. 83, 02A305 (2012).
N. Joshi, M. Droba, O. Meusel, U. Ratzinger, NIM A 606 310–313 (2009).

## Slide 17
                Cross Section of H- Generation Process
Jens PETERS, ICIS 07, August 26-31, 2007, Jeju, Korea

## Slide 18
Cs or Cs-free
Electron generation or heating (RF/Filament/ ECR)
Electron selection filter
Gas distribution
Collar in cold region
Liner material
Electron co-extraction suppressing
RF Breakup before cold region
Plasma bias
Extraction system structure
Space charge effect
…
                Topics for a Volume H- Source Design

## Slide 19
Haitao Ren, Shixiang Peng*, MOPFI034, Proceeding of IPAC13, Shanghai, China, May 12-17, 2013: 360-362.
100mA@50kV H+
Prototype source
1)Prototype H- Source 2012/10/28 - 2012/11/7
PKU Microwave Driven Cs-free H- Sources

## Slide 20
Operation parameters
Pressure 4.6  10-3 Pa
FR power 4.58 kV  41 mA
Time Schedule 166Hz/1 ms
Plasma Electrode：-35kV
Second Electrode: 2kV
Current at FC1：12 mA
Results from Prototype H- Source
Operation parameters
Pressure 4.6  10-3 Pa
FR power 4.58 kV  41 mA
Time Schedule 166Hz/1 ms
Plasma Electrode：-40kV
Second Electrode: 2.1kV
Current at FC1：15 mA
Extracted at 35kV
H- Beam
Trigger Signal
12mA
Extracted at 40kV
H- Beam
Trigger Signal
15mA
RF:2.8kW

## Slide 21
Unfinished missions and Lessons learned
E-dump - B Field configuration and its location;
Sparks elimination - extraction system with water cooled, suitable material for electrodes and its protection;
RF Breakup method- W-grid will be the weakest part inside the source body;
Higher Current and Higher Efficiency and the Source Stability, etc.
No Emittance Results
No CW H- Beam
No long term test
…

## Slide 22
2) Formal H- Source (since 2013/3)
S. X. Peng*, Y. Xu, H. T. Ren, etc. WEPWA027, IPAC2015, Virginia, May 3-8, 2015
S. X. Peng*, H. T. Ren, Y. Xu, etc. AIP Conference Proceedings 1655, 070005 (2015)
S. X. Peng*, T. Zhang, H. T. Ren, etc. Rev. Sci. Instrum. 87, 02B125 (2016)

## Slide 23
H- Source Bodies and their best results (Before Sept. 2015)
No.1
No. 4
No. 3
No. 2
High Voltage Region
230mm
Source Number |  | No.1 | No.2 | No.3 | No.4
Water Cooling | RF Window | No | Yes | Yes | Yes
 | Plasma Chamber | Poor | Yes | Yes | Yes
 | Connection Flange | No | No | Yes | Yes
 | Extraction | No | Poor | Yes | Yes
E-Dump Position |  | I | II | II | I
Current (mA) | CW | 8 | 10.8 | 25 | 29
 | Pulsed(100Hz/1ms) | 16 | 20 | 35 | 45

## Slide 24: Best Results from PKU H- Source
CW Mode
Parameter
RF power 1000 W
Pressure 4.0E-3 Pa
Ex. Voltage -35 kV
Sec. Voltage 2 kV
Ratio of H-/e: 4.7
H- current: 29mA
Power efficiency: 29 mA/kW
RMS,norm：0.18 pi.mm.mrad
Pulsed Mode Parameter
Pulsed 100Hz/1ms
RF(Peak) 2100 W
Pressure 4.5E-3 Pa
Voltage -35 kV
Second 2kV
Ratio of H-/e: 4.4
H- current: 45mA
Power efficiency:21.4 mA/kW
RMS,norm : 0.16 pi.mm.mrad
High Voltage Region
230mm

## Slide 25
Duty factor | H- (mA) | Power Efficiency(mA/kW)
20% (1ms+4ms) | 35 | 19.4
14.3%(1ms+6ms) | 34 | 18.9
10%(1ms+9ms) | 35 | 19.4
5%(1ms+19ms) | 34.2 | 19
3.3%(1ms+29ms) | 33 | 18.3
2%(1ms+49ms) | 30.5 | 16.9
1%(1ms+99ms) | 29 | 16.1
Duty Factor Variation Possibility
Peak RF Power :
1800W
No.3
No.4

## Slide 26: Summary and Prospect
RF driven Volume H- source can produce several tens mA beam at low duty factor(<6%). Several ones are used to deliver beams for accelerators. They need tens kW RF power.
Filament driven source was the only one that can produce 20 mA CW H- beam in the world. Lifetime of the filament is an important issue for discussion.
Penning source has been developed at RAL that can produce 60 mA H- beam with duty factor of 5%. Current and lifetime are still needed to be improved.
At PKU, 2.45Microwave driven H- sources were developed.
CW mode: 29 mA at 35kV. Power efficiency: 29 mA/kW. norm, RMS: 0.18 .mm.mrad.
Pulsed Mode: 100Hz/1ms, 45 mA at 35 kV. Power efficiency: 21 mA/kW； norm, RMS: 0.16 .mm.mrad.
Operation duty factor can be easily changed from 1% to 100%.

## Slide 27
Improvements, such as plasma electrode bias, Diamond like material liner, etc., will be done for higher current.
Long term operation test will be done in the future.
……
Next Step

## Slide 28
28
Thank you for your attention!
谢谢关注！