## Slide 1
Characterization of a
high intensity beam
P. A. P. NGHIEM
N. CHAUVIN, L. Ducrot, W. SIMEONI Jr., M. VALETTE, D. URIOT
ESS workshop: "Upgrading Existing High Power Proton Linacs", Nov 8-9th, 2016

## Slide 2
More particles
Higher space charge and power
 109 particles  6 109 parameters
 huge number
RMS e, a, b (,g)
Not enough !!
Distribution dependent
The two classical ways
Classically
Coordinates 105-6 particles in 6D phase space
 106 parameters
 very big number  num. simulations
Concentration ellipse
RMS e, a, b (,g)
 3 global parameters
High intensity

## Slide 3
Beam Optimization
Smaller emittance: Bigger size
Bigger emittance: Smaller size
Example: IFMIF SRF Linac (Laser Part. Beams 32, 10-118, 2014)

## Slide 4
HEBT entrance
exactly same a,b,g,e
3.5 m downstream
through 3 quadrupoles:
significantly different beam outputs
a,b,g,e
"Nominal" distribution
Gaussian distribution
Beam transport

## Slide 5
Beam Characterization
For high intensity beam
1) Characterize the beam by its actual number of particles
2) Characterize the beam by its projections onto a few axes
3) Characterize the beam by its core and halo separately

## Slide 6
1. Beam characterization
by the actual number of particles

## Slide 7
PCs
Linux / Windows / Mac
Multi-core or not
Cluster(s)
Cloud / LHC grid
TraceWin code
Principle : share simulations on many computers
Massive simulations (1)
Roscoff 2015

## Slide 8
For IFMIF-LIPAc, D+, 125 mA CW, 40 MeV
Actual number of particles: 5 109
 170 processors for 25 days, storing 38 To
 confirm losses < 10-7
 representative statistics of microlosses
Massive simulations (2)
(WEPOY032, IPAC'16)
Phase spaces on the beam dump (1.1 MW)
Share particles on many computers
Losses (W) along accelerator
zoom

## Slide 9
Massive simulations (3)
Share linacs on many computers, for error studies
Consequences of cavity errors (1°, 1%) on losses
for SPIRAL2, D+, 5 mA CW, 40 MeV
2.5 106particles, number of linacs: 1000
 150 processors for 7 days
 Losses due to RFQ: 30%, due to cavity errors:70%
Cumulative results of 1000 linacs

## Slide 10
Massive simulations (4)
Allow very precise and detailed analyse of certain physical phenomena:
Halo formation and evolution
Microloss location (10-6 of the beam)
More and more realistic beam transport
Need very fine description of optics elements, realistic input particle distribution

## Slide 11
2. Beam characterization
by its projections onto a few axes

## Slide 12
Beam Characterization
by projections on a few axes (1)
Objective: Reconstructing the whole distribution from
the only knowledge of its projections onto a few axes
Add supplementary hypothesis: where there is no data,
the shape is the most regular possible
 the dist. can be described by the least number of parameters
 the dist. should have a Maximum ENTropy  MENT
MENT method thoroughly developed in
G. Minerbo, Computer Graphics and Image Processing 10, 48-68 (1979)
then currently used in e.g.
C.T. Mottershead, IEEE Transactions on Nuclear Science NS-32 (1985)
D. Reggiani & M. Seidel, Proc. of IPAC'10, MOPE065, Kyoto, Japan (2010)
K.M. Hock et al., Nucl. Instru. Meth. Phys. Res. A 642, 36-44 (2011)
K.M. Hock et al., Nucl. Instru. Meth. Phys. Res. A 753, 38-55 (2014)
Quick convergence, in less than 5 iterations

## Slide 13
Beam Characterization
by projections on a few axes (2)
For correctly describing a given beam, the questions are:
- what is the minimum number of projections ?
- which projections to consider ?
We recommend:
1) Reconstruct the distribution with 4 axes regularly
positioned within 360°, i.e. 0°, 45°, 90° and 135°.
2) Calculate the concentration ellipse of the obtained distribution
then determine its axis angle q and aperture dq
3) Reconstruct finally the distribution with projection axes
regularly positioned within q ± dq,
and the same number of axes perpendicular to those ones.

## Slide 14
Beam Characterization
by projections on a few axes (3)
IFMIF-LIPAc MEBT exit
2 projections
4 projections
6 projections
Actual distribution
Projections within 360°
Projections
within
-57° ± 15°
and ⊥

## Slide 15
Beam Characterization
by projections on a few axes (4)
IFMIF-LIPAc SC-Linac exit
2 projections
4 projections
6 projections
Actual distribution
Projections within 360°
Projections
within
-6,1° ± 22,8°
and ⊥

## Slide 16
Beam Characterization
by projections on a few axes (5)
Reconstruct a distribution from its projections  MENT method:
Projection axes correctly chosen in direction and angle range
 ~ 2 projections are enough for describing the core
 ~ 6 projections are enough for describing inaddition the external parts
 ~ 10 - 30 parameters for 2D
BUT: how to go to 4D, 6D ?
MOPOR032, IPAC'16

## Slide 17
3. Beam characterization
by its core and halo separately

## Slide 18
Beam Characterization
by Core and Halo (1)
Further reduce the number of parameters :
describe the beam by the global characteristics of its CORE and its HALO separately
Fine details are lost BUT more insight in physics of the beam
High intensity beam : competition of internal forces (space charge)
and external forces (focusing)
Result: growth or decay of Core or Halo

## Slide 19
For 1D: Core-Halo limit based on density profile
Extreme case:
Core: uniform, sc force strictly linear
Halo: tenuous, sc force nonlinear
 core-halo limit: very steep (infinite)
variation of the slope
General case:
Continuously varying density
Core-Halo limit: steepest variation of
the slope  max of 2nd derivative
 Core & Halo are submitted to two
different space charge force regimes
Appl. Phys. Lett. 104, 074109, 2014
Phys. Plasmas 22, 083115, 2015: This core-halo limit ≡ good indicator of beam internal dynamics
Beam Characterization
by Core and Halo (2)

## Slide 20
Beam Characterization
by Core and Halo (3)
Example: Beam along the IFMIF prototype accelerator

## Slide 21
Beam Characterization
by Core and Halo (4)
Example: Beam along the IFMIF Prototype accelerator
Classically
Advanced
PHS
PHP

## Slide 22
Beam Characterization
by Core and Halo (5)
MOPWA010, IPAC'15: Extension to 2D
"Wheel algorithm": Max of second derivative
along many sections
Core-Halo limit contour
PHS, PHP
Emittance e and Twiss parameters a, b, g
of the core and the halo separately
THPMR014, IPAC'16:
This Core-Halo limit contour is consistent
with the well-established halo formation dynamics

## Slide 23
Beam Characterization
by Core and Halo (6)
Classically
Advanced

## Slide 24
Summary
Characterization of high intensity beam:
1) By the actual number of particles
precise and detailed description of halo formation, microlosses
but needs massive simulations and more realistic input distribution
2) By projections onto a few axes
truththful description of 2D distribution with reasonable number of parameters
but how to go to 4D, 6D ?
3) By global properties of the Core and the Halo separately
more insight in physical properties of the beam
but compared to above methods, fine details are lost

## Slide 25
Extra

## Slide 26
Two different beams...

## Slide 27
e = 3.30, a = -0.40, b = 0.95
e = 3.30, a = -0.40, b = 0.96
Same Emittance but different Halos

## Slide 28
PHS=90.1% PHP=30.9%
PHS=28.9% PHP=3.2%
e a b
Global 3.30 -0.40 0.96
Core 3.15 -0.41 1.00
Halo 8.95 -0.46 1.00
e a b
Global 3.31 -0.40 0.95
Core 1.40 -0.39 1.01
Halo 7.56 -0.40 0.93