## Slide 1: Linac Upgrade Scenarios for the ISIS Spallation Neutron Source
Upgrading Existing High Power Proton Linacs Workshop
08.11.2016, ESS, Lund
Ciprian Plostinar, STFC

## Slide 2: Overview
Can the accelerating gradient be increased?
Can the beam current be increased?
Can the beam energy be increased?

## Slide 3: ISIS @ RAL

## Slide 4: ISIS @ RAL
Inaugurated in 1984
Accelerator:
  H- Ion Source
  70 MeV Linac, 202.5 MHz
  800 MeV proton synchrotron
~230 μA (2.9*10^13 ppp)
50 Hz, 184 kW
  148 kW to TS-1 (40 Hz)
  36 kW to TS-2 (10 Hz)

## Slide 5: ISIS @ RAL

## Slide 6: ISIS @ RAL
Some “Recycled” Components
ISIS was originally expected to have an operational lifetime of 20 years
ISIS is the prototype for modern spallation facilities
Its scientific success will probably double its lifetime
  Neutron demand from users
  Maintenance, refurbishment, investment
    Short/Medium Term Upgrades
    Medium/Long Term Upgrades

## Slide 7: The ISIS Linac
H- Source
LEBT
RFQ
DTL
202.5 MHz
35 keV
665 keV
~70 MeV
HEDS
Ion Species | H- | 
Energy | 70.4 | MeV
Frequency | 202.5 | MHz
Pulse Length | 200-250 | μs
Peak Current | 25 | mA
Repetition Rate | 50 | Hz
Duty Cycle | 1-1.25 | %
Total Length | 55 | m

## Slide 8: The ISIS DTL
 |  | Tank 1 | Tank 2 | Tank3 | Tank4
Input Energy | MeV | 0.6647 | 9.90 | 30.4 | 49.7
Output Energy | MeV | 9.90 | 30.4 | 49.7 | 70.4
Accelerating Gradient (E0) | MV/m | 1.6 – 2.2 | 2.45 – 2. 55 | 2.3 – 2.4 | 2.6
Synchronous Phase | Deg | -30 | -30 | -30 | -30
Max. Surface Electric Field | Kilpatrick | 0.67 | 0.81 | 0.84 | 0.87
Number of Cells |  | 56 | 41 | 27 | 24
Tank Diameter | cm | 93.4 | 92.71 | 81.28 | 88
Drift Tube Diameter | cm | 18 | 17.78 | 17.78 | 16
Aperture Diameter | cm | 2.5 | 3.81 | 3.81 | 3
Stems/Cell |  | 1 | 2 | 2 | 1
Total Length | m | 7.15 | 11.95 | 11.25 | 12.1
7.15m
11.95m
11.25m
12.1m
9.9 MeV
30.4 MeV
49.7 MeV
70.4 MeV
665 keV
Tank 1
Tank 2
Tank 3
Tank 4

## Slide 13: Short/Medium Term: Tank 4 Replacement
50 – 70 MeV, 12 m
Manufactured in the 1970s
  Showing its age
  Maintenance almost impossible
Replacement effort underway
  Prevent catastrophic failure
  Like for like
  Higher accelerating field (Kilp=0.87) and output energy would have required an injection upgrade as well

## Slide 14: Short/Medium Term: Tank 4 Replacement

## Slide 15: Short/Medium Term: Tank 4 Replacement
A complete 2m section has been built
  Re-engineered for better access (6x2m sections)

## Slide 16: Short/Medium Term: New MEBT
RFQ to DTL beam mismatch
~20% beam loss in Tank1.

## Slide 17: Short/Medium Term: New MEBT
New MEBT Layout with chopper
Would allow increasing beam current to ~30 mA
  RF systems can cope

## Slide 18: Long Term Plans: Two Linac Upgrade Options
180 MeV Normal Conducting
800 MeV Superconducting

## Slide 19: 180 MeV Linac
Ion Species | H- | 
Output Energy | 180 | MeV
Frequency | 324/648 | MHz
Pulse Length | 0.1 – 1 | ms
Peak Current | 60 | mA
Repetition Rate | 50 | Hz
Duty Cycle | 0.5 – 5 | %
Average Beam Power | 54 - 540 | kW
Accelerating Structures | RFQ, DTL, CCL | 
Accelerator Length | ~99 | m

## Slide 20: 180 MeV Linac

## Slide 21: 180 MeV Linac

## Slide 22: 180 MeV Linac

## Slide 23: 180 MeV Linac

## Slide 24: 800 MeV Linac
Ion Species | H- | 
Output Energy | 800 | MeV
Frequency | 324/648 | MHz
Pulse Length | 0.1 – 1 | ms
Peak Current | 60 | mA
Repetition Rate | 50 | Hz
Duty Cycle | 0.5 – 5 | %
Average Beam Power | 240 - 2400 | kW
Accelerating Structures | RFQ, DTL, CCL, SCL | 
Accelerator Length | ~244 | m

## Slide 25: 800 MeV Linac

## Slide 26: 800 MeV Linac

## Slide 27: 800 MeV Linac

## Slide 28
Conclusions
Can the accelerating gradient be increased?
  Current machine: No/Maybe* - Tank4
  Upgrade machines: Yes
Can the beam current be increased?
  Current machine: Yes
  Upgrade machines: Yes
Can the beam energy be increased?
  Current machine: No/Maybe* - Tank4
  Upgrade machines: Yes