Accelerator techniques

Project work

## Starting conditions:

An accelerator laboratory is built for 123-I and 18-F production. The cyclotron will be bought from a commercial supplier. The beam will be guided to two different production targets.

### Known parameters:

| Particles |  | H-, D- |
| --- | --- | --- |
| Beam energy |  | 30 MeV, 15 MeV |
| Beam intensity |  | 300 A, 150 A |
| Emittance at cyclotron exit | Horizontal, vertical | 5  mm mrad, 10  mm mrad |
| Beam width at cyclotron exit | Horizontal, vertical | 2 mm, 3 mm |
| Orientation of emittance ellipse at cyclotron exit |  | Upright |
| Cooling water temperature |  | 20 oC |
| Max pressure drop of cooling water |  | 6 bar |
| Beam diameter at target |  | < 10 mm |

### Task:

Design the ionoptical elements needed for beam transport

- Geometrical dimensions

  - Length/bending radius

  - Apertures

- Coils

  - Conductor

  - Dimensions of coils

  - Cooling

    - Max temperature rise 20 oC

  - Power supply parameters (current voltage)

# Text boxes

10 m

10 m

10 m

Target

Cyclotron

60 o