## Slide 1: Gamma Blockers Kick-off Meeting Technical System Scope
Iñigo Alonso
Linac Integration Section
www.europeanspallationsource.se
9 November 2016

## Slide 2: Outline
Purpose
Requirements
  Level 3 (from the SoW)
  Level 4 (proposal)
Components
Interfaces
Other stakeholders’ needs
References from SNS

## Slide 3: Purpose
"Absorb gamma radiation from the target or beam dump, during maintenance periods."
Minimize, at least to the levels described in the "ESS hands on maintenance conditions" document (ESS-0008351), the ambient residual dose rates to which maintenance workers would be exposed while working on components that would in the absence of the gamma blocker element have a direct line of sight to the target/dump.
Notes: Other means of minimizing the backshine radiation during maintenance would be: the reduction of the source's strength (this is given by the irradiation and cooling times), the reduction of exposure times (determined by the maintenance procedures), or increasing the separation between source and workers/components (not possible, set by the lattice design).
An improper design could actually make the situation worse, if the radiation coming from the target/dump interacts with the gamma blocker core material and creates secondary radiation that could be absorbed more readily by the workers (any gamma blocker will increase the dose rate in the tunnel by creating a new transverse radiation field).

## Slide 4: High level requirements (L3)
Name | A2T unit | DMPL Unit
Protection from gamma back-shine during maintenance | A gamma blocker shall be used during equipment maintenance periods to reduce the back shine gamma radiation from the activated target wheel. | A gamma blocker shall be used during equipment maintenance periods to reduce the back shine gamma radiation from the activated tuning dump.
Gamma blocker location | The gamma blocker shall be located as close as it is mechanically possible to the Neutron Shield Wall (NSW). Maintainability and inspectability should be considered. | The gamma blocker shall be located as close as it is mechanically possible to the outside shielding wall of the tuning dump vault. Maintainability and inspectability should be considered.
Hands on maintenance | The gamma blocker shall be designed to achieve hands-on maintenance levels of dose equivalent rate in the beam line components of the A2T section upstream of the gamma blocker. The hands on maintenance levels are described in ESS-0008351. | The gamma blocker shall be designed to achieve hands-on maintenance levels of dose equivalent rate in the beam line components of the Dump Line section upstream of the gamma blocker. The hands on maintenance levels are described in ESS-0008351.

## Slide 5: Proposed L4 requirements
Name | Text | Clarification
Gamma Blocker Positions | The gamma blocker core shall have two positions: In and Out. | "In" means coaxial to the surrounding beam pipe, "Out" means at the resting position away from the beam path. No intermediate positions are valid.
Core Diameter | The gamma blocker core diameter shall be at least the same as the internal diameter of its surrounding beam pipe. | 
Gamma Blocker Resting Position | When in the "Out" position, the gamma blocker core shall allow for a full free aperture of at least the same diameter as the internal diameter of its surrounding beam pipe. | 
Gamma Blocker Life Time | The gamma blocker shall be operable within the specifications for at least 45 years under the operational Radiation, Temperature, and Humidity Conditions. | This implies the usage of materials that are compatible with the foreseen operational conditions.

## Slide 6: Proposed L4 requirements (continued)
Name | Text | Clarification
Temperature Conditions | The gamma blocker shall meet its requirements under the nominal tunnel temperature conditions of 22.5±7 °C. | 
Humidity Conditions | The gamma blocker shall meet its requirements under the nominal tunnel humidity conditions based on a dew point temperature of 16 °C. | 
Maximum Mechanical Length | Maximum mechanical length of the gamma blocker shall be less than 500 mm. | Length in the direction longitudinal to the beam pipe.
Gamma Blocker Cooling | The gamma blocker shall be air cooled. | Fully passive heat transfer to air.
Lifelong lubrication of moving parts | The moving parts of the actuator shall not need further lubrication once installed for the lifetime of the gamma blocker. | 
End of stroke sensors | The gamma blocker shall have end of stroke sensors in both ends of the stroke. | Also known as limit switches.
Fail-safe mode | The gamma blocker shall remain in its current position in case of a failure of the actuator or its power supply. | "Fail-as-is": If the device is inserted it should remain inserted, if it is retracted, it should remain retracted.

## Slide 7: Components
There will be two Gamma Blockers:
  One in the A2T section, before the NSW
  One in the Dump Line section, in front of the Tuning Dump
The Gamma Blockers include:
  A sliding core,
  a vacuum chamber,
  CF beam line flanges,
  actuator(s),
  interfaces to controls/PSS/MPS
The complete systems will include:
  The GBs themselves,
  their stands,
  cables and power supplies, if needed.

## Slide 8: Interfaces
Vacuum
Controls/MPS/PSS
Site Infrastructure
  Supports
  Pneumatic connector if needed
Survey and Alignment
  Fiducials

## Slide 9: Other stakeholders’ needs
Stakeholder | Need/Expectation/Objective
Installation | Fits in the tunnel and in the installation schedule
Operations | Is part of the procedures
RAMI | Simplicity in design: leads to less failures
RAMI | The actions required to use them (insert, extract, lock...) should not interfere in the maintenance, start-up or any other activity. GBs actions should not increase the length of these regular activities.
RAMI | Maintenance to any of the components of the GBs should be possible to be done easily and in a short period of time.
RAMI | Fail-safe system, in case of failure: If beam on: stay out, if no beam: stay in, if during action: stay put and wait for manual action
Conventional Safety | No electrical hazards
Conventional Safety | No moving parts hazards

## Slide 10: References from SNS
Section 3.2.3.10.3 (Gamma blockers) in the FSAD-PF (Spallation Neutron Source Final Safety Assessment Document for Proton Facilities 102030103-ES0018-R02, page 3-53), emphasis not in the original:
  Components inside the injection dump and the target become activated during normal operation. Gamma radiation from these activated components can shine back down the flight tube when the accelerator is shut down. To minimize gamma dose rates for workers in the applicable tunnel segments, gamma blockers have been installed as an ALARA measure in the vacuum pipe near the injection dump in the Ring tunnel and at the end of the RTBT.
  Each gamma blocker consists of a vacuum chamber containing a metal cylinder that is rolled in and out of the beam path via pneumatic cylinders. These actuators are controlled by the PPS. When the tunnel is accessible, the respective gamma blocker is rolled into the beam path. When personnel are excluded from the tunnel, the PPS rolls the gamma blocker out of the way, allowing beam operation. The design of the gamma blocker results in a “fail-as-is” design. On loss of air or power, the gamma blocker stays in the last position.
  The inserted and retracted position of the gamma blocker is monitored by the PPS and MPS using redundant position switches. If the gamma blocker remains in the beam path when commanded to open, both the MPS and PPS would prevent beam operation. If the gamma blocker fails to close when the tunnel is accessible, the PPS requires operator intervention to open the PPS access doors to the tunnel (personnel cannot enter via the badge reader only mode). The position of each gamma blocker is indicated in the central control room via status lights and also on the EPICS displays.

## Slide 11: References from SNS
From SNS Document 102030102-ES0083 R00 page 7, emphasis not in the original:
  The Gamma Blockers are shield plugs that are remotely inserted into the beam flight path upstream of the ring injection dump and target as an ALARA measure to reduce local radiation back streaming when personnel enter the tunnels (see Section 3.2.3.10.3 in the FSAD-PF). The PPS provides the non-credited function of monitoring the position of the Gamma Blockers to ensure that the Gamma Blockers are inserted when personnel access the tunnel and to ensure that they are removed prior to beam operations. The PPS provides a non-credited Gamma Blocker Bypass function such that when the key switch is in the Gamma Blocker Bypass position, the operator may transition from Power Permit to Beam Permit mode if either one of the two Gamma Blocker position switches does not indicate “OUT”.