## Slide 1: Challenges and Deadlines for Production
Marcin Wojciechowski Nov. 09, 2016

## Slide 2
GB core:
  Stainless steel block, ø200x200 [mm]
  Two secure positions: on-axis and off-axis
Functional elements:
  Vacuum chamber
  Beamline flanges
  Positioning device
  Support
Gamma Blocker overview

## Slide 3
Vacuum chamber
  Pressurized UHV-class vessel
Beamline flanges
  Compatible with beamline dimensions, UHV compatible
Positioning device
  Manual operation,
  Electric/pneumatic actuator
  Self locking (forces: gravity, vacuum)
  UHV compatible: sealed with welded bellow
Gamma Blocker overview

## Slide 4
Gamma Blocker Proposed solution:
Cylindrical vacuum chamber, with two CF DN160 ports for beamline
DN350, CF type flange mounted positioning module
Welded bellow
Industry-standard linear motion system
  Trapesoidal thread and nut based
  Manually driven
  Position indication
  Independent position locking
Outline: max 1m from axis

## Slide 5
Gamma Blocker Proposed solution:
Cylindrical vacuum chamber, with two CF DN160 ports for beamline
DN350, CF type flange mounted positioning module
Welded bellow
Industry-standard linear motion system
  Trapesoidal thread and nut based
  Manually driven
  Position indication
  Independent position locking
Outline: max 1m from axis

## Slide 6
Keeping the schedule in preliminary stage
  Recalculation of doses
  Changes in construction idea
  Additional interfaces to MPS/PPS
Requirements on actuator materials (radhard)
Gamma Blocker challenges:

## Slide 7
Gamma Blocker production schedule & deadlines:
KickOff
Preliminary Design
2016.12.09
Preliminary Design Report
2016.12.30
Detailed Design
2017.03.31
Purchases
2017.09.29
Critical Design Report
2017.04.21
Production & deliveries
2018.01.31
Factory tests
2018.03.09
FAT Report
2018.03.30
GB Facility Elements delivery
2018.04.29
SAT Report
2018.06.01
Installation Readiness Report
2018.11.30
Final assembly
2018.02.14
Note: deadlines for NCBJ

## Slide 8
Machining and assembly @NCBJ
Purchases of standard/prefabricated components
  UHV components
  Positioning devices
  Support components
Gamma Blocker workflow:

## Slide 9
Production:
  Accelerators:
    Small machines for medicine, industry and science (i.e. GBAR)
    Large machine accelerating cavities (PIMS modules for Linac4)
  Components for nuclear reactor Maria @NCBJ (i.e. for cooling systems)
  Nuclear medicine facilities equipment (bunker doors, treatment tables)
NCBJ experience:

## Slide 10
CNC milling/turning centres
WaterJet cutting machine
Sheet metal bending press
Welding facility
Clean rooms
Vacuum ovens
Chemical treatment facility
Precision welding facility
Quality control witch 3D geometry measurement
Vacuum testing facility
NCBJ resources: