## Slide 1: Digital Platform Interfaces to FBIS
Annika Nordt
Integrated Control System Division
www.europeanspallationsource.se
2017-04-06

## Slide 2: FBIS Interface - Sensor Side Scope (Partial View)
BIS
FBIS
ESS Timing System
Ion Source
System
MP-related Beam Monitoring Systems
MP-related RF Systems
LEBT Chopper System
MEBT Chopper
System
Ion Source Plasma + Extraction Power
Other MP-related Systems for «Fast» Protection Functions
BIS: Set of all «Logic Systems» being part of Protection Functions
FBIS: Subset of the BIS dealing with «Fast» Protection Functions
We talk about those links

## Slide 3: FBIS Interface - Sensor Side Requirements Analysis
Primary Functional Requirement
  Transmit boolean BEAM-PERMIT signal.
Primary Performance Requirements
  Optimize for speed.
    Derived from Requirement for “Fast” Protection Functions
      Processing time from input of FBIS to output to actuation systems shall be < 3µs
  PIL 2 capability
  Minimize “spurious trip” probability
On the next slides: additional Requirements from Protection Function Failure Analysis according to IEC 61508-2:2010

## Slide 4: FBIS Interface - Sensor Side Requirements Analysis – Mode Confusion
Foreseeable Failures with Impact on Interface Design
  Mode Confusion: subset of sensor systems assume wrong mode, i.e. wrong reference values for off-nominal state detection  Loss of protection function

## Slide 5: FBIS Interface - Sensor Side Requirements Analysis – Mode Confusion
Mode Confusion - Current Concept of Operations
  MP-related Systems for which the following conditions apply
    they are part of a «fast» protection function;
    their MP-related function depends on a «mode» setting;
  transmit the «mode» they are using to the FBIS.
  The FBIS checks whether all received «mode» information is consistent and compliant with the «intended mode» distributed through the timing system.
  If this is not the case, the FBIS inhibits beam.
 Link to FBIS needs to support transfer of «mode» information.

## Slide 6: FBIS Interface - Sensor Side Requirements Analysis – Sensor “death”
Foreseeable Failures with Impact on Interface Design
  Sensor System “dies” with stuck-at OK  Loss of Protection Function

## Slide 7: FBIS Interface - Sensor Side Requirements Analysis – Sensor “death”
Sensor System «death» - Current Concept of Operations
  MP-related systems that are part of a «fast» protection function send a regular «heartbeat» signal to the FBIS
    can be timestamp, incrementing counter, ..., but it must confirm the proper functioning of the MP-related functions running on that system.
  The FBIS inhibits beam if the «death» of an MP-related system is detected.
 Link to FBIS needs to support transfer of «heartbeat».

## Slide 8: FBIS Interface - Sensor Side Requirements Analysis – Link Faults
Foreseeable Failures with Impact on Interface Design
  Link Faults:
    Stuck-At OK  Loss of Protection Function
    Stuck-At NOK, Glitches  Loss of Availability (Spurious Trips)
    Degraded Connection, Connection Loss  Both Consequences possible

## Slide 9: FBIS Interface - Sensor Side Requirements Analysis – Link Faults
Options given in IEC 61508 for Diagnostic Measures

## Slide 10: FBIS Interface - Sensor Side Requirements Analysis – Link Faults
Additonal Requirements from Facility Operations point of view:
  System shall allow to detect disconnected or degraded links directly and explicitly.
  Rationale: allow for efficient system test, fast problem diagnostics and troubleshooting.
 Link to FBIS needs to support direct detection of connection loss and degraded connection.

## Slide 11: FBIS Interface - Sensor Side Requirements Analysis – Speed
Speed Optimization - Consequences
  Signal type must support «high-density» logic
    Manage as many signals a possible on one FBIS logic board to minimize FBIS «tree»-depth
  Minimize BEAM-PERMIT transmission latency
    Transmission over «dynamic» signal, like a constant frequency (e.g. frequency-present = OK and frequency-absent = NOK) or a data-link, introduces additional latency
      Increasing the link frequency to lower the latency increases complexity of the signal handling; e.g. proper management of spurious packet-loss or pulse-loss would again increase latency.
 BEAM-PERMIT Transmission through «dynamic» signals would compromise optimizatzion for speed

## Slide 12: FBIS Interface - Sensor Side Satisfy all Requirements – Current Proposal
Discrete, static link for BEAM-PERMIT transmission
  Minimize Latency
  Support «high-density» logic
Additional data-link
  Transmission of «mode» information
  Transmission of «heartbeat»
  Redundant and diverse transmission of BEAM-PERMIT states
  Bonus: full Handshake Capability (e.g. for BCM Calibration Support)
Primary Requirement: Speed
Mode Confusion Check
Sensor «Alive» Check
Allows Input comparison/voting (Table A.7 IEC 61508-2)

## Slide 13: FBIS Interface - Sensor Side Discrete Link - Current Status
Discrete Link: two options under detailed investigation
  3-wire current loop
    Separate current loop for OK and NOK transmission. Current through both loops or no current indicate link failures.
  RS-485 with additional link-fault circuit
    Fast off-the-shelf components available (with data-sheet latencies < 20ns).
A few more discussions and investigations are needed.

## Slide 14: FBIS Interface - Sensor Side Data Link - Current Status
Data Link: current proposal is to use standard Ethernet (100 Mb, Layer-2) for data communications
  Proven in use, Easy to integrate, «Networkeable», Still allows low latency data transmission
  Upgreadable from simple ethernet to realtime and/or safety profiles on same hardware
Current activities: investigate options for network topology
Identify additional requirements from IEC 61508-2:2010 for «black-channel» implementation: general rules from IEC 61784-3

## Slide 15: «Black-channel» communication in the scope of IEC 61508  IEC61784-3

## Slide 16: Realization Options for Ioxos IFC 14x0 based boards - Connectivity
Three connection options
  Dedicated Interlock Piggy-Back (top picture shows mock-up)
  Dedicated Interlock FMC Card
  Interlock Connectivity on uRTM
Connector options under investigation
  3M-SDR 26 pin
    mixed data-link and multiple discrete signal connection (bottom picture shows connector example; courtesy of Ioxos)
    Support for redundant interface
  3M-SDR for discrete signals and RJ-45 for data link

## Slide 17: Realization Options for Ioxos IFC 14x0 based boards - Firmware
Direct Integration of interlock interface management into TOSCA framework:
  User does not need to cope with data-link protocol details or concrete discrete link implementation
Include «heartbeat» generation into MP-related protection function processing

## Slide 18: Realization Constraints for other boards
Hardware-side
  Foresee enough space and «FPGA-Pins» to drive both the discrete links (at least one) and data-links (at least one).
    «Enough» will be fixed, once the final decision for the interface has been made.
    Be ready to support redundant connectivity if part of «fast» protection function with PIL 2 requirement
Firmware-side
  Implement control (and monitoring) of discrete signal outputs
  Include «heartbeat» generation into MP-related protection function processing
  Be ready to implement Ethernet communication to send «mode» and «heartbeat» information (if applicable)