## Slide 1: WP11: CDS-SL CDR Overview
April 19th 2017

## Slide 2: ESS MACHINE
The European Spallation Source (ESS) LINAC
CNRS CONTRIBUTION (CNRS/IN2P3/IPNO)
Moderated neutrons To experiments lines
LENGTH:
SRF LINAC: ~312 m
    Elliptical section (~256 m):
    design of the 30 cryomodules
    (collaboration with )
P
    SRF cavity cooling: 2 K in saturated He II bath ( simple techno.+ few energy stored + pressure control)
    Design, construction and installation of the Spoke section (~56 m)
    Design, construction and installation of the cryogenic C&C system of theLINAC

## Slide 3: ESS Spoke section
Spoke section overview
  13 Spoke cryomodules (CM)
  Cryogenic Distribution System for Spoke linac (CDS-SL)
    main four-channels cryoline (headers)
    13 valve boxes (VB): one for each Spoke cryomodule
    1 end box: to return flow to the cryogenic plant (ACCP)
    13 branch cryolines (cryogenic jumper): connection from headers to each CM
    auxiliary process lines
    1 part of the vent line
Beam direction
To the CDS-EL and ACCP
End box 
Spoke cryomodule
Valve box

## Slide 4: ESS Spoke section
Spoke section overview
  Cryogenic Distribution System for Spoke linac (CDS-SL)
    main four-channels cryoline (headers)
    1 End Box: to return flow to the cryogenic plant (ACCP)
    auxiliary process lines
    1 part of the vent line
Vent line
Valve box
Headers
Auxiliary lines
End Box

## Slide 5: ESS Spoke section
Spoke section overview: the Cryogenic Distribution Line
  Components
HU03
HU02
End box
VB01
VB02
VB03
VB13
Interface with the CDS-EL
Beam direction
x
y
HU-EL
TCS axis
HU01
HU13
1x End box
13x valve box (VB)
13x (standard) Headers Unit (HU)
1x Elliptic interfaced Headers Unit (HU-EL
Spoke cryomodules

## Slide 6: ESS Spoke section
Spoke section overview
  Flexible components
valve box (VB)
(standard) Headers Units (HU)
Elliptic interfaced Headers Unit (HU-EL)
1x End box
Flexibility wrt the cryomodules cryo. distribution
Flexibility of the CDS-SL
Flexibility wrt the vent line
HU03
HU02
End box
VB01
VB02
VB03
VB13
Interface with the CDS-EL
Beam direction
x
y
HU-EL
TCS axis
HU01
HU13

## Slide 7
Spoke section overview
  Flexible components (vacuum vessel and cryolines)
Header Unit
Auxiliary lines
Valve box
Valve box
Beam direction
Flexibility
Flexibility
Flexibility

## Slide 8: ESS Spoke section
Spoke section overview
  Supports of the cryolines (with respect to the vacuum vessel)
HU03
HU02
End box
VB01
VB02
VB03
VB13
Interface with the CDS-EL
Centring (sliding) support wrt the vacuum jacket
Centring support wrt the vacuum jacket
Fixed displacement along the beam axis
Beam direction
x
y
HU-EL
TCS axis
HU01
HU13
Centring support wrt the vacuum jacket
Fixed displacement along the beam axis
Free Rx, Ry, Rz
Tx free; Ty0; Tz0
Free Rx, Ry, Rz
Tx0; Ty0; Tz0
Rx=0, Ry=0, Rz=0
Tx=0; Ty=0; Tz=0

## Slide 9: Main components of the CDL
Valve box
Valve box support
Positioning frame
Interface with the Header unit
Fiducials supports
Cryogenic valves
Interface with the cryomodule
He relief branch line

## Slide 10: Main components of the CDL
Headers units
Support frame
Handling and positioning frame (to be removed after installation)
Installation tooling (compression and positioning of the bellows)

## Slide 11: Main components of the CDL
End Box

## Slide 12: Design framework
European Pressure Equipment Directive (PED 2014/68/UE)
    EN 13445: Unfired pressure vessels
    EN13480: Metallic industrial piping
    EN 13458: Cryogenic vessels – Static vacuum insulated vessels  End Box
    gives rules for:
    Design
    Materials
    Manufacturing
    Installation
    Tests
    Maintenance
AFS 2005:2

## Slide 13: Design framework
Pressure Equipment Directive (PED 2014/68/UE)
  Process lines:
   Category I for CDS-EL
   Category I for CDS-EL
   Category I for CDS-EL

## Slide 14: Design framework
Pressure Equipment Directive (PED 2014/68/UE)
  End Box: cryogenic pressure vessel
50
VLP MAWP = 5 barg
 cat I for CDS-EL
 §3.3 for CDS-SL)
Aim: to remain in category I
Max. volume of the End Box helium tank (50 L)

## Slide 15: STATUS
Valve box
  Design nearly finished
  Procurement phase
Headers Units
  Design nearly finished
End Box
  Design under progress (tank supports)
Auxiliary lines
  Design nearly finished
Support frames
  Design nearly finished

## Slide 16: End Box status
Function of the End Box:
  To return the flow to the ACCP
  To smooth the heat loads changes
Design concepts
  From He supply to VLP
  12.3 g/s (up to 27.1 g/s)
  Helium liquefaction (JT)
    Benefit from phase change
     T° fixed by pressure
    the vapours flowing back to the ACCP starts from saturated vapours at a fix T°
    Needs to produce vapours from liquid
    JT does not need to be very efficient (no subcooling heat exchanger)
    Need of heaters (170 to 382 W)
    Heat loading of the LHe is allowed
  Vapours flowing from the End Box (VLP)
    Limit heat loads on the vapours

## Slide 17: End Box status
Goal:
Design
  Support of the LHe is to finalize
  (comply with pressure loading due to “end effect”)
  Pipe routing is finished
  (burst disk connection to vent line is to be confirmed: depends on the helium collector design)
  Thermal shield is integrated
  Vacuum vessel is designed
Analyses
  Mechanical: to finalize LHe support
  Thermal analysis: under progress (support)
  Thermoacoustic: done

## Slide 18: REQUIREMENTS
List of requirements
  A list of 117 requirements was established
  All requirements concerning the CDS-SL are validated
  Most of the interface requirements are agreed and validated
  But:
    We have to procure or complete some interfaces sheets describing the interfaces

## Slide 19
WP is interfaced with
  WP04: Spoke cryomodules
    Cryogenic branch lines (including the cryogenic jumper)
  WP11 : Cryogenic Distribution System for the Elliptical Linac
    Main process lines (headers)
    Auxiliary lines
    Safety devices
  WP12 : Vacuum
    Pumping ports
    Diagnostic
    Control ports (diagnostic and pumping if required)
  WP13 : Safety
    (Safety devices)
    Burst disks
    Vent line
  WP15 : Cabling & Conventional Power
    Instrumentation and actuators
  ICS : Control/Command
    Instrumentation and actuators

## Slide 20: REQUIREMENTS
List of requirements
  WP04: Spoke cryomodules
    List not validated by WP4
     to be validated with the cryogenic jumpers designs (WP4 and WP11)
  WP11 : Cryogenic Distribution System for the Elliptical Linac (CDS-EL)
    List completed and several iterations. In Chess?
  WP12 : Vacuum
    List completed and validated. In chess?
  WP13 : Safety
    Requirements concerning MAWP and safety devices were written as interface requirements with CDS-EL  validated. In Chess?
    Helium collector:
    ESS does not want to establish requirement  ESS and IPNO agreed to postpone the design of the vent line. When?

## Slide 21: REQUIREMENTS
List of requirements
  WP15 : Cabling & Conventional Power
    No requirement needed
    List of cables established
  WP99 :AccelInfrastructure & Installation
    Requirements list validated
  ICS : Control/Command
    No requirement yet written
    List of instrumentation written and discussed with ESS

## Slide 22: PROTOTYPING
CNRS’ contribution to ESS
Prototype Valve box
Prototype Cryomodule
Uppsala univ.
Uppsala univ.
IPNO
  A prototype and test valve box:
    Prototype valve box  to validate the valve box concepts
     to validate the prototype Spoke cryomodule
    Test valve box  to validate 13 series Spoke cryomodules
     Compromise between an optimized test stand and a demonstrator (cryoprocess, assembly)
  A versatile (flexible) valve box
    Tests at IPNOrsay (FRANCE)
    Tests at Uppsala University (SWEDEN)
     To manage different cryogenic infrastructures
ESS Series cryomodules
and test

## Slide 23: PROTOTYPING
Prototypes
VALVE BOX
SPOKE CRYOMODULE
CRYOGENIC JUMPERS

## Slide 24: Prototyping the Spoke section
Flow scheme (PID): prototype version
Main differences with machine:
Instrumentation
Saturated LHe supply
Saturated LN2 supply
   phase separator in the VB
   same subcooler
   RF coupler heat intercept
  cold sat vapours used (instead of SHe)
 Interfaces with the infrastructures

## Slide 25: Prototyping the Spoke section
Valve Box
Delivered in September 2016 (delay = 9 months)
But not the cryogenic jumpers…
Cool-down and operation at 4 K  some minor problems detected but tests were OK

## Slide 26: Prototyping the Spoke section
Cryogenic jumpers
After delivery of the cryogenic jumpers in November
Connection of the cryomodule and… troubles with the both cryo jumpers:
- delivered bellows (inside the jumpers and covered by MLI) were not corresponding to the manufacturing drawings
- cryogenic jumpers pressure test tools were not well sized
 damaged bellows  leaks
Everything was done (and tried) to perform a cryo test
some components changed and repair at IPNO
(with on-stock components)
but VB jumper finally repaired by the manufacturer
CM jumper modified by IPNO (to use in-stock components):
VLP branch line was modified (DN40 inside a DN100 !)
Exhaust burst disk line modifed: DN100  DN40 (use of mock-up cavities so beam
vacuum loss incident is not considered)

## Slide 27: Prototyping the Spoke section
2K test
    - March: cryomodule and valve box connected
    Configuration "not optimal" (or the worst possibel configuration) as:
      1 magnetic shield not cooled
      1 power coupler double-wall installed but not cooled
      VLP branch line modified abd heat intercept suppress
      Configuration "not optimal" (or the worst
    - But 4 K and 2 K cryogenic tests were performed
    with the Spoke cryomodule and test valve box
    - Heat loads were important (but as evaluated)
    - Liquid level regulations loop were tested successfully at 4 K and 2K
     LHe II level was correctly maintained in the cryomodule cavities

## Slide 28: CNRS - WP11
The team
  P. DUTHIL
    Work Unit leader
    Cryogenics, numerical analysis, procurements WP4: same activities
  M. PIERENS
    Cryogenics, instrumentation
    WP4: instrumentation and tests
    WPxx (C&C): WP leader
  D. REYNET
    System engineer
    Mechanics, design, mechanical analysis,
    WP4: Same activities + procurements + quality
  S. BRAULT
    Design and drawings
    WP4: Same activities + procurements + tests
  F. CHATELET
    Experimental activities and cryogenic tests
    WP4: same activities
  V. POUX
    Quality Manager
    WP4: same activities
  V. LAURENCIER
    Finance management
    Procurements
  IPNO/IN2P3 support
    Equipment
  CNRS support
    Procurement

## Slide 29: Thank you for your attention Special thanks to Matthieu Pierens Denis Reynet Sylvain Brault Frédéric Chatelet
CSP12
28 Novembre 2014