## Slide 1: Work Unit 11.11.5.3 - AIK 11.2 CDR of the CDS-SL Mechanical analyses of the valve box
April 19th 2017

## Slide 2: Design framework
European Pressure Equipment Directive (PED)
    EN 13445: Unfired pressure vessels
    EN13480: Metallic industrial piping
    EN 13458: Cryogenic vessels – Static vacuum insulated vessels  End Box
    gives rules for:
    Design
    Materials
    Manufacturing
    Installation
    Tests
    Maintenance
AFS 2005:2

## Slide 3: Material 1/3
Model
AISI 304L (1.4306 / X2CrNi19-11)
E = 190 000 Mpa
= 0.305
ρ = 7 900 kg/m3

## Slide 4: Material 2/3
Pressure Equipment Directive 2014/68/EU
  EN 10028-7
    Proof strength: Rp1,0 = 240 Mpa @ room T° (= pressure test T°)
    Tensile strength: Rm  500 Mpa @ room T° (= pressure test T°)
    Elongation after fracture: A  45 %
  EN 13445-3 (p25)
 fd 304L = 166 MPa
 ftest 304L  250 MPa

## Slide 5: Material 1/3
Pressure Equipment Directive 2014/68/EU
  EN13445-3
p565
for the membrane stresses
(=neutral fibre of the shell elements):
  - for areas away from the shape discontinuities:
  f = fd (cf. §2.2 for fd)  smax membrane < 166 MPa
  - for areas near shape discontinuities:
  f = fd x 1.5  smax membrane < 249 MPa
for the bending stresses: f = fd x 1.5
 smax bending < 249 MPa
 for normal pressure operation (i.e. for MAWP = Ps):

## Slide 6: VALVE BOX
Vaccum vessel
  Static analysis
  Thicknesses of shell elements

## Slide 7: VALVE BOX
Vaccum vessel
  Static analysis
    Considered:
      gravity,
      the weights of non-modelled components such as the piping, valves and thermal shield;
      the forces due to the thermal shrinkage which are transmitted onto the vacuum vessel;
      and the pressure loads (external pressure.
 magnitude displacement of the vacuum vessel: 0.9 mm at the jumper location

## Slide 8: VALVE BOX
Vaccum vessel
  Static analysis: valve box standing on its 3 support pods
    Considered:
      gravity,
      the weights of non-modelled components such as the piping, valves and thermal shield;
      the forces due to the thermal shrinkage which are transmitted onto the vacuum vessel;
      and the pressure loads.
Left: total (membrane + bending) stress
 σmax 188 Mpa (at a geometric discontinuity)
Right: bending stress on shell elements
 σmax 188 Mpa

## Slide 9: VALVE BOX
Vaccum vessel
  Static analysis: valve box lifted by use of its 3 eye rings
    What is considered:
      gravity,
      the weights of non-modelled components such as the piping, valves and thermal shield;
      the forces due to the thermal shrinkage which are transmitted onto the vacuum vessel;
      and the pressure loads.
Left: total (membrane + bending) stress
 σmax 37 Mpa
Right: bending stress on shell elements
 σmax 14 Mpa

## Slide 10: VALVE BOX
Buckling analysis of the vacuum vessel
  Evaluation of the critical external pressure by use of EN13445
=960
1000
ea
Thickness ea = 6 mm

## Slide 11: VALVE BOX
Buckling analysis of the vacuum vessel
  Circumferential stress Py (EN 13445: equation 8.5.3-15)
  Theoretical elastic instability pressure (EN 13445: equation 8.5.2-5)
  Calcluating the ratio Pm/Py and detrmining Pr/Py
  Maximum external pressure
se: Yield strength
ea: Thickness
R: Mean radius of the cylinder
se = 200 MPa
ea = 6 mm
R = 497 mm
 = 0
G = 0
= 2.41 MPa
E = 190000 MPa
ea = 6 mm
e = 0.0006 with:
L/2R = 0.96 & 2R / ea = 165
R = 497 mm
= 1.38 MPa
Pr / Py = 0.56  Pr = 1.35 MPa
Pm / Py = 0,57
Pmax < Pr / S
S = safety factor = 1.5
Pmax < 0.9 Mpa = 9 bar (external pressure)
with ea = 6 mm, sufficient margin is expected

## Slide 12: VALVE BOX
Buckling analysis of the vacuum vessel
  Comparison with a FEM analysis
    Only pressure loads are considered
The critical pressure is evaluated to be 9.4 bar
 comparison is satisfactory

## Slide 13: VALVE BOX
Buckling analysis of the vacuum vessel
  Considering all loads: pressure but also gravity (and forces, cf. previous static analysis)
The critical pressure is evaluated to be 5.2 bar
 sufficient margin is expected

## Slide 14: VALVE BOX
Static analysis of the internal pipes
    What is considered:
      gravity,
      the connections with the vacuum vessel;
      the pressure loads,
      the contacts between elements such as the supports  frictionless contacts
Rx = 0 imposed at the ends of the 4 main cryolines
 assess the reaction moments (torsional moment to be transmitted to the bellows of the Headers Unit)
x-axis

## Slide 15: VALVE BOX
Static analysis of the internal pipes
    Results:
Total deformation
 δmax ≈ 4 mm (essentially in the X axis direction)
Temperature field (T > 55 K in red)

## Slide 16: VALVE BOX
Static analysis of the internal pipes
    Results:
Left: total (membrane + bending) stress
 σmax 172 Mpa (in a discontinuity area)

## Slide 17: VALVE BOX
Static analysis of the internal pipes
    Results:
Bending stress on shell elements only
 σmax 56 Mpa
 Maximum moment:
13.1 N.m estimated at the extremity of the VLP
 compatible with torsional moment accepted by bellows

## Slide 18: CONCLUSION
Valve box mechanical analysis
  Static analyses of the vacuum vessel and internal piping were performed:
    Maximum stress comply with EN13445
    Maximum moments are compatible with the use of bellows
  Buckling analysis:
    The critical buckling pressure was evaluated
     5,2 bar is estimated taking into account all (possible) static loads
     we consider that this is a sufficient margin
Next steps
  Transport
    Modal analysis has to be performed
     evaluation of the eigen modes
    Static analysis with different acceleration (magnitude and directions)
     evaluation of the stress
     design of the transportation (and handling) tooling

## Slide 19: Thank you for your attention
CSP12
28 Novembre 2014