## Slide 1: Work Unit 11.11.5.3 - AIK 11.2 CDR of the CDS-SL Installation integration
April 19th 2017

## Slide 2: CDS-SL
Overview
Headers unit
Valve box
Part one : the valve box
Part two : the headers units

## Slide 3: CDS-SL
Part one : installation of the valve boxes

## Slide 4: Tunnel integration
Integration of the Valve box : support feet installation
Drilling jig (floor drilling)
Intermediate plates
(floor fixation by anchors bolts)
Central foot
External feet
Fiducials
Multiplication of holes to prevent the concrete reinforcement

## Slide 5: Tunnel integration
Valve box setting up
Trolleys
Electrical pulling/pushing vehicle

## Slide 6: Tunnel integration
Valve box setting up
Introduction between the feet
Put down and attach to the feet

## Slide 7: Tunnel integration
Valve box setting up
Remove the 2 trolleys
Ready to align

## Slide 8: Valve box alignment
3 Adjustable and lockable feet (at 120°)
Alignment
1,5” corner cube reflector
(Fabien REY ESS-Alignment)
7 fiducial marks
Fine (sensitive) adjustement:
- along X and Y axis : ±40mm
- along Z axis : ± 50mm
Threaded shaft (fine thread)
Thrust ball bearing
Concave and convex washers

## Slide 9: Valve box and wave guide interface
Space for RF distribution (wave guides)
Wall
Large free space under the support frame

## Slide 10: Headers unit
Part two : installation of the headers units

## Slide 11: Headers unit : Handling trolley
Fine adjustement:
- along X and Y axis : ±40mm
- along Z axis : ± 50mm
Useful for:
- transportation inside the tunnel
- positioning
Removable and reusable
Threaded shaft (fine thread)
Concave and convex washers
Carrier ball
Adjusting screw

## Slide 12: Tunnel integration
Insertion of the header between two valve boxes
Compression tooling
Compression tooling
The compression of the cryolines is required during installation
(→ goal: free position of the bellows at cold T°)
4 independant blocks

## Slide 13: Tunnel integration
Insertion of the header between two valve boxes
5 mm gap
(compression)
5 mm gap
(compression)
insertion
Ajustment / Alignment
Fixation and removal of the trolley

## Slide 14: Tunnel integration
Welding of the cryolines sleeves
Sleeves
Relaxation of the bellows until contact between flanges

## Slide 15: Tunnel integration
Welding of the cryolines sleeves
Weld
Weld
Weld
Weld

## Slide 16: Tunnel integration
Welding of the cryolines sleeves
Removal of the compression tooling

## Slide 17: Tunnel integration
Welding of the cryolines sleeves
VPL line
TS lines
He Supply line
Easier to ensure the junction
4 times cut off
2 welds per sleeve
Sleeve

## Slide 18: Tunnel integration
Closing after global pressure test
Thermal shield and MLI implementation

## Slide 19: Tunnel integration
Closing
Dedicated tooling for sleeve translation

## Slide 20: Tunnel integration
Closing

## Slide 21: Tunnel integration
Closing
weld
weld
Adjust
Removal of the tooling

## Slide 22: Tunnel integration
Closing
Removal of the tooling
2,2 m
1 m

## Slide 23: Tunnel integration
Continue with the installation…

## Slide 24: Thank you for your attention Special thanks to Syvain Brault (chief designer)
CSP12
28 Novembre 2014