## Slide 1: Applications to Particle Physics
Lecture at the Nordic Particle Accelerator School 2017
August 2017, Lund, Sweden
Erik Adli
Department of Physics, University of Oslo, Norway
Erik.Adli@fys.uio.no

## Slide 2: The 27 km LHC at CERN

## Slide 3: Future colliders
The next big thing? After LHC, high energy, high luminosity, Linear Colliders of several 10 km of length have been proposed – why?

## Slide 4: Particle physics

## Slide 5
Materiens bestanddeler
Particle physics: study of fundamental particles and forces (as opposed to atomic physics, nuclear physics, chemistry, material sciences ….)
The Standard Model
of particle physics :
Mathematically consistent framework modeling the world as 3 families of matter particles, plus force carries.
10-10
10-14
10-15
10-18
meter
10-18 = 0.000000000000000001

## Slide 6: Example of matter and forces, according to the Standard Model
Hydrogen atom
Kaon (K-)
Beta decay
e-
e-
Proton
Matter and forces of nature are modeled as particles.
"Feynman diagram"

## Slide 7
+ The Higgs Boson
The final piece of the Standard Model, the Higgs Boson, was discovered by the particle collider LHC in 2012.

## Slide 8
We are far from understanding the universe

## Slide 9
Vi vet egentlig ingenting!
Why three families? Anti-matter?
Dark matter, does super symmetry exist?
Nature of neutrinos?
Can we unify the description of the forces?
We will need high-energy physics experiments for a long time to come!
Many open questions

## Slide 10
2012
1996
1983
1968
1974
1897
1936
~1975
1977
1956
1962
2000
(1968)
Year : Accelerator discovery
Year : Non-accelerator discovery
2012
Colliders: Heavy particles  more energetic collisions are required.
ECM >= mc2
Energy requirement for pair production:
Ephoton = 2mec2 + Ek
Requirements: Energy
Probe wavelength: Particles are waves. Wavelength of probe should be smaller than the object you want to study. De Broglie wavelength :
l = h / p
(~ 1 Å for 100 MeV e-)

## Slide 11: Energy : fixed target versus colliding beams
Colliding beams are needed in order to reach the highest center of mass energies.
m2

## Slide 12: Requirements: particle type
Lepton collisions: elementary particles (leptons, muons…)
  Collision process, and initial state known
  Well defined energy
  Lepton collisions  precision measurement
Hadron collisions: compound particles (protons, ions…)
  Mix of quarks, anti-quarks and gluons: variety of processes
  Parton energy spread
  Hadron collisions  large discovery range
  “If you know what to look for, collide leptons, if not collide hadrons”
Hadron production from
lepton collisions
Lepton production from hadron collisions

## Slide 13: Requirements: luminosity
High energy is not enough, production rate are as important, because the events we are looking for are rare.
The probability for particle physics processes to occur are quantified by “cross section”, s, an area, with units in “barns”, b = 10-28 m2.
The higher the cross section, and the more collisions per second, the higher reaction rate R for a given process is :
The proportional factor, L, called the luminosity [cm-2s-1], depends on the colliding beam parameters as :
  n1, n2 :particles per bunch
  x, y : bunch transverse size at the interaction point
  f: bunch collision rate

## Slide 14: Main parameters characterizing a high-energy physics accelerator
Particle type
Energy spectrum
Emittance
Focusing
Charge per time
Time structure
…
Luminosity

## Slide 15: Review of some basic accelerator concepts

## Slide 16: It’s about a beam, in 6D
A charged particle beam, taken at a given point in time, can be characterized by a six dimensional distribution, two transverse planes + one longitudinal plane.
y(x, y, z)

## Slide 17: Beam evolution
The rms beam size:
Beam quality
Lattice design
Luminosity :
Notes: Write on blackboard

## Slide 18: Beta function and emittance
Beta function, b(s): how well the beam is focussed. Minimum, b*, at the beam waist.
Emittance, e: beam quality, phase-space area; e = √(<y2><y’2> - <y y’>2)
Two key concepts that defines a charged particle beam:
Evolution of the transverse phase-space in free space along the beamline :
s= √(eb (s))

## Slide 19: LHC: four collision points

## Slide 20: LHC: the collision point
Collision region:
* Very strong quadrupoles,
* close to the interaction point
Upgraded magnet, more beta squeeze, more luminosity.

## Slide 21: What limits the collision energy of the LHC?

## Slide 22: LHC energy: limited by bending magnets
8.3 T maximum field (allows for 7 TeV per proton beam). Generated by a current of 12 kA in the superconducting Rutherford coils.
Developments for higher energy hadron colliders (HE-LHC, FCC) : Nb3Sn, HTS

## Slide 23: Particle colliders

## Slide 24: Particle collider Livingstone plot
CLIC
ILC
each step: pushed and overcome the next limits in luminosity/intenesty and energy/power.
Great success of accelerator physics and technology.
(a "Europe-centric " selection)

## Slide 26: Hadron versus lepton colliders
Hadron collider SppS, √s=540 GeV, W+/- and Z0 discovery
Lepton collider LEP, √smax=209 GeV, precision measurements of Z0 decay width
1983
2000

## Slide 27: LHC versus future colliders
Linear Collider: Precision measurements if the trilinear HHH-coupling (Courtesy of M. Battaglia)
Analogy: Higgs physics
Standard Model Higgs:
scalar spin-0 particle
specific form of scalar potential :
ATLAS and CMS@LHC, discovery of the Higgs boson confirmed in 2012. LHC continues to study properties of the Higgs boson. Precision measurements can be very hard with a hadron collider.
Linear Collider: Higgs spin measurements by energy scan (spin 0 established by LHC by other techniques)
Linear e- e+ collider : can perform complementary, model independent Higgs physics.

## Slide 28: Energy limitation in rings: synchrotron radiation
Limiting factor for the LEP energy (e- Ecm,max = 209 GeV). LHC?
Total cost scaling for rings: ~E2
TeV e- e+ collisions: circular colliders not a practical option
Linear acceleration : ~E with respect to E2 for rings
Synchrotron radiation power loss :
U: energy loss per turn
C: cost of circular machine
SR: a blessing
and a problem

## Slide 29: Circular versus linear colliders
We lose two advantages of circular colliders by going linear :
The cavities accelerate only once
...length for TeV scale collisions?
2) The bunches collides only once
Linear collider: retain sufficiently high total acceleration voltage (centre of mass energy of ~TeV) and total collisions (luminosity ~1034/cm2/s), while limiting total power to a few 100 MW (nuclear power plant: ~1GW).
Linear collider: need ultra-small beams at the interaction point.
e+
e-
Collision energy = 2* linac-length * Cavity gradient
f, collision frequency for LHC: 40 MHz
LHC

## Slide 30: Linear collider ingrediences

## Slide 31: Linear Collider Projects
The Compact Linear Collider, CLIC
Main linac technology: two-beam scheme. Normal conducting Cu RF 12 Ghz TW cavities, 100 MV/m. Nominal design for ECM = 3 TeV (375 GeV to 3 TeV)
The International Linear Collider, ILC
Main linac technology: super conducting RF 1.3 GHz SW cavities, 31.5 MV/m
Nominal design for ECM = 0.5 TeV (250 GeV to 1 TeV)

## Slide 32: ILC: Japanese proposal
The Japanese scientific community has proposed to host the ILC in Japan, and commit to fund 50% of the material costs (70% of an Ecm = 250 GeV first stage). Basically ready to construct political support is secured. Decision may come around 2019.

## Slide 33: CLIC : a CERN-centered multi-TeV LC study
Drive Beam Generation Complex
Main Beam Generation Complex
Main & Drive Beam generation
complexes not to scale

## Slide 34: CLIC High Gradient research
CLIC main linac structure :
12 GHz Cu TW
100 MV/m gradient (loaded)
BDR < 3 x 10-7/pulse/m
Rf pulse length: tp = 240 ns
High gradient limitations :
* Surface magnetic field
  Pulsed surface heating DT => material fatigue => cracks
* Field emission due to surface electric field
  RF break downs
  Break down rate (BDR) => Operation efficiency,
  Local plasma triggered by field emission => Erosion of surface
  Dark current capture => Efficiency reduction, activation, detector backgrounds
* RF power flow
  RF power flow and/or iris aperture apparently have a strong impact on achievable Eacc and on surface erosion. Mechanism not fully understood.
BDR = f(max field, rf pulse length, freq) ~ Eacc30tp5 (empirical)
CLIC limit: DT < 50 K, limits pulse length to few 100 ns
Cu Surface after break down

## Slide 35: The CLIC Two-Beam scheme
Animation courtesy SLAC ACD group
(A. Candel)
Main beam – 1 A, 156 ns
from 9 GeV to 1.5 TeV
Drive beam - 101 A, 240 ns
from 2.4 GeV to 240 MeV
CLIC: “Transformer ratio” of ~1.5 TeV / 2.4 GeV = 15
Demonstrated experimentally at the CLIC Test facility at CERN.

## Slide 36
Helsinki Institute of Physics (Finland)
IAP (Russia)
IAP NASU (Ukraine)
IHEP (China)
INFN / LNF (Italy)
Instituto de Fisica Corpuscular (Spain)
IRFU / Saclay (France)
Jefferson Lab (USA)
John Adams Institute/Oxford (UK)
Polytech. University of Catalonia (Spain)
PSI (Switzerland)
RAL (UK)
RRCAT / Indore (India)
SLAC (USA)
Thrace University (Greece)
Tsinghua University (China)
University of Oslo (Norway)
Uppsala University (Sweden)
UCSC SCIPP (USA)
ACAS (Australia)
Aarhus University (Denmark)
Ankara University (Turkey)
Argonne National Laboratory (USA)
Athens University (Greece)
BINP (Russia)
CERN
CIEMAT (Spain)
Cockcroft Institute (UK)
ETHZurich (Switzerland)
FNAL (USA)
Gazi Universities (Turkey)
John Adams Institute/RHUL (UK)
JINR (Russia)
Karlsruhe University (Germany)
KEK (Japan)
LAL / Orsay (France)
LAPP / ESIA (France)
NIKHEF/Amsterdam (Netherland)
NCP (Pakistan)
North-West. Univ. Illinois (USA)
Patras University (Greece)
CLIC multi-lateral collaboration
48 Institutes from 25 countries
The CLIC collaboration
Notes: 36

## Slide 39: Conclusions
The synchrotron LHC at CERN is the world's largest accelerator. It is currently running close to its design energy (14 TeV) and design luminosity (1034 /cm2/s). It will run for at least 15-20 years more, with its technology continuously upgraded
Several projects, linear colliders or very large synchrotrons, are on the table as options for the next high-energy physics machine after the LHC.
Regardless of machine chosen, the next generation projects have plenty of interesting physics and technology challenges for young accelerators physicists and engineers to overcome.

## Slide 40: Extra

## Slide 41: Parameters: LEP, LHC and CLIC
 | LEP | LHC | CLIC
Particle type | e+ and e- | p, ions (Pb, Au) | e+ and e-
Max. collision energy | 209 GeV | p: 14 TeV (~ 2-3 TeV mass reach, depending on physics) | 3 TeV
Time structure | 4 bunches circulating, 50 MHz collsion rate | 2800 bunches circulating, 40 GHz collision rate | 312 micro-bunches, colliding at 50 Hz repeition rate
Luminosity | Peak: 1032 cm-2s-1 Integrated L in total : ~ 1000 pb-1 (per experiment) | 1034 cm-2s-1 (IP1 / IP5) Integrated L up to now : ~ 27 fb-1 (per experiment) | 1034 cm-2s-1
CERN-based colliders, nominal parameters :

## Slide 42: History: SLC
One e+ e- collider have been in operation, the Stanford Linear Collider (SLC) from 1989 to 1998
Ecm = 91 GeV (Z0), gradient 17 MV/m, L~1030/cm2/s, single bunch collisions at 120 Hz, sx~1.5 um, sy~0.5 um
Very challenging to operate, but brought under control by hard work and careful accelerator physics studies, in particular ring and linac instabilities
Valuable proof of principle and lessons learned

## Slide 43
Luminosity
Energy reach
  Typical accelerator gradient ~10 MV/m -> ~100 km site for 1 TeV collisions
Structures: large accelerating gradient with low breakdown rate
Luminosity per power is the key figure of merit for a linear collider
Beam acceleration: ~10 MW of beam power with high gradient and efficiency
--- compare to “1 TW” LHC type beam: reduce transverse dim. by a factor ~105
Generation of ~10 nm vertical emittances by radiation damping
Preservation of ultra-small emittances through main linacs :precise static alignement, beam-based alignmen. Advanced feedback and feed-forwards. Stability of nanometer range.
Chromaticity corrected final focus with beta function on the order of 100 um : very strong final doublet magnets. Sextupoles to compensate chromatic aberrations. Stability of sub-nanometer range.
Linear collider challenges

## Slide 44: Requirements: time structure
Linear collider time structure : charge delivered in micro-bunched pulses
Example for the International Linear Collider (500 GeV high lum.)
charge delivered in pulses of 1 ms, at 5 Hz
3 nC charge in each micro-bunch
Circular collider time structure : constant collision rate
Example for LHC, nominal parameters
charge delivered in bunches at 25 ns spacing
16 nC charge in each bunch
2800 bunches in each beam, colliding at 40 GHz
Time structure may be driven by accelerator (collective effects) and/or detector (read-out) constraints.
LHC: four collision points

## Slide 45: The Muon collider option
Poses a number of hard, and very interesting, accelerator physics challenges.
TeV lepton collisions in a small circular collider? Muons!