## Slide 1: EPICS status and future at KEK Control Group / Commissioning Group e-/e+ Injector Linac, KEK, Japan Masanori Satoh

## Slide 2: EPICS status in KEK
Accelerator facilities in KEK
  Tokai campus
    J-PARC (Linac + Rapid Cycle Synchrotron + Main Ring)
  Tsukuba campus
    KEKB => SuperKEKB (7 GeV e-, 4 GeV e+ collider w/ positron damping ring)
    PF (2.5 GeV light source)
    PF-AR (6.5 GeV light source)
    Injector linac for SuperKEKB and light sources
    ATF (Accelerator test facility for Linear Collider)
    STF (Superconducting test facility)
    cERL (ERL test facility)
We have used the EPICS based control system for KEKB project. After that, other machines have adopted EPICS based system.
Original control systems of Injector, PF, and others have been replaced by the EPICS based ones.

## Slide 3: EPICS status in Injector Linac
The original control system softwares have been gradually transferred to the EPICS based ones.
All control parameters are accessible via EPICS PVs.
Base R3.14.12 - R3.15.5 (~ 150 IOCs)
CSS archiver, CSS alarm
OPI: Many GUIs are implemented by Python/Tkinter/Qt4.

## Slide 4: EPICS status in Injector Linac (cont’d)
Local controller (~ 400)
  VMEx64: MRF EVG, EVR for timing system, DAC, ADC for LLRF control, BPM readout (VxWork 6.8)
  PLC for magnet power supply, vacuum, safety system (NetDev)
  Network attached power supply (x100) (StreamDevice)
  Embedded computer for klystron controller (Almazillo)
  PXI based DAC, ADC, MRF EVR for pulsed magnet control (LabVIEW based, Windows Pro. 8.1)

## Slide 5: Future in KEK
For the recent new project like cERL, 100% EPICS based control system was developed from the beginning.
In the other facilities like injector linac, PF, the original control system => EPICS in this decade.
EPICS V3 is still mainstream for the time being.
EPICS7 will be tested, and gradually deployed for the beam operation.
e-/e+ Injector Linac
  The original (non-EPICS) control applications still exist. These old ones will be obsoleted soon.
  EPICS7 functionalities
    Improvement of the data transfer performance (camera data of profile monitors )
    Hierarchal data structure could be effective for commissioning tool developments.