## Slide 1: IOC Utilities at PSI
Dirk Zimoch :: Controls Section :: Paul Scherrer Institut
EPICS Collaboration Meeting at ICALEPCS 2017

## Slide 2: Goal: Make Life Easier
Simplify tedious work
  Adding new scan rate
  Adding breakpoint tables
  Setting EPICS_CA_MAX_ARRAY_BYTES
Help debugging with reverse lookup functions
  Listing all aliases of a record
  Listing all links pointing to a record
  Listing all CA connections to a record
Accessing info fields
  List matching infos of all records
  Iterator API function to traverse matching infos
  Read infos with Channel Access

## Slide 3: Adding New Scan Rate
Edit menuScan.dbd the right way and rebuild
Or simply execute addScan command in startup script:
    addScan .3
  Automatically calls sysClkRateSet() on vxWorks if necessary
    choice(menuScan_2_second,".2 second") choice(menuScan_1_second,".1 second") }
choice(menuScan_3_second,".3 second")
  menu(menuScan) { choice(menuScanPassive,"Passive") choice(menuScanEvent,"Event") choice(menuScanI_O_Intr,"I/O Intr") # Periodic scans follow, ordered from slowest to fastest choice(menuScan10_second,"10 second") choice(menuScan5_second,"5 second") choice(menuScan2_second,"2 second") choice(menuScan1_second,"1 second") choice(menuScan_5_second,".5 second")
Basically arbitrary name
Defines new scan rate. Up to R3.15: unit must be “second”
    choice(menuScan_2_second,".2 second") choice(menuScan_1_second,".1 second") }

## Slide 4: Adding Breakpoint Tables
Include bpt*.dbd, edit menuConvert.dbd and then rebuild
Or simply load bpt*.dbd files and update menuConvert in startup script
    dbLoadDatabase bptMyConv.dbd dbLoadDatabase bptMyOtherConv.dbd updateMenuConvert
    }
    choice(menuConvertmyConv,"myConv") choice(menuConvertmyOtherConv,"myOtherConv")
  menu(menuConvert) { choice(menuConvertNO_CONVERSION,"NO CONVERSION") choice(menuConvertSLOPE,"SLOPE") choice(menuConvertLINEAR,"LINEAR") choice(menuConverttypeKdegF,"typeKdegF") choice(menuConverttypeKdegC,"typeKdegC") choice(menuConverttypeJdegF,"typeJdegF") choice(menuConverttypeJdegC,"typeJdegC") choice(menuConverttypeEdegF,"typeEdegF(ixe only)") choice(menuConverttypeEdegC,"typeEdegC(ixe only)")
Must match name of breaktable in bpt*.dbd file
Basically arbitrary name
    }

## Slide 5: Setting EPICS_CA_MAX_ARRAY_BYTES
EPICS_CA_MAX_ARRAY_BYTES on IOC too small: array PVs inaccessible
  (Not needed any more with R3.16)
Check size of all array fields of all records
  Keep in mind CA type promotion (e.g. ULONG  DOUBLE)
  Add overhead for status, severity, time stamp, …
  Find maximum
Add to startup script: epicsEnvSet EPICS_CA_MAX_ARRAY_BYTES,…
Or simply calculate it automatically
  Init hook checks potential array fields of all records
    Two SynApps records needed patch for cvt_addr(): sCalcout record and table record
  Sets EPICS_CA_MAX_ARRAY_BYTES if current value (or default) is too small

## Slide 6: Listing All Aliases of a Record
Translating alias name to record name is easy
  Remote: caget aliasname.NAME
  On IOC shell: dbla aliasname
    Works with patterns: dbla *XYZ
Finding all aliases of a record is difficult
  Call dbla without parameter, then search the list
Or modify dbla to accept alias or record name patterns
    > dbla recordname alias1 -> recordname alias2 -> recordname alias2 -> recordname

## Slide 7: Listing All Links Pointing to a Record
Finding link targets of a record is not too difficult
  On IOC shell: dbpr record,4 then search the output for links
  Or get known link field: dbgf record.OUT
Finding all links with a given target record is very difficult
  Analyze record database offline and search for links
Or use new IOC shell function: dbll record-pattern
    > dbll *:X A.DOL --> DEV1:X B.INPA --> DEV2:X.VAL MS CP C.OUT --> DEV3:X.RVAL PP
Filter for target field
    > dbll *:X.VAL A.DOL --> DEV1:X B.INPA --> DEV2:X.VAL MS CP

## Slide 8: Listing All CA Connections to a Record
It is possible to get all CA connections to an IOC
  On IOC shell: casr 2
Good luck searching the output for a specific record!
Or use new IOC shell function: cal record-pattern
    > cal MYRECORD zimoch@pc1234:47643 --> MYRECORD.VAL zimoch@pc1234:47643 --> MYRECORD.EGU archive_user@archive_host:83542 --> MYRECORD.VAL

## Slide 9: Accessing Info Fields
Records can have info fields
    record (ai, "REC1") { info(autosaveFields_pass0, "LOLO LOW LLSV LSV") }
But info fields are not easily accessible
Use new IOC shell function: dbli info-pattern [pattern ...]
    > dbli autosaveFields* REC1.autosaveFields_pass0 "LOLO LOW LLSV LSV" REC2.autosaveFields_pass1 "VAL"

## Slide 10: Accessing Info Fields (cont.)
New iterator API function: dbNextMatchingInfo
    char* patternlist[] = {"autosaveFields*", NULL};
    dbInitEntry(pdbbase, &dbentry); while(dbNextMatchingInfo(&dbentry, patternlist) == 0) { printf("%s.%s \"%s\"\n", dbGetRecordName(&dbentry), dbGetInfoName(&dbentry), dbGetInfoString(&dbentry)); } dbFinishEntry(&dbentry);
Goody: Use Channel Access to read info fields
    $ caget REC1.autosaveFields_pass0 REC1.autosaveFields_pass0 LOLO LOW LLSV LSV
NULL terminated array of pattern strings

## Slide 11: How to get it?
Package with utility functions (everything except Channel Access patch) http://epics.web.psi.ch/software/iocUtils.tgz
Patch for Channel Access to info fields
  for EPICS 3.15 and 3.16 http://epics.web.psi.ch/software/caInfoFields-R3-15.patch
  for EPICS 3.14 http://epics.web.psi.ch/software/caInfoFields-R3-14.patch
I will try to get these changes into EPICS base.